## Slide 1: ルミノシティ調整
Y. Funakoshi
Accelerator Laboratory, KEK
2017.9.8@SuperKEKB国内レビュー

## Slide 2: Contents
Phase 2 commissioning
衝突調整
  Dithering system（水平方向の衝突調整用システム）の最近の進展と立ち上げ
  垂直方向の衝突調整
ルミノシティ調整

## Slide 3: SuperKEKB commissioning phases
Phase 1
w/o QCS and Belle II
vacuum scrubbing
basic machine tuning
Phase 2
w/QCS and Belle II
w/o Vertex detector
BKG study
Luminosity tuning
Target luminosity: 1~2 x 1034 cm-2 s-1
Phase 3
Physics Run
Luminosity tuning
Feb. 2016 ~ June 2016
Already done!
Feb. 2018 ~ July 2018
~ autumn 2018
Damping ring commissioning: ~ Dec. 2017
No beam collision

## Slide 4: Tasks in Phase 2
Basic tuning
  Beam injection of the beam from DR, vacuum scrubbing…
Performance check of QCS magnets
Squeezing IP beta functions at IP
  Optics corrections
Beam collision tuning with “Nano beam scheme”
Belle II beam BG study and tuning
Other studies: electron clouds, other instabilities…
Luminosity tuning
Physics Run

## Slide 5: 衝突調整
衝突状態のサーチ
ビーム衝突フィードバック（軌道フィードバック）システムの立ち上げ
ビームアボート後の衝突の確立の手法

## Slide 6: ビーム衝突のサーチ
Closed orbit correction of each beam
Bunch timing adjustment
  Rough adjustment: search for collision bucket
    BPM measurement, luminosity monitor?
  Fine adjustment: RF phase scan
    Observer horizontal beam-beam deflection
Orbit adjustment
  Scan orbits
    beam-beam deflections
    Luminosity
    beam lifetime

## Slide 7: 軌道フィードバックシステム
アルゴリズム
  Vertical
    Beam-beam deflection (like KEKB)
    Based on COD measurements using BPMs
  Horizontal
    Dithering system (like PEP-II)

## Slide 8: Orbit feedback at IP :Algorism
Beam-beam deflection (SLC, KEKB vertical)
Luminosity feedback (dithering)(PEP-II)
Beam size feedback (KEKB horizontal)
Dy at IP=
~5nm ~1/10sy*
BPM
IP
BPM
Dy at BPM= ~1.3mm
SupeKEKB case
y
Luminosity
When we shake the beam at around the peak of the luminosity (dithering), the dithering frequency in the luminosity is minimized and there appears twice of the the dithering frequency.
x
Beam size
sy (LER)
Luminosity
At KEKB before installation of crab cavities, the vertical beam of LER was used for the horizontal orbit feedback at IP.

## Slide 9: Horizontal orbit feedback
Difficulty to develop based on the beam-beam defection like the vertical case
  Small xx
    xx ~ 0.0028(e+), 0.0017(e-)
  Two sources of horizontal beam-beam kick
    Horizontal offset and shift of collision timing
We need a different method for the Hor. feedback.
  Luminosity feedback (dithering) (like PEP-II)
  Beam size feedback (like KEKB Hor. feedback before crab)
Effect of horizontal offset
  Due to Hor. offset, the two beams collide at the position which is shifted from the waist point.
  The crab waist seems to compensate this shift of waist.
  However, actually the situation becomes worse with the crab waist, since we have to keep the both beams at the design collision point with this scheme.
Feedback speed
  Fast vibration of IR quads is tolerable. We do not need very fast feedback ( slower than ~ 1 Hz).

## Slide 11
Fast luminosity monitoring - Plan for 2018 (and beyond... ) (1)
01/2018-06/2018: tests during phase II of SuperKEKB commissioning
- Bhabha acquisition and first luminosity measurement tests
- Single beam background characterization
- Luminosity DAQ output provided to the SuperKEKB monitoring system and dithering system tests:
8 locations for the dithering coils in LER around IP.

## Slide 14
Luminosity monitor
Detection system
Belle 2
Electronics
Hut
SuperKEKB
Tunnel
B4
Control room
Lock-In-Amps (1~3)
(x; y, y’ optional)
Luminosity
1kHz b/w
Programmable Amplifier
(x; y, y’ optional)
Power supply (12)
Luminosity monitor
Luminosity monitor
Dithering coils (12)
ADC
DAC
ADC
ADC
Offset signals (phase, amplitude; 2x1)
Lumi in
PLC: Feedback process control
Dither waveform (sine wave)
(1~3)(BNC)
Amplitude control
Amplitude readback
12x1
12x1, 12x1
12x2
Readback
Drive voltage
12
12(BNC)
EPICS control
Bump magnet controller
EPICS control network
EPICS control (< 1Hz)
To HER iBump magnets
Dithering System
Block Diagram
Network
EPICS control
EPICS
control
In phase 2, only x direction
-> can be switched to y or y’
ADC: 27 channels
12ch/module
-> need 3 modules
DAC: 12 channels
8ch/module
-> need 2 modules
CPU: 1 module
need 6 slots
ー＞prepare base module with 9 slots

## Slide 15: Orbit Feedback collaborators
Horizontal orbit feedback system
  Organizer
    M. Masuzawa, Y. Funakoshi
  Dithering coils, programmable amp (designed and fabricated at SLAC)
    U. Wienands, A. Fisher and others (SLAC)
  Fast luminosity monitor
    S. Uehara (Belle-II group)
    P. Bambade, C. Rimbault, D. EL Khechen, D. Jehanno, S. D. Carlo, C. Pang (LAL Group)
  Other hardware preparation (Lock-in Amp, Power supplies, PLC, DAC,cabling…)
    T. Oki, S. Nakamura, T. Kawamoto (Magnet Group) + Control group
  Software, Simulations
    U. Wienands, T. Oki, T. Kawamoto, Y. Funakoshi + Control group
Vertical orbit feedback system
  H. Fukuma and beam monitor group
    BPMs, feedback circuits….
  N. Ohuchi, H. Yamaoka (QCS group)
    QCS supports and vibration measurement, Simulation on QCS vibrations

## Slide 16
Dithering system components (TB4 control room, old)
Components for the dithering system has been installed.
Signal Recovery Model 7230 DSP Lock-in amp.
Yokogawa FA-M3 Programmable logic controller
Takasago BWS60-5 Power amps. for
SLAC Programmable amp.
iBump
(HER)
Dithering (LER)

## Slide 17: Tsukuba B4 control room (new)
PLC, DAC, ADC
Lock-in Amp
Programmable
Amp

## Slide 18
Goal: Realization of a fast luminosity monitor based on radiative Bhabha scattering measurements for SuperKEKB luminosity feedback, tuning and backgrounds studies (BEAST).
  Aimed precision for Train Integrated Luminosity (TIL): dL/L  10 -2 to 10-3 in 1 to 10ms
  Fast signal from each bunch crossing for Bunch Integrated Luminosity (BIL),
  2500 bunches/train, collisions every 4 ns
Measure the radiative Bhabha process at vanishing photon scattering angle
  Rate proportional to Luminosity
  Large cross section  0.2 barn
Two complementary techniques developed at LAL and KEK:
   5x5x0.5 mm3 single crystal CVD diamond sensors (CVD DS) pairs coupled to fast charge / current amplifiers (LAL)
  Cerenkov detector + scintillator (ZDLM group @ KEK)
positioned together outside of the beam pipe
Two optimized locations fixed in 2014 and 2015:
- In High Energy Electron Ring : 30m downstream the Interaction Point for Bhabha photon detection
- In Low Energy Positron Ring : 11.9m from IP for Bhabha scattered positron detection
Fast Luminosity Monitoring at LAL  KEK
C. Rimbault

## Slide 19
July 2016  December 2017 : Prepare phase 2 commissioning (1)
Fraction of detected Bhabha which can be achieved in 140 DS with different thickness radiator
Development of FPGA based DAQ for the phase II :
  Luminosity firmware development:
  signal pulse reconstruction algorithm: A1-A4
  test on Train Integrated Lumi (TIL) & Bunch
  Integrated Lumi (BIL) reconstruction: almost validated
Installation of a window in LER (confirmed for spring 2017)
 Adaptation of existing pillar for phase 2
 radiator design study: trapezoid shape Tungsten radiator
with thickness of 6*RL will be used.

## Slide 20: Recent progress in preparation of the dithering system
Hardware
  Network connection in TB4 control room: done
  Cabling among devices: almost done
  Installation and setup of PLC in TB4 control room: done
  Fast luminosity monitor: to be ready by the start of Phase 2
Software
  Soft IOC on PLC: setup done
  EPICS records for Lock-in-am, DAC, ADC: prepared
  Feedback control software written in Maple (U. Wienands)
    Transferring to SAD script is going on. Simulation will be done on SAD.
    In the actual operation, it will work in soft IOC on PLC in the present plan.
System tests in TB4 control room
  System test of Lock-in Amp was done.
  System test of programmable amp was done.
    U. Wienands stayed at KEK for a week for the test at the end of August.

## Slide 21: iBump LER (Phase 3)
Bumpがない時：8.18E-13 m
Bump Height: 10 mm

## Slide 22: iBump LER (Phase 2 4x8)
Bumpがない時：1.96E-13 m
Horizontal kick < 44.4mrad

## Slide 23: Parameters for dither simulation
Luminosity | 1 x 1034 cm-2 s-1 |  | 1 x 1035 cm-2 s-1 |  | 8 x 1035 cm-2 s-1 | 
 | LER | HER | LER | HER | LER | HER
Ibeam [A] | 1.0 | 0.8 | 2.7 | 1.95 | 3.6 | 2.6
# of bunches | 2500 |  | 2500 |  | 2500 | 
ex/ey (nm/pm) | 2.2/44 | 5.2/104 | 3.2/51.84 | 4.6/77.28 | 3.2/8.64 | 4.6/12.88
bx*/by* (mm) | 128/2.16 | 100/2.4 | 128/1.08 | 100/1.2 | 32/0.27 | 25/0.30
sx*/sy*(mm/nm) | 16.8/308 | 22.8/500 | 20.2/237 | 21.4/305 | 10.1/48 | 10.7/59
sx*eff (mm) | 249 | 208 | 249 | 208 | 249 | 208
xx/xy | 0.0033/0.024 | 0.0013/0.0257 | 0.0083/0.049 | 0.0052/0.046 | 0.0028/0.0881 | 0.0012/0.0807
Dx (lumi:20% drop) | ~110mm |  | ~55mm |  | ~10mm | 
Lumi. meas. | 1kHz |  | 1kHz |  | 1kHz | 
accuracy | ~5 x 10-3 (w/ radiator) |  | 1.3 x 10-3(w/o radiator) |  | < 1 x 10-3 | 
sx*eff = szsinf
initial
nominal
ultimate

## Slide 24: Field measurements and programmable amp calibration data
Measured on Aug. 31st 2017

## Slide 25
Damping and phase delay of a magnetic field
A.W. Chao and M. Tigner, Editors,
Handbook of
Accelerator Physics and Engineering,
World Scientific, Singapore (1999), p. 268
Damping ratio Phase delay
Red: outer radius = 51mm, thickness = 6mm Green: outer radius = 48mm, thickness = 3mm
Blue: outer radius = 42mm, thickness = 2mm
Phase difference: ~ 5 degrees @77Hz among coils
T. Oki

## Slide 26
Conceptual drawing for 3 type of beam pipes
ZDS1{L, R}P
  Inner diameter: 80 mm
  Thickness: 2 mm
ZDS2{L, R}P
  Inner diameter: 90 mm
  Thickness: 3 mm
  10 mm Cu coating inside.
Y. Suetsugu
ZDS{3, 4}{L, R}P
  Inner diameter: 90 mm
  Thickness: 6 mm
  10 mm Cu coating inside.
All pipes are made of SS316L.

## Slide 27: Effect of phase difference among coils
Phase 2 4x8

## Slide 28
Damping of magnetic field due to eddy current
A.W. Chao and M. Tigner, Editors,
Handbook of
Accelerator Physics and Engineering,
World Scientific, Singapore (1999), p. 268
Damping ratio
Resistive and thinner pipe suppresses the damping effect.
1k 10k 100k
SS316L
Copper
(KEKB
LER pipe)
Dithering
freq. range
T. Oki

## Slide 29
K. Ohmi
by*~300mm
Swaist:1/10 by* (~30mm)
-> Lum. Loss ~ 3.5%
Dx = Tan[2f]*Ds
Ds=30mm -> Dx = =2.5mm

## Slide 30: Luminosity degradation due to horizontal orbit shift at IP
by*
8
4
1

## Slide 31
1000
100
10
1
0.1
Integral amplitude (nm)
Measured
ground motion
(input data)
25 nm@25 Hz
Luminosity degradation (based on beam-beam simulation by K. Ohmi)
QC1RP and QC1RE vibrate with same phase,
but the amplitude difference still arises: 25 nm at 25 Hz…
Phase (deg.)
H. Yamaoka
Frequency (Hz) | 24.85 | 38.93 | 69.34 | 99.60
DyIP*rms (nm) | 18.63 | 1.72 | 8.29 | 3.14
L/L0average (%) | 95.4 | 99.8 | 99.7 | 99.7
Estimation of QCS vibration and luminosity degradation
(vertical)
Feedback rejection gain
-16.7dB (19 nm -> 2.8 nm)
15 (recent meas.)
40
84
-23dB (40nm -> 2.8 nm)
Phase 3

## Slide 32
QCSLとQCSRクライオスタットの振動測定（山岡さん）
・2017/3/6の電磁石打合せの資料より…。
鉛直方向 QCSL: 45nm@20Hz QCSR: 300nm@15Hz
注意：前頁のはコイルの振動で、こっちはクライオスタット

## Slide 33
Beam-Beam simulation results
K. Ohmi
Just 20 nm offset leads to 6 % degradation of luminosity.

## Slide 34: Commissioning of orbit feedback systems
Tuning of iBump orbit
  iBump in HER: COD measurements -> correction so that the bumps are closed.
  iBump in LER (dither orbit):
    Response of bpm signal (phase) to coil excitation by using LIM
    observe the 77 Hz component at two BPMs outside of the bump with 90 degree phase difference in each horizontal and vertical directions -> correction so that the 77 Hz components are minimized
    correction using turn-by-turn BPMs?
    Prior to those corrections, should we do corrections by using a DC bump?
Setup the orbit feedbacks
  Vertical feedback
  Horizontal feedback (dithering)
    A. Fisher (SLAC) will stay at KEK in the commissioning of dithering system
    U. Wienands will stay at KEK for about 1 month in the commissioning of dithering system.

## Slide 35: ビームアボート後の衝突の確立の手法
KEKBでは、二つのビームを衝突状態に持っていく途中（過渡現象）でビームロスするなどの現象が見られ、苦労する場合があった。
  Nano beam 衝突はでどうか？
    実際にやって見ないとわからないことも多いが、予めシミュレーションをやっておきたい

## Slide 36: ルミノシティ調整
基本的なマシンパラメータの確立
  IP beta functions
  Betatron tunes
  Beam currents, Number of bunches
Tuning items
  Tuning knobs
    X-Y coupling
    waist points
    IP dispersions
    Target values of orbit feedback
    Betatron tunes
  Method of parameter search
    Scan, scan, scan,,,,,

## Slide 37: Strategy of Beta Squeezing in Phase-2
Phase | LER |  |  | HER |  | 
 | βx* [mm] | βy* [mm] | scale | βx* [mm] | βy* [mm] | scale
2.0* | 384 | 81 | 12 x 300 | 400 | 81 | 16 x 270
2.1 | 384 | 5.4 | 12 x 20 | 400 | 6 | 16 x 20
2.2 | 256 | 2.16 | 8 x 8 | 200 | 2.4 | 8 x 8
2.3 | 128 | 2.16 | 4 x 8 | 100 | 2.4 | 4 x 8
2.4 | 128 | 1.08 | 4 x 4 | 100 | 1.2 | 4 x 4
3.x | 32 | 0.27 | 1 x 1 | 25 | 0.30 | 1 x 1
We hope to squeeze the IP beta functions down to 4 x 8 in Phase 2.
If possible, 4 x 4 is desirable.
adiabatic squeezing
Y. Ohnishi

## Slide 38: Issues
IR design and dynamic aperture
Optics corrections & Low emittance tuning
Beam-beam related issues
IP orbit control to maintain beam collision
Beam loss and beam injection
Electron clouds
Injector upgrade for low emittance & high intensity beams
Detector beam background
The items in red were partially studied in Phase 1.

## Slide 39: SuperKEKB Luminosity Projection
A lot of difficult works should be done in Phase 2 and 3.

## Slide 40: Spare slides

## Slide 41: iBump LER (Phase 2 8x8)
Bump Height: 10 mm
Bumpがない時：1.96E-13 m

## Slide 42: iBump steering kick angle
iBump FB | 積分磁場（Tm） | kick angle(mrad) @7GeV @5A | Commemnt
垂直ステアリング | 0.00335 | 0.143571429 | 江川・植木さんの磁場測定結果
水平ステアリング | 0.00611 | 0.261857143 | 江川・植木さんの磁場測定結果
Dithering | 積分磁場（Tm） | kick angle(microrad) @4GeV @5A | 
Horizontal | 0.000451 | 33.825 | UliさんのIPAC論文
Vertical | 0.000592 | 44.4 | UliさんのIPAC論文

## Slide 43: Shift of collision timing makes a horizontal kick
With the drift of collision timing ->no shift of collision point ->no waist problem
However, the drift of collision timing makes a beam-beam defection and interferes with the detection of the true hor. offset.
Hor. offset from shift of collision timing
  offset：Dx=c Dt sinf
  Tolerance for true horizontal offset: Dx corresponding Dt =0.20ps ->RF phase of 0.07°
Lorentz boost
projection
f
Dt -> Dx=c Dt sinf

## Slide 44: Luminosity and beam-beam parameter with superbunch collision
Luminosity
Beam-beam parameter
σxeffective = σz sinφc
φc

## Slide 47
Fabrication and field measurement
Fabrication and measurement of coils will be finished by this March.
U. Wienands, S.D. Anderson, MFD Metrology, SLAC