## Slide 1: Domestic Review Report
SATOH, Kotaro (chairman)
KEK
Feb. 7, 2011

## Slide 2
Domestic short review on Jan. 18, 2011.
-Review only crucial issues inherent in SuperKEKB
-Improve the presentation for MAC
Issues are :
Electron source design, perspective
Emittance growth during the Linac acceleration
Optics, dynamic aperture, x-y coupling -Tolerance for machine errors, how to achieve them
Movable mask system
- Consistency with the injection acceptance
- Heat load on the mask surface
Background
- Estimate SR, back scattering, spent electrons
- How to protect detectors
How to collide extremely thin beams
QCS design
IR vacuum system, assembly process
Ring vacuum system

## Slide 3
Comments
Electron source - Determine the baseline plan, on which available resource should be focused.
Emittance growth - Correct alignment errors by practical methods. - Understand the growth mechanism by machine studies and simulation.
Optics - Analysis of crucial elements, BG, masks, tolerance, …, is extremely urgent. These could turn over the present design.
- Establish machine error detection methods based on the beam measurement.
Movable mask - Demonstrate the injection acceptance is secured. - Re-estimate the temperature rise with a more realistic model. Collect information of graphite coating used in the other accelerators.

## Slide 4
Background - Spent electrons lost inside QCS and tip scattering of SR at 9mm f aperture close to IP should be analysed immediately.
How to collide - Analysis of the FB loop using transfer functions is more effective to design the FB system, than particle tracking simulation.
QCS design - Analyze nonlinear field near iron-core magnets immediately. - Support should meet the condition on QCS movement causing miss-collision.
IR vacuum
- Solve issues related to NEG coating before finalizing the design.
- Issues are
QCS thermal shield for the activation,
lifetime shorten by frequent activation,
outgas from the coating heated by wall currents.