## Slide 1: Belle II Experiment
Yutaka USHIRODA (IPNS, KEK)
KEKB Review Meeting
Feb. 7, 2011

## Slide 2: Outline
Introduction
Detector Design
Machine-Detector issues
Construction Cost and Schedule
Summary

## Slide 3: Primary Target of KEKB/Belle
… was to confirm Kobayashi-Maskawa mechanism.
… and was so successful.

## Slide 4: Hot news from Belle in the past
CP violation in neutral B system
X（3872）
CP violation in penguin decays
CP violation in B→Kp decay
b→dg transition
B→tn decay
Anomalous CP violation in B→Kp decay
Z(4430)＋
Data size （fb-1）
Precise determination of SM (CKM)
Some unexpected observations such as new hadronic resonances
  (possible, but omitted in SM)
(Yet unclear) hints of new physics (impossible in SM, possible in NP)
333 physics publications

## Slide 5: Goal of Super B-factory
ATLAS/CMS may discover it.
Yes, but they cannot measure flavor couplings and not good at determining models.
LHCb started in good shape.
Yes, but they are not good at measuring neutral particles involved in many important decay modes (BF(Bgtn), S(KSp0g), K0p0, …).
Next-generation flavor factory in clean environment of e+e- collisions is important.
g SuperKEKB/Belle II
… is to search for NP,
discover it,
and determine model and parameters.
Or, to search for NP,
and constrain model and parameters.
Minimal Flavor Violation
Enhanced Flavor Violating Couplings

## Slide 6: SuperKEKB and Belle II
e- 7GeV 2.6 A
e+ 4GeV 3.6 A
Target: L = 8x1035/cm2/s
SuperKEKB
Colliding bunches
Damping ring
Low emittance gun
Positron source
New beam pipe
& bellows
Belle II
New IR
TiN-coated beam pipe with antechambers
Redesign the lattices of HER & LER to squeeze the emittance
Add / modify RF systems for higher beam current
New positron target / capture section
New superconducting /permanent final focusing quads near the IP
Low emittance electrons to inject
Low emittance positrons to inject
Replace short dipoles with longer ones (LER)

## Slide 7: Luminosity prospect
Shutdown
for upgrade
Integrated Luminosity
(ab-1)
Peak Luminosity
(cm-2s-1)
Milestone of SuperKEKB
9 month/year
20 days/month
Commissioning starts
in 2nd half of FY2014
We will reach 50 ab-1
in 2020~2021.

## Slide 8: Organization in KEK
Exp. group
Acc. group
Computing research center
Cryogenics center
Mechanical engineering center
Radiation safety office
KEK’s executive board
KEK’s board of directors
Administration department
Facility department
Public relations office
B Factory Board
(Bファクトリー推進委員会）
KEK-DG
BPAC
KEKB ARC
Executive committee
(Bファクトリー推進室）
M. Yamauchi
and many other field-level barrier-free interactions between machine and detector groups:
SuperKEKB kentoukai,
Belle II Executive Board meeting,
Belle II General Meeting
SuperKEKB Optics meeting,
IR technical meeting,
IR assembly meeting,
Belle II SVD mechanical meeting
…
(addition by YU)

## Slide 9: Belle II Collaboration
13 countries/regions, 57 institutes, 384 collaborators (Jan. 2011)

## Slide 10: Belle II Organization
+Task forces
EB mtg.
~1/month
Collaboration mtg.
3/year
IB mtg.
~3/year
Workshops, meetings

## Slide 11: Tsukuba-hall webcam
Beam Pipe and Vertex Detector extraction: on Nov. 10, 2010
Belle Detector Roll-out: Dec. 9, 2010
End-caps, CDC, B-ACC, TOF extraction: in Jan. 2011

## Slide 12: Belle II Detector (in comparison with Belle)
SVD: 4 DSSD lyrs g 2 DEPFET lyrs + 4 DSSD lyrs
CDC: small cell, long lever arm
ACC+TOF g TOP+A-RICH
ECL: waveform sampling (+pure CsI for end-caps)
KLM: RPC g Scintillator +MPPC(end-caps)

## Slide 13: Technical Design Report
arXiv:1011.0352: http://arxiv.org/abs/1011.0352
KEK Report 2010-1: http://www-lib.kek.jp/cgi-bin/kiss_prepri.v8?KN=201024001&OF=8.
Belle II web page: http://b2comp.kek.jp/~twiki/pub/Organization/B2TDR/B2TDR.pdf
Reviewed by BPAC members + external experts in May and in Nov.
Printed in Nov.

## Slide 14: Vertex Detector
Belle II Belle
Beam Pipe r = 10mm 15mm
DEPFET
Layer 1 r = 14mm
Layer 2 r = 22mm
DSSD
Layer 3 r = 38mm 20mm
Layer 4 r = 80mm 43.5mm
Layer 5 r = 115mm 70mm
Layer 6 r = 140mm 88mm

## Slide 15: PXD (DEPFET)
Each pixel is a p-channel FET on a completely depleted bulk
A deep n-implant creates a potential minimum for electrons under the gate (“internal gate”)
Signal electrons accumulate in the internal gate and modulate the transistor current (gq ~ 400 pA/e-)
Accumulated charge can be removed by a clear contact (“reset”)
Fully depleted: => large signal, fast signal collection
Low capacitance, internal amplification: => low noise
High S/N even for thin sensors (50µm)
Rolling shutter mode (column parallel) for matrix operation => 20 µs frame readout time
=> Low power (only few lines powered)
DEPFET:
http://aldebaran.hll.mpg.de/twiki/bin/view/DEPFET/WebHome

## Slide 16: DEPFET for Belle II
Power consumption in sensitive area: 0.1W/cm² => air-cooling sufficient
Mechanical mockup
total of 8 Mpx
radius pixel thickness
Layer 1 r = 14mm 50x50mm2 75mm(0.18%X0)
Layer 2 r = 22mm 50x75mm2 75mm

## Slide 17: Test System
PXD5 DEPFET matrix
DCDB readout chip,
Bump bonded on interface board
Switcher control chip
New switcher and DCD is tested with a DEPFET PXD5 matrix
So far the system reaches 120ns sampling time with 40nA (~ 100 electrons) noise
Some fine tuning needed to reach full speed (<100ns) (tests started 2 weeks ago)
Side remark: flipping and bump bonding of DCDB in adapter board worked without problems

## Slide 18: SVD (DSSD)
HPK resumed DSSD production with 6’’ wafers
Two types of rectangular sensors and
Trapezoidal sensors for slanted part (still under discussion)

## Slide 19: Flex PCBs and APV25
Origami PCB
PA1
PA2
PA0
glued onto hybrid
Origami PCB
  3-layer design
  237µm thick (nominal)
PA0, PA1 and PA2
  2-layer design
  145µm thick (nominal)
Thinned APV25
(300mmg~100mm)
~0.55%X0/layer

## Slide 20: First prototype ladder
A prototype ladder using the first 6 inch DSSD from HPK has been assembled and tested.

## Slide 21: Expected performance
p+ p-
Ks track
IP profile
B vertex
g
g
g
B decay point reconstruction
with KS trajectory
Larger radial coverage of SVD
Significant improvement in IP resolution!
pbsin(q)3/2 [GeV/c]
s[mm]
pbsin(q)5/2 [GeV/c]
Significant improvement in dS(KSp0g)
Less Coulomb
scatterings
Pixel detector close
to the beam pipe
s[mm]
Belle
Belle II’
Belle II
1.0
2.0
0
1.0
2.0
0
10mm
20mm

## Slide 22: Central Drift Chamber
longer lever arm
improve resolution of momentum and dE/dx
 | Belle | Belle II
inner most sense wire | r=88mm | r=168mm
outer most sense wire | r=863mm | r=1111.4mm
Number of layers | 50 | 56
Total sense wires | 8400 | 14336
Gas | He:C2H6 | He:C2H6
sense wire | W(Φ30μm) | W(Φ30μm)
field wire | Al(Φ120μm) | Al(Φ120μm)
normal cell
10~20 mm
18 mm
10 mm
6~8 mm
small cell
Belle
Belle II

## Slide 23
Analog signal of b-ray
with current Belle AMP
1205 field wires
384 sense wires
making cable
HV test
signal check
Cosmic ray
July 9
Aug. 12
July 29
Number of wires
wire stringing
Test chamber fabrication for 3D TRG study
Full-length (540x570x2200) test chamber has also been made

## Slide 24: Status of new 48ch board for CDC
TDC
Energy loss
16ch board
AMP shaper ASIC chip
4ch/chip
discriminator
ethernet port
for data transfer
FADC
NIM input for TRG
200mm x 175mm
AMP shaper discriminator chip
8ch/chip
Rocket I/O
for data transfer
FADC
NIM input for TRG
230mm x 150mm
Delivered on Oct. 26
48ch board
waveform sampling with
32MHz FADC
~200ns

## Slide 25: Particle Identification Devices
Aerogel radiator
Hamamatsu HAPD + readout
Barrel PID: Time of Propagation Counter (TOP)
Aerogel radiator
Hamamatsu HAPD
+ new ASIC
Cherenkov photon
200mm
n~1.05
Endcap PID: Aerogel RICH (ARICH)
200
Quartz radiator
Focusing mirror
Small expansion block
Hamamatsu MCP-PMT (measure t, x and y)

## Slide 26: Time of Propagation Counter (TOP)
TOF
TOP
MCP-PMT
～1.2m
Quartz radiator
  2.6mL x 45cmW x 2cmT
  Excellent surface accuracy
MCP-PMT
  Hamamatsu 16ch MCP-PMT
    Good TTS (<35ps) & enough lifetime
    Multialkali photo-cathode  SBA
Barrel PID: Time of Propagation Counter (TOP)
Quartz radiator
Focusing mirror
Small expansion block
Hamamatsu MCP-PMT (measure t, x and y)

## Slide 27: TOP (Barrel PID)
Beam test done in 2009
  # of photons consistent
  Time resolution OK
1st
2nd
3rd
1st
2nd
3rd
[1count/25ps]
[1count/25ps]
Time resolution
beam data
Simulations
# of photons
Beam spot
875mm
915mm
quartz
3rd
2nd
1st
Hamamatsu MCP-PMT
Quartz Radiator

## Slide 28: Test beam result
Aerogel
Hamamatsu HAPD
Q.E. ~33% (recent good ones)
Clear Cherenkov image observed
Test Beam setup
Cherenkov angle distribution
6.6 σ p/K at 4GeV/c !
Single photon angle resolution s0 = 13.5mrad
# of photoelectrons Npe = 15.3

## Slide 29: Expected Performance (Luminosity gain)
FWD BRL | ACC only | dE/dx only | As good as Belle | A-RICH
TOF, dE/dx NA | –74% | –69% | –68% | –62%
TOF NA | –41% | –35% | –32% | –22%
As good as Belle | –10% | –4% | 0% (definition) | +12%
TOP opt.0 | +27% | +33% | +40% | +59%
TOP opt.2 | +45% | +51% | +60% | +83%
Completely different world with excellent PID detectors!
No upgrade
BAD
Upgrade
GOOD
No upgrade
BAD
Upgrade
GOOD
B0gr0g

## Slide 30: Upgrade of ECL
Upgrade electronics to do waveform sampling & fitting
Upgrade crystals for end caps (pure CsI + photomultiplier as the baseline)
For Day 1

## Slide 31: New shaper/readout boards
Basically ready for mass production
(minor revisions because we still have time.)
One of older versions has been installed in Belle to readout part of the end cap in 2008. Tested OK.

## Slide 32: KLM: KL&Muon detector
GENERAL LAYOUT
One layer: 75 strips (4 cm width)/sector
5 segments 1 segment = 15strips
Two orthogonal layer = superlayer
F&B endcap KLM:
  Total area ~1400 m2
  16800 strips
  the longest strip 2.8 m; the shortest 0.6 m
WLS fiber in each strip
Hamamatsu MPPC at one fiber end
mirrored far fiber end
RPC g Scintillator (End cap)
also inner 1,2, or 3 layers of Barrel(?)

## Slide 33: One strip
fiber: Kuraray Y11 MC
MPPC: Hamamatsu
1.3×1.3 mm 667 pixels
(used in T2K ND)
Scintillator bar: Vladimir (Russia)
(used in T2K ND)
part II
part I

## Slide 34: Test modules adjacent to Belle KLM (2008)
Muon tag

## Slide 35
EKLM Module-0 assembled in
ITEP into the frame mock-up

## Slide 36
Close view of frame support structure
and strips with SiPM connectors
Strip SiPM connector

## Slide 37
Close view of strips.
Segment’s plastic plates are easily seen
Y-strip
X-strip
Plastic plates

## Slide 38: Machine-Detector issues
   IR design g Tuesday morning
   Beam Background g Tuesday morning
   Machine commissioning strategy
   Injection veto and PXD
   Beam energy asymmetry (settled)
   Detector rotation

## Slide 39: Machine commissioning strategy
BG level
Machine parameter
(I,L,s, …)
MC
Design value
1. Our BG estimation (MC/extrapolation) has large uncertainty.
2. We don’t like to burn our precious detectors before taking data.
3. We won’t roll-in Belle II until we are confident about the BG level.
We will prepare dedicated detector (BEAST II) for machine commissioning to monitor the BG level and compare with our estimation.
Machine parameters for BEAST II must be close enough to the design values so that natural extrapolation would work. Unpredictable jump should be avoided.
(somewhat small beam size, some beam current and some luminosity needed)
No discrimination power if MC is correct.
BEAST II with Solenoid magnet (?)
Discussion started

## Slide 40: Injection veto
Level 1 trigger is blocked after injection because BG is too high.
dead-time
Suppose n = 100, W1=1ms and m=300,
6.5% dead-time @ 50Hz injection.
DEPFET pixel detector integrates data for 20ms.
= 2 revolutions of noisy bunches.
Pixels are all exposed till the end of 2nd phase (4ms)
20% dead-time @ 50Hz injection.
Trying to increase the frame rate (20ms g 5ms), but still 10% dead-time @ 50Hz injection.
Any ideas
to reduce injection repetition rate (by reinforcing injectors?)
to achieve quiet injection, fast background dumping
are welcome.
~1ms
~3ms

## Slide 41: LER Beam Energy (settled)
better
worse
Larger boost, better Dt resolution
Smaller boost,
Larger acceptance
- J/yK0 tCPV
- fK0 tCPV
- Btn BR
3.5GeV g 4GeV to mitigate Touschek lifetime.
We are not so happy (25-30% loss in TCPV, 6% gain in full-recon.).

## Slide 42: Detector Rotation
Two beams have finite crossing angle (83mrad).
Belle solenoid axis must be bisector of the angle, but now it is not.
Either Belle or two rings must be rotated.
Parameters are OLD
Rotation is technically possible.
Additional cost (very preliminary estimate: 3 oku yen)
Possible damage in detectors (?)
Concern from bad experience of buckled CsI container when constructing Belle.
We will rotate Belle IF two rings cannot be rotated after all.
Cost to be covered by machine group.

## Slide 43: Belle II Construction Schedule

## Slide 44: Construction Cost
~40 Oku yen in three-four years
½ covered by KEK, ½ by collaborating institutes
Cost profile in FY2011-2014
(w/o comp. )

## Slide 45: Summary
SuperKEKB/Belle II with L=8×1035 cm-2s-1is can explore many fruitful flavor physics in coming 10-15 years.
Belle detector disassembly by end of Jan. as scheduled.
Detector R&D, part of construction going on. On schedule so far.
Several machine-detector issues to be cleared. Close cooperation of two groups is necessary.

## Slide 46: Backup

## Slide 47: Super B Factories
Although there exist interesting possible hints for the NP at the present B factories, all the results are consistent with the SM.
NP should exist at the higher energy scale, possibly in TeV region considering the hierarchy problem → LHC will discover it.
Super B factories can help the identification of the NP, i.e. whether it is SUSY or others, or how SUSY breaking occurs.
SUSY scenario
[based on T.Goto et.al. PRD77, 095010(2008)]
Observables
@ Super B factories or other experiments

## Slide 48: Physics with 50(75) ab−1
Two recent publications:
Physics at Super B Factory (Belle II) arXiv:1002.5012
SuperB Progress Reports: Physics (SuperB) arXiv:1008.1541
In addition to the topics in this talk,
Photon polarization of B→K*.
B→K().
CPV in D.
LFV in  decay.
…
Integ. Lum.（ ab-1 ）
Reach of B factories
Super B factories
Upper limits
 decay

## Slide 49
B- → t-n – charged higgs limits


b
u
W/H
5 ab-1
→ limit on charged Higgs mass vs. tanb
50 ab-1

## Slide 50
HFAG, Winter’09
D. Atwood et al., PRL79, 185 (1997)
(~SM prediction)
B → K*g t-dependent CPV
SM:
Left-Right Symmetric Models:

## Slide 51
ℓ
3ℓ,ℓ
model Br(→) Br(→ℓℓℓ )
mSUGRA+seesaw 10-7 10-9
SUSY+SO(10) 10-8 10-10
SM+seesaw 10-9 10-10
Non-Universal Z’ 10-9 10-8
SUSY+Higgs 10-10 10-7
LFV and New Physics
Integ. Lum.（ ab-1 ）
Reach of B factories
Super B factories
Upper limits
Neutral Higgs mediated decay.
Important when MSUSY >> EW scale
bkg. free (U.L. ∝ 1/L)
SUSY + Seasaw
Large LFV
bkg. from ee→ ttg (U.L. ∝ 1/√L)

## Slide 52: Comparison with LHCb
 | Belle | Belle II | Belle II | LHCb
 | ~ 0.5 ab−1 | 5 ab−1 | 50 ab−1 | 10 fb−1 [5yrs]
S(KS) | 0.22 | 0.073 | 0.029 | 0.14
S(’KS) | 0.11 | 0.038 | 0.020 | ---
fs from S(J/) | --- | --- | --- | 0.01
S(K*) | 0.36 | 0.12 | 0.03 | ---
S() | 0.68 | 0.22 | 0.08 | ---
B/B(B  ) | 3.5 | 10% | 3% | ---
Bs   | ∙ | ∙ | ∙ | 5 @ 6 fb−1
   [×10−9] | <45 | <30 | <8 | ---
   [×10−9] | <209 | <10 | <1 | ---
f2 | 11⁰ | 2⁰ | 1⁰ | 4.5⁰
f3 | 16⁰ | 6⁰ | 2⁰ | 2.4⁰
LHCb
Modes where the final states are charged only.
Bs
Bc, b
…..
B factories
Advantage:
Modes with , 0 .
Modes with  .
 decays.
KS vertex.

## Slide 53: ASICs for control and readout
All three chips fabricated and successfully tested
ACTIVE AREA
Switcher
Control of gate and clear
32 x 2 channels
Switches up to 30V
AMS 0.35 µm HV technology
Tested up to 36 Mrad
DCDB
Amplification and digitization of DEPFET signals
256 input channels
8-bit ADC per channel
92 ns sampling time
UMC 189nm
Rad hard design
DHP
Signal processor
Common mode correction
Pedestal subtraction
0-supression
Timing and trigger control
IBM 90 nm
Rad hard design
½ size (32 channel) test chip

## Slide 54: Test Beam in 2009 (ILC version)
(Not a typical) event display
TB 2009
120GeV p
Array of 6 DEPFET modules

## Slide 55: Radiation Damage
Gate oxide
DEPFET based on a MOS structure
problem with ionising radiation:
Creation of fixed (positive) charges in the oxide layer and at the interface
Attracts electrons at the Si/SiO2 interface
Need more negative gate voltages to compensate
=> Shift of transistor threshold
Solution: thin oxides
< 2.5V shift at 10Mrad
For standard DEPFETs the thereshold voltage shifts reach 14 V after 4 Mrad
Too large for safe operation!

## Slide 56: CDC: End-plate
Design finalized.
Purchased in this FY.

## Slide 57: Performance of 1-bar/2-bar TOP
1-bar
2-bar
Timing fluctuation (25ps)
Incident angle fluctuation (1mrad)
Performance similar (weighted) for physics case studies
3% fake~4s

## Slide 58: Configuration choice (May, 2010)
Two configurations show similar performance
1-bar configuration shows stable performance as a function of increased timing jitter. 2-bar need precise, continual timing calibration during experiment operation.
1-bar case has larger forward acceptance and requires readout only in the backward direction. (forward cable routing is very crowded)
We chose the 1-bar configuration as baseline, with 2-bar as a backup option, due to these practical considerations.

## Slide 59: MCP-PMT photocathode
Typical QE at max.
  Bialkali (SBA); 28%
  Multialkali (MA); 24%
Performance check by simulation
  Difference QE distribution makes different chromaticity effect.
SBA shows better performance.
   Chose SBA.
  We push HPK to improve QE during production.

## Slide 60: MCP-PMT: improvement in lifetime
10
1
Belle II year
0
Old MA
New MA
SBA1
SBA2
5 yr
Protections against
Ion feedback
Neutral gas
were effective.

## Slide 61: End-cap Particle Identification
２０ｃｍ
Ring imaging Cherenkov counter based on silica aerogel radiator
  Space limited -> proximity focusing with expansion distance of 20 cm
  Requirements
    Transparent silica aerogel
    Photo-detector
      Single-photon sensitivity
      Pixel 5x5mm2
      Operational in 1.5T
      Compact
    Readout electronics
      ~70K channels
n=1.05 aerogel
|sc(p)-sc(K)| = 23 mrad at P=4GeV/c
Target: More than 4 s p/K separation at 4 GeV/c

## Slide 62: Novel “focusing” radiator
n1
n2
Focusing by 2cm+2cm aerogel (n1:1.047, n2:1.057)
4cm-thick single index aerogel
sq(1p.e.) = 22 mrad
Npe ~ 10.6
sq(track) = 6.9 mrad
sq(1p.e.) = 14.4 mrad
Npe ~ 9.6
sq(track) = 4.8 mrad
NIM A548(2005)383
 Multiple aerogel layers with different indices
Possible only with aerogel !
Simple accumulation of radiator layer gives more photons, but degrades PID performance

## Slide 63: HAPD QE Improvement
Chart: wavelength (nm)
| 360 | 380 | 400 | 420 | 440 | 460 | 480 | 500 | 520 | 540 | 560 | 580 | 600
Super Bialkali | 33.1434 | 32.9559 | 31.7898 | 28.6209 | 26.2823 | 22.2542 | 18.962 | 16.8336 | 10.4808 | 6.8457 | 5.0468 | 3.6142 | 2.2878
Conventional bialkali | 25.3509 | 24.6003 | 23.2302 | 20.1536 | 17.1289 | 13.6334 | 10.6105 | 8.4242 | 4.5578 | 2.1563 | 1.099 | 0.44118 | 0.12779
25%
32%
Peak QE > 30% has been achieved
HAPD QE has been greatly improved with “super bialkali” technology by Hamamatsu.

## Slide 64: Studies to Reduce Neutron Damage
Contribution of N-layer (hole) is about 1/100 of that of P-layer (e).
 Thinner P layer
Improvement confirmed with APD irradiation tests
 presumably this improves HAPD tolerance, too
 HAPD irradiation test is under way.
Chart: Gain
| 1 | 1.0047798667734422 | 1.0045705627548049 | 1.0047957920792008 | 1.0066158270238801 | 1.0080946054164175 | 1.0096871359930175 | 1.0097098864298129 | 1.0153292443214823 | 1.0225183823529398 | 1.0360548922539312 | 1.0543007425742572 | 1.0841493156668609 | 1.1234165695981426 | 1.1758108255678521 | 1.2444716438555619 | 1.3285572582993592 | 1.4234265797903318 | 1.53105889633081 | 1.6530239880605706 | 1.7914831464764125 | 1.949325677052991 | 2.1295546374490391 | 2.3338308095515434 | 2.5677963016890075 | 2.8360922029702973 | 3.1427680911473512 | 3.4952861094932772 | 3.9022914239953397 | 4.3760920209668024 | 4.921283488643013 | 5.5587734784507861 | 6.3154757571345366 | 7.2067696199767033 | 8.28661910308678 | 9.5940867064647648 | 11.204590128130461 | 13.213681202679092 | 15.760592603378004 | 19.035062973209083 | 23.35446090564939 | 29.191995486313335 | 37.408770748398368 | 49.573201805474646 | 69.098309187536358 | 104.73482090856143 | 188.35860148514851
5280 | -2.89e-06 | 0.00021001 | 0.00030458 | 0.00038593 | 0.00047151 | 0.00055338 | 0.00060487 | 0.00068271 | 0.0007601 | 0.00083617 | 0.00092331 | 0.001031 | 0.0011296 | 0.0012589 | 0.0013797 | 0.0015607 | 0.0017623 | 0.0019935 | 0.0022146 | 0.0024458 | 0.0026784 | 0.0029244 | 0.0031938 | 0.0034556 | 0.0037516 | 0.0040642 | 0.0044026 | 0.0047713 | 0.0051857 | 0.0056322 | 0.0061409 | 0.0066954 | 0.007344 | 0.008076 | 0.00894 | 0.009961 | 0.011205 | 0.01273 | 0.01465 | 0.017079 | 0.020261 | 0.024527 | 0.03049 | 0.03927 | 0.053167 | 0.078608 | 0.1381
5266 | -1.38e-06 | 0.00022533 | 0.00032487 | 0.00040948 | 0.00049654 | 0.00057804 | 0.00063995 | 0.00073281 | 0.00079792 | 0.00086616 | 0.0009542 | 0.0010315 | 0.0011218 | 0.0012053 | 0.0013115 | 0.0014245 | 0.0015454 | 0.001695 | 0.0018542 | 0.0020354 | 0.0022639 | 0.0025529 | 0.0028589 | 0.0031486 | 0.0034466 | 0.0037493 | 0.0040562 | 0.0043768 | 0.0047187 | 0.0050777 | 0.005458 | 0.0058643 | 0.0063072 | 0.0067866 | 0.0073065 | 0.0078783 | 0.0085114 | 0.0092034 | 0.0099794 | 0.010851 | 0.011831 | 0.01294 | 0.01421 | 0.015666 | 0.017367 | 0.01939 | 0.021835 | 0.024842 | 0.028632 | 0.033471 | 0.039931 | 0.048832 | 0.061819 | 0.082426 | 0.11965
5252 | 6.6544e-06 | 7.7102e-05 | 0.00011596 | 0.00015204 | 0.00018677 | 0.00022441 | 0.00025622 | 0.000292 | 0.00033212 | 0.00036742 | 0.00041036 | 0.00045982 | 0.00051103 | 0.00054442 | 0.00061377 | 0.00065647 | 0.00074731 | 0.00084769 | 0.00096259 | 0.0011257 | 0.0012924 | 0.0015668 | 0.0019275 | 0.0024074 | 0.0030737 | 0.0040585 | 0.0055581 | 0.0079194 | 0.012002 | 0.019867 | 0.039453 | 0.13833
5256 | -9.9671e-06 | 0.00011728 | 0.0002046 | 0.00031965 | 0.00042671 | 0.00061222 | 0.00075996 | 0.00091312 | 0.0010838 | 0.0012431 | 0.0014451 | 0.0016421 | 0.0018746 | 0.002107 | 0.0023883 | 0.0027085 | 0.003057 | 0.0034672 | 0.0039364 | 0.0044835 | 0.0051248 | 0.0058781 | 0.0067575 | 0.0077593 | 0.0089003 | 0.010259 | 0.011922 | 0.014011 | 0.016653 | 0.020102 | 0.024675 | 0.030867 | 0.039583 | 0.052254 | 0.072246 | 0.10634 | 0.17446 | 0.36407 | 0.50605
5278 | -0.00025481 | -0.00017599 | -0.00014878 | -6.8894e-05 | 4.7066e-05 | -8.1021e-05 | -4.2216e-05 | 0.00021896 | 0.00018402 | 0.0004261 | 0.0009455 | 0.0011847 | 0.0013999 | 0.0017564 | 0.0024982 | 0.0030966 | 0.0039233 | 0.0043745 | 0.005653 | 0.006818 | 0.0087422 | 0.012054 | 0.018103 | 0.033063
5741 | 2e-06 | 5.339e-05 | 8.487e-05 | 0.00011852 | 0.00015512 | 0.00018641 | 0.00022947 | 0.00028939 | 0.00038229 | 0.00053341 | 0.00079504 | 0.00095074 | 0.0011558 | 0.0014312 | 0.0018188 | 0.0023799 | 0.0027607 | 0.0032534 | 0.0038918 | 0.0047728 | 0.006035 | 0.0079881 | 0.011395 | 0.01866
5289 | 3.0645e-07 | 9.4666e-05 | 0.00014844 | 0.00019665 | 0.00024105 | 0.00028822 | 0.00033556 | 0.00038386 | 0.00043319 | 0.00048549 | 0.0005412 | 0.0006021 | 0.0006656 | 0.00072837 | 0.0007977 | 0.0008785 | 0.00097733 | 0.0011 | 0.0012531 | 0.0014519 | 0.001707 | 0.0020456 | 0.0025038 | 0.003132 | 0.0040167 | 0.0053025 | 0.0072398 | 0.010309 | 0.015533 | 0.025504 | 0.049429 | 0.15373
5288 | -4.3795e-07 | 9.7968e-05 | 0.00015293 | 0.00020247 | 0.00024972 | 0.00029651 | 0.00034523 | 0.0003943 | 0.00044372 | 0.00049737 | 0.00055558 | 0.00061764 | 0.00068317 | 0.00074845 | 0.0008214 | 0.00090386 | 0.0010052 | 0.0011293 | 0.0012874 | 0.0014903 | 0.001752 | 0.0020995 | 0.002567 | 0.0032091 | 0.004116 | 0.0054274 | 0.0074076 | 0.010542 | 0.015871 | 0.02605
5258 | 1.3333e-06 | 0.00017418 | 0.00029286 | 0.00042995 | 0.00061865 | 0.00084693 | 0.001078 | 0.0012983 | 0.0015343 | 0.0017786 | 0.0020458 | 0.00235 | 0.0026693 | 0.0030325 | 0.0034298 | 0.0038815 | 0.0044014 | 0.0049994 | 0.0056953 | 0.0064996 | 0.0074458 | 0.008557 | 0.009858 | 0.011381 | 0.013072 | 0.015086 | 0.017559 | 0.020645 | 0.024572 | 0.02966 | 0.036413 | 0.045571 | 0.058354 | 0.077213 | 0.10666 | 0.15696 | 0.25758 | 0.53675
5257 | -2.8327e-07 | 0.00015891 | 0.00026672 | 0.00039474 | 0.00056564 | 0.00078409 | 0.0010131 | 0.0012175 | 0.0014466 | 0.001685 | 0.0019205 | 0.0021939 | 0.0024852 | 0.0028179 | 0.0031923 | 0.0036214 | 0.0041082 | 0.0046723 | 0.005333 | 0.0060957 | 0.0069828 | 0.0080291 | 0.0092565 | 0.010675 | 0.012264 | 0.014164 | 0.016506 | 0.019419 | 0.023137 | 0.027945 | 0.034316 | 0.042948 | 0.054976 | 0.072646 | 0.1001 | 0.1466 | 0.23814 | 0.4832
Thick P
Current, thick N,
thin N
thin P
APD D leakage current (1012n/cm2)
P
N-
N
P+
N+
  Thinner APD to reduce neutron induced lattice deficits
：electron
：hole

## Slide 65
Trial production of the front end board in progress (Ljubljana).
~74mm
(~final size)
Prototype Merger board will be designed in this fiscal year.
The design of the next version of the ASIC (S03) has just started.
Shorter shaping time.
Production schedule depends on HAPD & front-end board development
Status of Readout Electronics for Aerogel RICH

## Slide 66: Front-end electronics of ECL
Back-end DAQ

## Slide 67: ECL Collector module
Role of the module:
Configure Xilinx FPGA on ShaperDSP modules
Synchronize sampling process on all 12 ShaperDSP modules
Collect data from 12 connected ShaperDSP modules
Calibration signal generation
Interface with remote PC for stand-alone operation
Provide interface with Belle II TTD and DAQ
Status:
Prototype module … produced
Remote firmware configuration on ShaperDSP … established
Interface with remote PC …established
Calibration signal generation … established
Rocket-I/O … to be tested soon

## Slide 68: Shaper DSP module
Key features:
16 channels per module
t=0.5ms shaper
FADC
Waveform fitting
  Output pulse height, timing, and quality of fit
Fast shaper + Variable gain amp. for trigger output.
Linearity <0.3%
(0.5% for Belle)
 | Belle | Belle II
Linearity | <0.5% | <0.3%
Shaping time | 1ms | 0.5ms
ENE | ~200keV | ~300keV
ENE (w/ pile-up noise) | 500-1000keV | 400-600keV
Status:
Prototype module … produced
New revision … to be submitted in this FY

## Slide 69: Most critical path of each subsystem
 | Most crucial item | Necessary time
BP | Design study, Beryllium pipe production | 1-1.5 years, 1 year
PXD | Sensor production | 1.5 years
SVD | Sensor production | 2 years
CDC | Drilling small cell end-plate | 9 months after getting skilled
TOP | Quartz bar production | 2.3 years
A-RICH | HAPD production | 1.3 years
ECL | (To exchange pre-amps If we do so) | 
KLM | Scintillator bar production | 1.5 years,
Simpler Be pipe by new companies
(g 4 months)
New companies (in US)
g 1 year

## Slide 70: Commissioning procedure
Roll-out position
Roll-in position
Belle II constructed
Linac commissioning,
MR commissioning phase 1
Global Cosmic Ray
w/ and w/o B-field
BEAST II
Belle II roll-in
Belle II w/o VXD
phase 2
VXD installation
GCR
Belle II
Physics Run
Main Ring commissioning with BEAST II, without Solenoid, probably with Aluminum beam pipe.
Main Ring commissioning with Solenoid. VXD is not installed in Belle II.
Field measurement along beam line.
VXD
Belle II
t
<1 month Global Cosmic Ray w/o B field if required.
No earlier than 2014.10
Extensive Software-completion Phase
(slow-control, online, alignment, PXD-ROI, … )
VXD = BP+PXD+SVD (scenario 1)