## Slide 1: Overview of Design Issues
17th KEKB Accelerator Review
Feb. 20, 2012
Haruyo Koiso

## Slide 2: Parameters
 | 2011 Feb. HER no wiggler | 2012 Feb. HER 60% wigglers
Energy (GeV) (LER/HER) | 4.0/7.00729 | 4.0/7.00729
by* (mm) | 0.27/0.30 | 0.27/0.30
bx* (mm) | 32/25 | 32/25
ex (nm) | 3.2/5.3 | 3.2/4.6
ey /ex (%) | 0.27/0.24 | 0.27/0.28
sy(nm) | 48/62 | 48/62
xy | 0.0897/0.0807 | 0.0881/0.0801
sz (mm) | 6/5 | 6/5
Ibeam (A) | 3.6/2.6 | 3.6/2.6
Nbunches | 2500 | 2500
Luminosity (1034 cm-2 s-1) | 80 | 80
HER ex with 60% wigglers is used as the nominal value.
Lower HER ex can relax some other parameters (bx/y*, ey /ex , etc. ).
At present, larger ey /ex in HER is adopted.

## Slide 3: HER Wiggler Section
・Decrease the horizontal emittance with wigglers.
・Only reuse LER wiggler magnets at T=0. (60%)
・Install more wigglers if possible. (40%)
Oho Straight Section
Reuse LER wiggler
RF section
beam

## Slide 4: IR Design
Design of IR (magnets, vacuum chamber, beam background estimation, collimation system, collision feedback system, etc) has been improved.
  Iron yokes for 3 more superconducting quadrupoles (QC1LE, QC1RE, QC2RP)
  More precise correction of higher multipoles
  Optimization of solenoid field distribution
  Optimization of physical aperture
Modeling of IR optics has also been improved by using 3D magnetic field calculation.
  Touschek lifetime is marginally kept to be ~600 sec.
Lattice design of IR (Tsukuba section + a part of arcs) is required to be finalized around the end of this fiscal year (March 31) to meet the construction schedule.
-> A. Morita, Ohuchi, Nakayama, Kanazawa, Funakoshi, et al.

## Slide 5: Injection
The synchrotron injection (fully or partially) will be necessary in HER because the transverse aperture is not sufficiently large for the betatron injection.
With the beam-beam interaction, simulations say that transient vertical blowup occurs after the betatron injection even in LER, which causes beam loss or background.
  Optimization of phase space profile by octupole correctors may cure this blowup.
Good qualities of injected beams with sufficient intensities are essential for stable operation with very short lifetimes.
  Overall (Touschek, luminosity and beam-gas) lifetime: LER/HER 360/373 sec, estimated by A. Morita.
  Needs optimization of beam distribution in Linac/BT lines.
-> M. Yoshida, T. Kamitani, H. Ikeda, T. Mori, et al.

## Slide 6: Error Correction
Estimation of error tolerance and development of optics correction system have been in progress.
  Requirements for beam diagnostics and control system (number of monitors, accuracy, speed, etc) are being decided step by step.
Error tolerances of IR magnets ( vibration, ripple of power supplies, etc) are very small. Realistic solution to maintain good conditions of optics and collision should be developed.
Sufficient correction and tuning knobs for optics correction and luminosity tuning should be equipped.
  Correction winding of each quadrupole (0.5%)
  Skew quadrupole windings of each sextupole (Dy ~ 1 mm)
  Rotated sextupoles or skew sextupoles to correct chromatic couplings
  etc.
-> H. Sugimoto, Y. Funakoshi, et al.

## Slide 7: Example of Parameter Dependence
90%
90%
HER coupling
0.28 -> 0.329 %
to keep xy LER<0.09
Luminosity degradation depending on some parameters are not so steep.
We will find several ways to reach 90 % of the target luminosity.

## Slide 8
backup