## Slide 1
Magnet Power Supply System
T. Kawamoto
T. Sueno
N. Tokuda
T. Oki
17th KEKB Accelerator Review Committee

## Slide 2
Contents
Existing KEKB power supplies.
New power supplies to be developed for SuperKEKB.
R&D and the preliminary test results.

## Slide 3
Existing KEKB Power supplies
We have ~ 2300 power supplies:
Class | # of power supplies | Typical load
Small-class (< 10 A, 0.5 kW) | 1885 | Steering magnet etc
Medium-class (< 500 A, 100 kW) | 368 | Local Quads
Large-class (< 500 A, 500 kW) | 14 | Quad families
Megawatt-class (< 1250 A, 1 MW) | 6 | Bending and Wigglers
Stability | < 20 ppm / day
Ripple | < 10 ppm
Setting resolution | <  50 ppm (16-bit DAC)
Typical spec.
To be reused
after appropriate maintenance and overhaul : in progress.
Rubbished and replaced by newly developed PSs: in progress.
To be reused.
Current setting resolution will be improved by 20-bit DAC.

## Slide 4
First new megawatt-class power supply
Other 9 power supplies for bending and wigglers will be delivered by end of March.
Just delivered to KEK in last week
(B2E, 2012/Feb./15th @D2)

## Slide 5
New Power supplies to be developed for SuperKEKB
Power | # of power supplies | Typical load
0.95 MW | 2* | LER / HER Bends.
0.4~1 MW | 8* / 1† | LER / HER Wiggs.
< 100 kW | (~ 50) | Local Q
~ 10 kW (1000 A) | (~ 10) | QCS main
~ 0.5 kW ( 50 A) | (~ 50) | QCS correction
< 70 kW | 23* | Damping Ring (Q, B …)
< 630 kW | 2† | Damping Ring (Bends.)
< 36 kW | (Many) | Damping Ring (Others)
Target spec. of power supply for Bends and Wiggs.
Stability | < 2 ppm / day
Ripple | < 1 ppm
Setting resolution | <  0.1 ppm (~23-bit)
*:developed in FY2011; †: in FY2012; ():spec./# has not been fixed.

## Slide 6
For more precise setting of the current,
increasing the DAC bits from present 16 to 20 or more is necessary.
  Step 1. Try new commercial use 20-bit DAC.
  (AD5791: released in 2010/March/11th by Analog Devices)
  Step 2. Two 20-bit DAC’s are combined for 24-bit resolution.
  Step 3. For 24-bit resolution, another scheme has been tried:
  summing the output of sixteen (= 24) 20-bit DAC’s.
R&D 1: higher current-setting resolution
1/220
1/24
+
Setting value
in 20-bit (major)
DAC
Setting value
in 4-bit (minor)
DAC
1/24
+
+

## Slide 7
Preliminary test result: two 20-bit DAC's 24-bit system
DAC output voltage (mV)
+2
0
−2
−4
−6
−8
Increasing DAC input digital value by 1 least significant bit (LSB),
DAC output voltage is measured by DMM KEITHLEY 2002.
(range: 2 V, integrate time in Power Line Cycles (PLC): 50, 10 moving digital filter)
1 LSB (0.6 mV) response can be seen.
2 mV
0 1 2 3 4 5×1000
Time (s)

## Slide 8
Digital feed back control for long-term stability improvement.
R&D 2: current-stability improvement
+
N
P
Output terminal
DCCT
DMM
Setting value
in 20-bit (major)
DAC
Error Detection
Setting value
in 4-bit (minor)
DAC
1/24
+
+
+
-
+
-
current loop
minor-
voltage loop
-
-

## Slide 9
Preliminary test result: digital feedback system
Long-term stability test was performed by using
a medium-class power supply (15 V, 500 A).
1.4 ppm / 8 hrs
(peak-to-peak fluctuation included)
7.5 ppm / 8 hrs
0.2 ppm (2 mV/10 V)
2 ppm (20 mV/10 V)
8 hrs
8 hrs
measured by DMM (20 V range, 10 PLC, 10 moving Filt)

## Slide 10
Summary
Small/medium-class power supplies: Overhaul is in progress.
Large-class power supplies for the Quad families: Improvement is planned for more precise setting resolution, increasing the DAC bits from present 16 (LER)/18 (HER) to 20. And overhaul is planned.
Megawatt-class power supplies: Old PSs were rubbished, and have been replaced by newly developed PSs: in progress.
New 10 megawatt-class power supplies for the main ring and 23 medium-class power supplies for the damping ring are to be delivered by end of March 2011.
R&D has been performed, and the preliminary results are satisfactory. 24-bit setting resolution and digital feedback system have been applied to the new 10 megawatt-class power supplies.

## Slide 11
Back-up slide

## Slide 12
Why sixteen DAC's 24-bit system?
Care must be taken to the monotonicity of two DAC’s 24-bit system
Not so bad
Bad

## Slide 13
Non linearity and monotonicity
LSB: least significant bit
DNL: differential non linearity
INL: integral non linearity
AD7846K (16-bit): DNL ±0.5 LSB max
INL ±2 LSB
AD5791B (20-bit): DNL ±0.75 LSB typ. (test result: <±0.1 LSB）
INL ±0.5 LSB typ. (test result: -0.2～+0.6 LSB）
Lose monotonicity

## Slide 14
Typical long-term stability
Prototype power supply for QCS main coil
  Power supply: Transistor-dropper type (1000 A-30 V).
  Test Load: 1.2 mW resistor
25℃－
15℃－
Initial drift
9 ppm
Stability: 11 ppm / 24 hrs.
24 hrs.
Temp: 20 ～27.5 ℃

## Slide 15
For precious control, lower jitter is necessary on the current monitoring.
Current is measured by a DCCT and a DMM.
      Power supply: Transistor-dropper type (1000 A-30 V).
    DCCT: 1000 A / 10 V output
    DMM: KEITHLEY 2002 (10 PLC, 20 V range)
How much jitter on the measured current
Chart: Current (A)
| 1000 | 800 | 600 | 400 | 200 | 0 | 200 | 400 | 600 | 800 | 1000 | 900 | 700 | 500 | 300 | 100 | 0
工藤電機 | 6.5928 | 3.9895 | 2.0584 | 2.281 | 4.6436 | 3.2431 | 2.1599 | 3.4123 | 2.0162 | 2.7384 | 8.253 | 5.8371 | 3.1172 | 2.7394 | 2.4842 | 1.8383 | 1.4705
IDX大型 | 4.3392 | 3.1154 | 3.1847 | 2.8907 | 2.8685 | 2.2392 | 2.1465 | 2.6217 | 3.469 | 3.8555 | 3.9699 | 3.0133 | 3.2146 | 2.3079 | 2.1791 | 2.1395 | 1.0396
10 mV corresponds to 1 ppm
Noise level: 0.6 mV

## Slide 16
Measured voltage ripple
Typical ripple
QF4E magnet system
  Power supply: Transistor-dropper type (500 A-380 V).
  Load: 40 Quads connected in series around KEKB ring.
Measured load impedance
50 Hz 300Hz
Z ~ 0.66 W + 0.58 H ( f < 1kH)
50 Hz: 0.7 ppm
300Hz: 0.3 ppm

## Slide 17
Schedule