## Slide 1: Optics Correction
Hiroshi Sugimoto (KEK) for SuperKEKB Optics Group
Contents
1. Correction of XY Coupling and Vertical Dispersion 2. Correction of Betatron Function 3. Full Optics Correction

## Slide 2: Introduction
Correction of beam optics errors will be a critical factor in SuperKEKB.
Innovative optics measurement & correction schemes are probably necessary at high-current beam operation. i.e. Horizontal & vertical (XY) coupling measurement with single-pass BPMs. (Ref. Ohnishi’s talk @ the 16th KEKB review)
On the other hand, KEKB based optics measurement using closed orbit distortion (COD) will be employed at early stage of the commissioning and low-current and non-collision operation.
It is informative to investigate how effective is KEKB based scheme.
Today’s Report
Optics Correction with KEKB based scheme
1. XY-Coupling and Vertical Dispersion 2. Betatron Function 3. Full Optics Correction

## Slide 3: XY-Coupling and Vertical Dispersion

## Slide 4: Measurement & Correction Scheme
XY-coupling measurement & correction. 1. XY-coupling is estimated by observing the vertical leakage orbits associated with horizontal kick. 2. Suppress the vertical leakage orbit by skew correctors.
Vertical dispersion measurement Use vertical orbit response with RF frequency change.
Phase slip factor
Orbit change
Frequency change
RF frequency

## Slide 5: Correctors
Skew winding of sextupole magnet will be available.
Symmetric / asymmetric excitation of skew-corrector pare can be used as orthogonal correctors for coupling and vertical dispersion.
Symmetric Excitation (XY-coupling corrector)
Asymmetric Excitation (Vertical-dispersion corrector)
Coupling parameters
Vertical dispersion
Skew-field
SD
SD

## Slide 6: Simulation
Assumptions - No orbit drift in time. - Zero-current (ignore intra-beam scattering in emittance evaluation). - No error source in the IR region.
 | Vertical misalignment [mm] | Rotation error [mrad]
Normal quadrupoles | 0 | 100
Normal sextupoles | 100 | 0
Sextupoles (local chromaticity) | 50 | 0
Error Source
All errors are Gaussian distributed.
Skew correctors are adjusted by measured optics and response matrix of the model lattice with singular value decomposition.

## Slide 7: Simulation Example
Before Correction
Vertical leakage orbit
IP
No BPM Jitter

## Slide 8: Simulation Example (No BPM Error)
After Correction

## Slide 9: Vertical Emittance and BPM Jitter Error
Target
Design
100 simulations with different seed of random numbers.
Emittance before correction
Jitter Error 0 mm Jitter Error 2 mm Jitter Error 5 mm
Emittance after 1 correction
Corrections of XY-coupling and vertical dispersion effectively reduce vertical emittance.

## Slide 10: Vertical Emittance and BPM Jitter Error
Target
Design
Jitter Error 0 mm Jitter Error 2 mm Jitter Error 5 mm
After 5 corrections
Iterative correction is effective especially when BPM jitter error is large
Emittance before correction
100 simulations with different seed of random numbers.

## Slide 11: Vertical Emittance and BPM Rotation Error
0.1 mrad 0.3 mrad 0.6 mrad
Vertical Emittance after 5 corrections
BPM rotation error should be less than 0.5 mrad for the target vertical emittance.
Target
Design
100 simulations with different seed of random numbers.

## Slide 12: Dynamic Aperture (DA)
DA is dramatically improved by the optics correction.
Before Correction
After Correction
100 simulations with different seed of random numbers.
Design

## Slide 13: Betatoron Function

## Slide 14: Beta Measurement
COD at the i th BPM induced by j th steering kick in two forms.
Find
which reproduce measured beam positions
The solution is obtained by iteratively minimize two quadratic functions.
and
Ref. A. Morita et al, PRSTAB 10, 072801 (2007)
Analyze CODs induced by steering kicks.

## Slide 15: Beta Measurement @ SuperKEKB HER
This scheme inevitably has two ambiguous.
IP
No BPM Jitter
1. Scaling of beta function
2. Phase origin
Measured
Exact

## Slide 16: Beta Measurement @ SuperKEKB HER
To avoid the ambiguous we use difference between neighborhood BPMs in the optics correction.
IP
No BPM Jitter
Measured
Exact

## Slide 17: Simulation of Beta Correction
Assumptions - No orbit drift in time. - Zero-current (ignore intra-beam scatteringin emittance calculation). - No error source in the IR region. - Exact values of perturbed tunes are known.
Error Source (Gaussian distributed)
Beta Measurement - Use 6 horizontal and 6 vertical orbit kicks. - Orbit amplitude at Arc section is about < 1mm.
Corrector all quadrupoles (fudge factor of the electric power supplies)

## Slide 18: Beta Correction @ SuperKEKB HER
No BPM Jitter
After
Before
After
Before

## Slide 19: Global Beta Beat After Correction (SuperKEKB HER)
BPM Jitter 2 micron
Typically, global beta beat for 2 micro bpm jitter is within ~5% for horizontal and within ~10% for vertical betatron motion.
100 simulations with different seed of random numbers.

## Slide 20: Full Optics Correction

## Slide 21: Measurement Method and Corrector Knob
All measurements are based on COD or its response.
 | Measurement Method | Corrector Knob
COD | BPM reading | Horizontal/Vertical Steerings
XY Coupling | COD response associated with horizontal steering kick | Skew winding of sextupoles
Vertical Dispersion | COD response associated with RF frequency change | Skew winding of sextupoles
Betatron Function&Phase | COD response associated with steering kick | quadrupole (fudge factor)
Horizontal Dispersion | COD response associated with RF frequency change | Horizontal mover of focusing sextupoles

## Slide 22: Simulation Condition
Assumptions - No orbit drift in time. - Zero-current (ignore intra-beam scattering in emittance calculation). - No error source in the IR region. - Exact values of perturbed tunes are known.
Error Source
 | Horizontal misalignment [mm] | Vertical misalignment [mm] | Rotation error [mrad] | DK/K
Quadrupoles | 100 | 100 | 100 | 2.5*10-4
Sextupoles | 100 | 100 | 0 | 0
Beam optics is unstable if we introduce the error sources at once.
Thus, we gradually increase the error amplitude with the optics corrections.

## Slide 23: Emittance
Target
Design
Jitter Error 5 mm Jitter Error 2 mm Jitter Error 0 mm
100 simulations with different seed of random numbers.
Iterative correction with adjusting correction parameters is necessary to improve vertical emittance.
Reached vertical emittance is sensitive to the correction parameters especially when BPM jitter is large.

## Slide 24: Beta Beat After Optics Correction
100 simulations for different random seeds.
2 micro BPM Jitter
Vertical beta beat is typically within ~10%, and ~5% for horizontal direction.

## Slide 25: Dynamic Aperture
On-momentum aperture is improved to the design level.
Optimization of higher order multipole magnets is necessary to improve off-momentum aperture (in progress)
Design
2 micro BPM Jitter
20 samples

## Slide 26: Summary and …
COD based scheme is applied to SuperKEKB HER lattice.
Iterative corrections is necessary to reduce vertical emittance.
BPM rotation should be less than 0.5 mrad for the target vertical emittance.
In typical case, global beta beat is within ~5% for horizontal and within ~10% for vertical betatron motion.
After full optics corrections, we can reach the target vertical emittance.
Achieved vertical emittance is sensitive to the correction parameters especially when BPM error is large.
On-momentum DA is improved to the design level.
As for off-momentum DA, it is expected to be improved by tuning higher order multipole fields, but not confirmed yet.
To be studied
More detailed study on optics measurement using single-pass BPM.
Error source in IR region.
Orbit drift
and so on…
Thank you for listening!