## Slide 1: Optics Issues
Hiroshi Sugimoto for Optics Group
Notes: 1

## Slide 2: Contents
Optics Design Issues Except for IR - Tsukuba straight line, nominal tune, Beast optics, etc. - Tunnel subsidence effect on vertical emittance
IR Optics Design - Design changes - Dynamic aperture and Touschek lifetime
Error Field from Final Focusing Magnets (QCS) - Normal sextuple error field - Skew sextuple error field - Possible design change plan

## Slide 3: Optics Design Issues Except for IR
Notes: 3

## Slide 4: Machine Parameters
Change LER vertical tune from 44.57 to 44.57
 | LER | HER
Energy (GeV) | 4.0 | 7.00729
Current (A) | 3.6 | 2.6
#of bunches | 2500 | 2500
bx* (mm) | 32 | 25
by* (mm) | 0.27 | 0.30
ex* (nm) | 3.2 | 4.6
ey* (pm) | 8.64 | 11.5
sz* (mm) | 6 | 5
nx , ny | 44.53 , 46.57 | 45.53 , 43.57
ns | -0.0247 | -0.0280
xy | 0.0881 | 0.0807
Luminosity (1034 cm-2 s-1) | 8x1035 | 

## Slide 5: LER Optics Changes - Wiggler Section -
Vertical beta is suppressed to mitigate the beam-gas scattering effects.
Integer part is increased by 2 while keeping the fractional part.
Old
New
by
bx
hy
hx

## Slide 6: Tsukuba Straight Line is Finalized
LER
HER
Belle Axis
IP
Interference problem between LER&HER has been resolved while keeping optics, orbit length and IP geometry.
concrete shield
concrete shield

## Slide 7: Off 4S Operation
Capability of off-4S operation is confirmed considering limitation of magnet field strength.
Optics and hardware design is carried so that keep the capability.

## Slide 8: Phase 1 - Linear Optics -
Optics W/O QCS and solenoid has been designed
QCS and solenoid is replaced by drift space.
Machine tuning except for IR is expected to be done in this phase.
LER
HER
Drift
Drift

## Slide 9: Phase 1 - Dynamic Aperture -
DA example assuming, - Design bunch current. - 2% emittance ratio.
Beam loss estimation is ongoing from view point of radiation protection.
HER Touscheck Life ~6.3 hours
LER Touscheck Life ~1.4 hours
Funakoshi-san’s talk
Physical Aperture
RF Bucket
Notes: Physical aperture LER 91*sigma
Physical aperture HER 48*sigma
rf bucket HER 36.07
rf bucket LER 33.89

## Slide 10: Simulation of Tunnel Subsidence
The subsidence effect is investigated with numerical simulation.
Put the subsidence to design lattice as a vertical misalignment of each magnet.
Marker Level (Measurement)
IP
Change amplitude of misalignment, and evaluate vertical emittance.
Numerical Simulation
IP
BPM Readings
Beam Orbit
Misalignment
Import
Simulation

## Slide 11: Simulation of Tunnel Subsidence (cont’d)
Vertical emittance exceeds the target values, 5pm, after 7 years when 2mm/year is assumed.
ey
ey
shy
shy
ey
shy
W/O Optics Correction
W/ Optics Correction
Target (ey=5pm)

## Slide 12: Simulation of Tunnel Subsidence (cont’d)
V-LCC misalignment has very critical impact on emittance.
Need special care for orbit control or/and alignment in this region.
What is the most dominant source of emittance dilution?
W/O V-LCC misalignment
W/ V-LCC misalignment
ey
shy
ey
ey
shy
shy
Target (ey=5pm)

## Slide 13: IR Optics Design
Notes: 13

## Slide 14: IR Design
All quadrupoles except for QC1P have iron yoke for preventing field leakage to the another beam line
Canceller coils are installed for HER beam line to suppress leakage filed from LER QC1 magnet.
All magnets have super-conducting corrector coils. - Normal&Skew Dipole, Skew Quad, Octupole

## Slide 15: IR Design Upgrade
LER QCs now have vertical offset to reduce dipole corrector strength.
Old
New
Vertical Kick Angle
Beam orbit
Magnet | QC1LP (mrad) | QC2LP (mrad) | QC1RP (mrad) | QC2RP (mrad)
Old | 2.472 | 2.746 | -2.082 | 2.491
New | -0.149 | 1.651 | -0.644 | 1.602
Vertical Kick Angle
QC2RP
QC1RP
QC2LP
QC1LP
IP
Vertical Offset
IP
1.0mm
1.5mm

## Slide 16: Dynamic Aperture & Touschek Lifetime
Touschek lifetime is optimized with Down-hill simplex method.
Available knobs are 54 sextupole families and 4 octupole magnets.
Lifetime of both beams is almost reached the target value, 600 sec.
HER 615 sec
LER 588 sec

## Slide 17: Error Field from QCS
Notes: 17

## Slide 18: Field Measurements of QCS Prototype
Unexpected normal&skew sextupole have been observed.
Their magnetic field strength is ~0.1% of quadrupole field.
Impact on dynamic aperture has been investigated.
Normal Sext.
Skew Sext.
Field profile along QC1P
Longitudinal position [mm]
Field strength relative to quad. field [x10-4]
Ohuchi -san’s talk

## Slide 19: LER DA with Normal Sextupole Error Field
Thin lens Sextupoles are inserted to QC1L and QC1R.
There magnitudes are same, but signs are independent.
Evaluate DA for 4 possible combinations of sign at each error field strength.
Effect is very critical.
QC1R w/ sext. error
QC1L w/ sext. error
IP
Same Sign
Opposite Sign

## Slide 20: Sextupole Corrector Coil
Only R-size design can be changed. (L-size is already fixed)
No more space for installing the corrector to QCS itself.
We are considering installation between QC1R and QC2R.
HER
Octupole
Sextupole Coil
IP
QC2LP
QC1LP
QC1RP
QC2RP
QC2LE
QC1LE
QC1RE
QC2RE
LER
Octupole
Octupole
Octupole
Octupole
Octupole
Octupole
Octupole
Sextupole Coil

## Slide 21: DA Improvement by Corrector Coil
DA degradation is improved, but B3/B2 < 0.1% is preferable.
Introduce sextupole error to ALL QCs.
Check whether we can mitigate DA degradation by optimizing the corrector strength.

## Slide 22: Skew Sextupole Error Field
Analogous calculation for skew sextupole error field.
Different feature compared to the normal sextupole case.
DA Improvement is not enough level.

## Slide 23: Lifetime and Corrector Coil Position
DA survey with changing corrector position.
Only QC1RP has skew sextupole error.
Corrector coil must be installed between QC1L & QC1R
Design
QC2R
QC1R w/ error
QC1L
QC2L
IP
Scan effective corrector position

## Slide 24: Design Change Strategy
Points to be considered.
Need 1 normal sextupole corrector.
Need 2 skew sext. correctors.
One of skew sext. must be installed to QC1R.
Each QC can have only one corrector coil
Possible to install additional coil between QC1R and QC2R.
Octupole
Octupole
Octupole
Octupole
Octupole
Octupole
Octupole
Octupole

## Slide 25: R-side Design Change Plan (Not Fixed Yet)
Possible Plan
Install normal Sext. coil (+octupole) to between QC1 and QC2.
Install skew Sext. coil to both QC1 and QC2 instead of octupoles.
Octupole
IP
QC2LP
QC1LP
QC1RP
QC2RP
QC2LE
QC1LE
QC1RE
QC2RE
Octupole
Octupole
Octupole
Octupole
Octupole
Octupole
Octupole
Normal Sext. (+ Oct.)
Skew Sext.
Skew Sext.
Skew Sext.
Skew Sext.
Normal Sext. (+ Oct.)

## Slide 26: DA W/ and W/O R-side Octupoles
Touschek lifetime estimated by DA seems OK.
HER W/ Octupoles ~ 670 sec
HER W/O Octupoles ~ 660 sec
LER W/ Octupoles ~ 580 sec
LER W/O Octupoles ~ 590 sec

## Slide 27: Side Effect of Removing Octupole from QC1
HER
LER
No remarkable effect is observed so far.
FMA indicates enhancement of some ronances.
W/ Octupoles
W/O Octupoles
4th order 5th order
6th order 7th order

## Slide 28: Summary
Thank you for listening!
Optics Design and Issues (Except for IR) - Almost completed. - Minor changes related to detailed hardware design is now continued. - Need special cares for orbit control or/and alignment in V-LCC region.
IR Design - Vertical offset is adopted to LER-QCS for saving dipole corrector strength. - Lifetime of both beams is almost reached the target value, 600 sec.
Error Field from QCS - Nomal&Skew sextuple error field has critical effects on DA. - Additional corrector coil is planned to install.

## Slide 29: Appendix
Appendix

## Slide 30: Touschek-Lifetime History
DA has been steadily improved by feedback cycle between Optics & Magnet group.
HER
LER
2D IR Model
3D IR Model