## Slide 1
Collision feedback
OKI, Toshiyuki
on behalf of the working group
2014/MAR/3rd
19th KEKB Accelerator Review Committee

## Slide 2
Introduction
 | SuperKEKB | KEKB
ey | ~8.6pm (LER) | 150pm
by* | 0.27mm(LER) | 5.9mm
sy* | 48nm | 940nm
The beam size is 20 times smaller than one of KEKB.
How to collide beams successfully is much more difficult than KEKB.
High luminosity machine can be spoiled by the small vibration of QCS (QC1, QC2) caused by ground motion, even if it didn’t affect KEKB.

## Slide 3
1000
100
10
1
0.1
Integral amplitude (nm)
Measured
ground motion
(input data)
25 nm@25 Hz
Luminosity degradation (based on beam-beam simulation by K. Ohmi)
Y. Funakoshi
QC1RP and QC1RE vibrate with same phase,
but the amplitude difference still arises: 25 nm at 25 Hz…
Phase (deg.)
H. Yamaoka
Frequency (Hz) | 24.85 | 38.93 | 69.34 | 99.60
DyIP*rms (nm) | 18.63 | 1.72 | 8.29 | 3.14
L/L0average (%) in case of model-A (and F) | 95.4 (96.1) | 99.8 (99.8) | 99.7 (99.8) | 99.7 (99.8)
Estimation of QCS vibration and luminosity degradation
(vertical)

## Slide 4
Beam-Beam simulation results
K. Ohmi
Just 20 nm offset leads to 6 % degradation of luminosity.

## Slide 5
H. Yamaoka
Reinforcement of bridge structure
2013 Dec.

## Slide 6
Feedback scheme in vertical direction (y and y’)
The orbital feedback system was used successfully for KEKB, which is based on beam-beam kick calculated from the BPM readouts at both sides of the IP.
Offset at IP
Dy= ~5nm (0.1 sy*)
4 BPMs
(0.5m from IP)
Difference at BPM
Dy = ~1.3mm
Prototype BPM was tested by using sinusoidal input signal.
0.1mm resolution has been obtained, successfully.
H. Fukuma
For SuperKEKB, It will be expected to work well. The target resolution of BPM is the order of micrometer.
beams are deflected
by beam-beam kick

## Slide 7
ps & magnet
1st order lag
(delay = 0.1ms)
+
−
PID
Ge
plant
1st order lag
(delay = 0.21ms)
reference
monitor out
PID tuning
Ziegler-Nichols
disturbance
Ga
M
monitor LPF(FIR)
D
delay 3 clocks
Fs = 32kHz
Group delay of LPF =0.4ms
+
+
Result shows
−16.7dB@25Hz is expected.
Amplitude of DyIP*rms @25Hz will be
reduced from 19 nm to 2.8 nm.
10
0
− 10
− 20
− 30
− 40
− 50
− 60
0 20 40 60 80 100 120 140 160
Frequency (Hz)
Rejection gain (dB)
Rejection gain evaluation of the feedback system
H. Fukuma

## Slide 8
Beam-beam kick will not be a sensitive parameter for monitoring collision, as beam-beam parameter ξx is so small:
        ξx ~ 0.0028(e+), 0.0012(e-)
        (↔ ξy ~ 0.0881(e+), 0.0807(e-))
Beams are not so much deflected in horizontal direction.
⇒The Luminosity dither is being considered, which was used for PEP-II successfully.
Feedback scheme in horizontal direction (x)
Dx
When two beams overlap, the luminosity drops on either side of the peak, giving modulation at 2ωdith.
Off center, there is additional modulation at the fundamental.
Dithering simulation by U. Wienands and S.Uehara:
Max. dithering amplitude, which corresponds to 10 % drop of the peak luminosity should be prepared.

## Slide 9
Luminosity dither system for horizontal feedback
(+ vertical offset and angle)
  (1) Fast luminosity monitor (ZDLM): S. Uehara and P. Bambade.
(2) Electronics to discriminate dither signals:
  Lock-in amplifiers and/or digital technic are considered.
(3) Beam pipes: made of stainless steel for magnetic field penetration.
(4) Air-core dithering coils:
    - Dithering coils will be installed into 8 locations.
    - Dither frequency: 60~100 Hz is chosen to avoid power line interference.
    - Kick angle of dither coils: to generate ±50 mm horiz. bump.
    - Design work, production and field measurement are under way at SLAC.
(5) Power supplies for actuating coils: commercial bipoler PS (± 65 V, ± 5 A).
(6) Iron-core steering magnets at HER for orbit correction.

## Slide 10
Lock-in amplifier: Stanford research systems model SR830
SLAC loaned us the Lock-in amp. last summer.
We have tried to use it with EPICS for a remote control.

## Slide 11
Locations for the dithering coils
8 locations for the dithering coils in LER around IP.
ZDS1RP
ZDS2RP
ZDS3RP
ZDS4RP
ZDS1LP
ZDS2LP
ZDS3LP
ZDS4LP

## Slide 12
Designs for 3 type of beam pipes
ZDS1{L, R}P
  Inner diameter: 80 mm
  Thickness: 2 mm
ZDS2{L, R}P
  Inner diameter: 90 mm
  Thickness: 3 mm
  10 mm Cu coating inside.
ZDS{3, 4}{L, R}P
  Inner diameter: 90 mm
  Thickness: 5 mm
  10 mm Cu coating inside.
All pipes are made of SS316L.
Y. Suetsugu
Pipes will be delivered to KEK by this March.

## Slide 13
Damping of magnetic field due to eddy current
A.W. Chao and M. Tigner, Editors,
Handbook of
Accelerator Physics and Engineering,
World Scientific, Singapore (1999), p. 268
Damping ratio
Resistive and thinner pipe suppresses the damping effect.
1k 10k 100k
SS316L
Copper
(KEKB
LER pipe)
Dithering
freq. range

## Slide 14
Coil mechanical design
M. Kosovsky, SLAC

## Slide 15
Coil field evaluation
Calculations show that the field quality meets the requirements:
10 mm (15 sx + 2 mm) radius of good field region for dB/B < 10−3
  ‒ verification of model using OPERA-3D was performed.
  ‒ Note: Effect of chamber eddy currents not included.
U. Wienands, SLAC
10−3
10−3
Example of horizontal coil

## Slide 16
Coil parameter
Resistance, inductance and power are within acceptable limits
(up to ~ 10 V, 13 W/coil (real peak power) at 5 A, 100 Hz)
U. Wienands, SLAC

## Slide 17
Fabrication and field measurement
Fabrication and measurement of coils will be finished by this March.
U. Wienands, S.D. Anderson, MFD Metrology, SLAC

## Slide 18
Summary
— It is challenging to collide small beams successfully.
— For vertical offset and angle feedback:
Orbital feedback system is under consideration. It was used for KEKB and is based on beam-beam kick calculated from the BPM readouts at both sides of the IP.
— For horizontal offset feedback:
Luminosity dither is being considered as used for PEP-II, because beam-beam kick will not be a sensitive parameter for monitoring collision due to small beam-beam parameter.

## Slide 19
Appendix

## Slide 20
Model-A
R側
L側
25nm@20Hz
14nm@50Hz
Oscillation phases of QC1RP and QC1RE.
H. Yamaoka

## Slide 21
Experience at KEKB
(1) Finding good collision
1. Calculate beam-beam kick (b-b deflection)
using BPMs.
2. Change bb kick by changing setting of
steering magnets located on either side of the IP.
3. Luminosity scan: Lumi. vs bb kick.
(2) Maintaining good collision
Beam-beam kick
Vertical bump height @IP
Bump height created by steering magnets @IP to maintain bb-kick
Luminosity scan
M. Masuzawa

## Slide 22
Damping and phase delay of a magnetic field
A.W. Chao and M. Tigner, Editors,
Handbook of
Accelerator Physics and Engineering,
World Scientific, Singapore (1999), p. 268
Damping ratio Phase delay
~wt
~1/(wt)
1/√2
p /4
t =1/wcutoff

## Slide 23
Test setup
KEKB LER beam pipe made of copper:
53 mm radius, 6 mm thickness.

## Slide 24
Chart: frequency (Hz)
Test results
— I (mA)
— B (mT)
— B/I (T/A)
— Phase difference (B−I) (deg)
Chart: frequency (Hz)
Without beam pipe
With beam pipe

## Slide 25
Test result summary
Material: Copper
Inner diameter: 94 mm
Thickness: 6 mm
Good agreement with calculation.
Strongly damped at the target frequency range: Dithering (60~100 Hz)
1k 10k 100k
1k 10k 100k

## Slide 26
Conceptual drawing of beam pipes
Kanazawa
Material: SS316L
Inner diameter: 80 mm
Thickness: 2 mm
Material: SS316L
Inner diameter: 90 mm
Thickness: 3 mm for round type, 6 mm for antechamber
10 mm Cu coating inside.
Suetsugu

## Slide 27
Calculations for the round SS beam pipes
Resistive and thinner pipe suppresses the damping effect.
The Cu coating is effective above 1 kHz.
1k 10k 100k
1k 10k 100k
t =0.26, 0.12, 0.07 ms