## Slide 1: Ring commissioning
2015.2.24
SuperKEKB Review
Y. Funakoshi for the SuperKEKB commissioning group and IP orbit FB group

## Slide 2: Injection time (question by F. Zimmerman to Kamitani-san)
Injection time
  Linac beam charge: 1nC
  Repetition rate: 50Hz
  To accumulate 1A, it takes about 5 min.
  In Kamitani-san’s talk, he mentioned e+ charge of 0.66nC/bunch at the end of Linac. In this case, it takes about 2.5 min. to store 1A in phase 1.
Actual injection time depends on the injection efficiency and the beam lifetime.
At KEKB, a typical injection time for storing the operation beam current (~1.0A e-, ~1.6A e+) was ~30min at 50Hz (sum of e- and e+ injection).

## Slide 3: Beam lifetime
 | KEKB (design) |  | KEKB (operation) |  | SuperKEKB Design | 
 | LER | HER | LER | HER | LER | HER
Radiative Bhabha | 21.3h | 9.0h | 6.6h | 4.5h | 28min. | 20min.
Beam-gas | 45ha) | 45ha) |  |  | 24.5min.b) | 46min. b)
Touschek | 10h | - |  |  | 10min. | 10min.
Total | 5.9h | 7.4h | ~133min. | ~200min. | 6min. | 6min.
Beam current | 2.6A | 1.1A | 1.6A | 1.1A | 3.6A | 2.6A
Loss Rate | 0.12mA/s | 0.04mA/s | 0.23mA/s | 0.11mA/s | 10mA/s | 7.2mA/s
a) Bremsstrahlung
b) Coulomb scattering, sensitive to collimator setting
As for loss rate, beam loss accompanied with the beam injection should be added.
4nC@25Hz
2.9nC@25Hz

## Slide 4: Contents
Update of commissioning scenario
Operation tools
Update of dithering system for beam collision
Collaboration with other laboratories

## Slide 5: Contents
Update of commissioning scenario
Operation tools
Update of dithering system for beam collision
Collaboration with other laboratories

## Slide 6: Update of commissioning scenario
Time of commissioning
  Phase 1: start from Jan.-Mar. 2016
  Damping ring commissioning: start before phase 2
  Phase 2: start from spring 2017?
Period of commissioning
  Damping ring commissioning
    3 weeks (old estimation) -> ~3 months (recent more realistic estimation)
More precise consideration of each step
  Beast study
    Emittance control bump system will be required sometime in phase 1.
    We have discussing with Belle II group on the slow control system.
      Which kinds of information are needed on both sides as the EPICS records.
        How fast? and Time preciseness of the data?
    Belle II people wanted to know the history of vacuum pressure change from the beginning of KEKB commissioning.
    Required machine time for Beast: ~ 1 week (phase 1), ~2 weeks (phase 2)

## Slide 7
DR Commissioning
LTR commissioning 2 days
BPM commission
First turn 1 day
COD meas. and correction 2 day
BPM commission
Optics meas. 2 days
RTL commissioning 2 days
Injection to LER
25 Hz operation
SR commission
Vacuum scrubbing ~14 days
~ 3 weeks
by wishful thinking
SuperKEKB Commissioning Meeting 2011.11.08 Kikuchi, M.
~ 9 days
M. Kikuchi

## Slide 8: Commissioning phase 1 (updated) (~5 months)
Machine condition
  No QCS, No solenoid (no Belle II), No beam collision
Tuning items (We assume ~1A beam current)
  Linac tuning (if necessary)
  Basic commissioning of machine (~ 1.5 month)
    Injection tuning, Hardware check and bug fix, software bug fix
  Vacuum scrubbing (>~3 months) <- important goal of Phase1
    Belle II people request enough vacuum scrubbing in this stage (before Belle II roll-in). At least one month with beam currents of 0.5 ~ 1 A.
  Detector beam background
    Study with Beast detectors, check of collimator system (two new-type collimators in LER)
      For beam background machine study, emittance control bump system should be ready to be used sometime in phase 1.
  Some optics tuning
    With day-1 optics
    Low emittance tuning w/o Belle-II solenoid
  Study of beam instability (FII, e-cloud, TMC)
    Tuning on bunch-by-bunch feedback

## Slide 9: Emittance control bump system at KEKB HER (iSize bump system)
We need to reconfigure the emittance control bump systems for both ring to be used sometime in phase 1.

## Slide 10: Phase 1 optics (HER)

## Slide 11: Vacuum scrubbing at KEKB （HER/LER）
HER
LER
HER
LER

## Slide 12
T. Ishibashi

## Slide 13: Collimators location (phase 2)
Suetsugu

## Slide 14: Vacuum pressure (LER) KEKB commissioning phase

## Slide 15: Commissioning phase 2 (~5 months)
Machine condition
  w/ QCS, w/ Belle II (w/o VXD),TOP detectors partially installed, full accelerator tuning, no physics experiment
Tuning items
  Optics tuning
    Tentative target values of IP beta’s: βx*: x4, βy*: x8
    Optics tuning with QCS and Belle II solenoid
    Low emittance tuning w/ Belle II solenoid
    Optics tuning w/ beam collision
  Detector beam background
    Study with Belle II detector, test of continuous injection (BEAST)
  Increase of beam currents (instability, RF power, vacuum issues)
    Detector background may possibly give some restriction.
    Continue upgrade for RF system (support ~70% of design beam currents)
  Beam collision tuning
    Orbit feedback (fast feedback, dithering system)
    Collision tuning w/ “Nano-Beam” scheme
  Luminosity tuning
    Tuning knobs (x-y coupling at IP etc.)
    Target luminosity: 1 x 1034 cm-2 s-1 (design of KEKB)

## Slide 16: Luminosity prospect in phase 2
Three parameters to determine the luminosity
  Beam currents
    RF system can support 70% of design currents.
    We experienced many troubles to increase the beam currents at KEKB.
  Beam-beam parameters
    Our experience is that the beam-beam parameters were increased very slowly by the many trial-and-errors most of which were unsuccessful.
    “Nano-beam scheme” is a new scheme. Maybe we will need a lots of trial-and-errors before we find effective tuning methods with this scheme.
  IP beta functions
    There is big uncertainty as to how low values of IP beta functions in phase 2.
    I think that we have to make many efforts to squeeze the beta functions by making optics corrections (not easy task).
    We may need hard time of many years until we approach the design IP beta functions.
The target luminosity in phase 2 is 1x1034 cm-2s-1.
  There is big uncertainty whether we can achieve this luminosity.
  My feeling is that exceeding the KEKB record luminosity (2.1 x1034 cm-2s-1) in phase 2 is very difficult, although it is worthwhile to challenge of course.

## Slide 17: Detuned Optics (4x8)
βx*: x4, βy*: x8, x-y coupling =2 %, ξy ~ 0.025, ILER = 1 A.
Example of machine parameters for 1034 cm-2s-1

## Slide 18: To do list for commissioning scenario
More concrete plan of each step
  We have started discussion also for damping ring
  Procedures of optics corrections in main ring and other tools related to the beam optics
  Belle II and Beast related issues
    Tools for collimator control
Operation energy in phase 2
Requirement to Belle II in phase 2
Beam operation mode from the viewpoint of radiation safety
others…

## Slide 19: Contents
Update of commissioning scenario
Operation tools
Update of dithering system for beam collision
Collaboration with other laboratories

## Slide 20: Operation tools
Commissioning group asked control group to develop operation tools
  Alarm system
    At KEKB, a member of commissioning group (K. Oide) developed the system.
  Injection control system
  Data logging system
    KBLog system (upgrade the system used at KEKB)
    CSS archiver system (backup)
  Task launcher
    SAD based system (KEKB) -> CSS based system (SuperKEKB)

## Slide 21: New Alarm system for SuperKEKB
In KEKB, we used SAD-based alarm system.
In SuperKEKB, we are going to construct the CSS-based alarm system.
CSS-based Alarm System
Used at PF-AR from 2011 fall.  operated with no problem so far
Recently installed at Linac.
(J-PARC is also considering to install the system.)
To apply the CSS-based alarm system to SuperKEKB
１） We must make sure that It stably operates under the several
10 thousands alarm data points. (~25,000 in KEKB)
 We did load tests.
２） We must develop the software tools to meet our accelerator
operation system.
M. Iwasaki

## Slide 22: CSS Alarm System
Alarm Config Tool
Alarm DB
Alarm Server
JMS (ActiveMQ)
JMS2RDB
Log DB
Alarm Client GUI
User
Operator
IOC
IOC
IOC
IOC
IOC
IOC
Channel Access
Alarm log
Alarm status
Alarm status
Alarm status
Alarm log
Write Alarm Log
XML
Definition setting file
Change the setting parameters
List of EPICS records
to be monitored
Alarm message/ Beep / etc..
Show the Current Alarm Status
Monitor EPICS records
(monitor the severity)
Alarm history
Initial setting
M. Iwasaki

## Slide 23: Test of the CSS Alarm System
Alarm Config Tool
Alarm Server
JMS2RDB
Alarm Client GUI
Software IOC
(50,000 record)
20-30 seconds
Initial setting
2.5 minutes
10-15minutes
20-30 seconds
Alarm Server
JMS2RDB
Alarm Client GUI
Software IOC
(50,000 records)
Without the initial
parameter setting
Total 13.5 to 18.5 minutes
8-10 minutes if we directly edit RDB
Total 3.5minutes
Takuya Nakamura (Mitsubishi Electric SC) and K. Asano (KIS)
Directly edit RDB
7minutes
- By generating 50,000 test records, we did CSS alarm system load test.
 Our Alarm system can stably operates.
- We also measured the start up time of the system.
20-30 seconds
2.5 minutes
20-30 seconds
 To change the alarm configuration during the operation, it takes 3-4 minutes.
Plan: We develop 1) the software IOC to take care of the records which cannot be
directly monitored , and 2) user interface tools.
M. Iwasaki

## Slide 24: Contents
Update of commissioning scenario
Operation tools
Update of dithering system for beam collision
Collaboration with other laboratories

## Slide 25: Update of dithering system for beam collision
Orbit feedback system at IP
  Vertical direction: system based on beam-beam deflection (observables: BPM orbit measurement)
  Horizontal direction: dithering system (observables: luminosity)
    For redundancy, dithering of IP vertical offset and angle can be done.
System layout
  We will start with an analog system, which is a copy of PEP-II system, due to a lack of human resources. We will upgrade to a digital system, if necessary.
  Components
    Fast luminosity monitor, lock-in amps, coils for dithering, dither circuits (drive amps, amplitude and phase adjustment), actuators (slow bump systems which is commonly used for fast vertical feedback), control system (actual feedback algorithm which will be run in an IOC), Power supplies
Collaborations
  SLAC
    Fabrications of dither coils (2013) and dither circuits (2014)
    Simulations (U. Wienands)
  LAL-Orsay
    Fast luminosity monitor

## Slide 26
Locations for the dithering coils
8 locations for the dithering coils in LER around IP.
ZDS1RP
ZDS2RP
ZDS3RP
ZDS4RP
ZDS1LP
ZDS2LP
ZDS3LP
ZDS4LP

## Slide 27
Dither coils: Fabrication and field measurement
Fabrication and measurement were done last year.
All sets of dither coils have been delivered to KEK and will be installed
in LER ring in coming spring.
U. Wienands, S.D. Anderson, MFD Metrology, SLAC

## Slide 28: Dither Circuit
An amplifier board has been being fabricated at SLAC and will be completed within this fiscal year.
U. Wienands and D.Brown SLAC

## Slide 29: Simulations on dithering system
U. Wienands (SLAC) has been doing the simulations by modifying a code used for PEP-II.
Input data for the simulations
  Orbit dependence of the luminosity (K. Ohmi)
  Information on accuracy of fast luminosity monitors (P. Bambade(LAL), S. Uehara(KEK))
  QCS vibrations in the horizontal direction (H. Yamaoka)

## Slide 30: Parameters for dither simulation
Luminosity | 1 x 1034 cm-2 s-1 |  | 1 x 1035 cm-2 s-1 |  | 8 x 1035 cm-2 s-1 | 
 | LER | HER | LER | HER | LER | HER
Ibeam [A] | 1.0 | 0.8 | 2.7 | 1.95 | 3.6 | 2.6
# of bunches | 2500 |  | 2500 |  | 2500 | 
ex/ey (nm/pm) | 2.2/44 | 5.2/104 | 3.2/51.84 | 4.6/77.28 | 3.2/8.64 | 4.6/12.88
bx*/by* (mm) | 128/2.16 | 100/2.4 | 128/1.08 | 100/1.2 | 32/0.27 | 25/0.30
sx*/sy*(mm/nm) | 16.8/308 | 22.8/500 | 20.2/237 | 21.4/305 | 10.1/48 | 10.7/59
sx*eff (mm) | 249 | 208 | 249 | 208 | 249 | 208
xx/xy | 0.0033/0.024 | 0.0013/0.0257 | 0.0083/0.049 | 0.0052/0.046 | 0.0028/0.0881 | 0.0012/0.0807
Dx (lumi:20% drop) | ~110mm |  | ~55mm |  | ~10mm | 
Lumi. meas. | 1kHz |  | 1kHz |  | 1kHz | 
accuracy | ~5 x 10-3 (w/ radiator) |  | 1.3 x 10-3(w/o radiator) |  | < 1 x 10-3 | 
sx*eff = szsinf
initial
First milestone
Design

## Slide 31
K. Ohmi
by*~300mm
Swaist:1/10 by* (~30mm)
-> Lum. Loss ~ 3.5%
Dx = Tan[2f]*Ds
Ds=30mm -> Dx = =2.5mm

## Slide 34
Results（QC1R)
Integrated amplitude (> 1Hz) ~< 0.1 mm
QC1RP and QC1RE vibrate coherently up to ~50Hz.
Simulation by H. Yamaoka
U. Wienands

## Slide 35
Results（QC1L)
Integrated amplitude (> 1Hz) ~< 0.2 mm
QC1LP and QC1LE vibrate coherently up to ~80Hz.
Simulation by H. Yamaoka
U. Wienands

## Slide 36: Orbit change at IP with 1mm offset of QCS magnets
 |  | K1 (/m) | Distancefrom IP [m] | bQ [m] max. | bIP[mm] | Dyy/2p | COD@IPfor 1mm Q-offset [mm]
QC1L (V) | LER | -1.721 | 0.920 | 2897.7 | 0.27 | 0.24995 | -0.734
 | HER | -1.206 | 1.165 | 5834.8 | 0.3 | 0.24995 | -0.768
QC1R (V) | LER | -1.712 | 0.930 | 2897.8 | 0.27 | 0.24995 | -0.736
 | HER | -1.140 | 1.172 | 5895.0 | 0.3 | 0.24995 | -0.730
QC1L (H) | LER | 1.721 | 0.920 | 153.0 | 32 | 0.24364 | 0.867
 | HER | 1.206 | 1.165 | 310.7 | 0.3 | 0.24616 | 0.901
QC1R (H) | LER | 1.712 | 0.930 | 156.9 | 32 | 0.24372 | 0.882
 | HER | 1.140 | 1.172 | 305.5 | 0.3 | 0.24619 | 0.857
COD
>
>
>
>
V:1mm (QC1 offset) <-> ~0.7mm orbit change at IP
H:1mm (QC1 offset) <-> ~0.9mm orbit change at IP
Lattice : sler_1689, sher_5769
Horizontal orbit vibration due to QC1 vibration (~ <1Hz) ~< 0.2 mm
U. Wienands

## Slide 37: Location of fast luminosity monitor
12m downstream of IP Monitor detects lost positrons
As a backup, another fast luminosity monitor will be installed in 28m downstream of HER, which detects photons from Radiative Bhabha scatterings.

## Slide 38: Proposed vacuum chamber modification for fast luminosity monitor by LAL
Kanazawa-san is considering the design for this chamber. Impedance issues have been studied by Shibata-san. The chamber is considered to install for phase 2 operation.

## Slide 39
S. Uehara

## Slide 40
S. Uehara

## Slide 41: Contents
Update of commissioning scenario
Operation tools
Update of dithering system for beam collision
Collaboration with other laboratories

## Slide 42: Collaboration with other laboratories
Japan/US Cooperation Program
  Coordinator: M. Tobiyama
TYL-FJPPL
Others
  Collaboration with NLF, IHEP, BINP…
Very important for SuperKEKB

## Slide 43: US-Japan collaboration
Collaboration with SLAC, FNAL, BNL, Cornell ...
  Draws on deep experience base of US accelerator laboratories to solve these challenging problems.
  Utilizes existing facilities and outstanding human resources of US laboratories to assist in constructing SuperKEKB accelerator components.
  Develops and tests SuperKEKB components using working accelerators.
Both KEK and US laboratories have much to gain from collaboration.
Achieve high luminosity faster!
M. Tobiyama

## Slide 44: Project overview
Development and fabrication of accelerator components important to the construction and operation of the SuperKEKB accelerator
  Collaborate with SLAC to develop
    IP collision feedback systems (4,500k JPY, to US 4,000k JPY)
    Fast luminosity monitor
    Beam collimators (7,500k JPY)
    Beam background, Machine Detector Interface
    Accelerator Physics
      Main Ring commissioning
      Damping Ring commissioning
      Linac commissioning
    BPM for Linac/BT
    X-band deflecting cavity
    Stripline kicker for high beam current
    X-ray detector
    Flux Concentrator to increase capture efficiency of positrons
    Beam energy calibration using laser Compton scattering
M. Tobiyama

## Slide 45: Project overview (cont)
R&D on accelerator technology important for the next generation of high luminosity colliders.
  Development of general purpose bunch-by-bunch feedback systems (KEK, SLAC) (3,000k JPY, to US 2,000k JPY)
  Development of bunch-by-bunch X-ray beam size monitor using coded aperture mask (KEK, Univ. Hawaii, Cornell Univ., SLAC)
    (8,900k JPY, to US 8,900k JPY)
  Development of Large Angle Beamstrahlung Monitor for collision monitoring (KEK, Wayne State U.) (1,100k JPY: to US 1,100k JPY)
  Study of electron cloud instability and its cure (KEK, SLAC, LBNL, Cornell Univ., FNAL) (5,000k JPY)
  Simulation of beam-beam interactions on various accelerators (KEK, SLAC, LBNL, Cornell Univ., FNAL) Total budget 30,000k JPY
  R&D of injector components(KEK, SLAC) Travel 4,500k + 700k JPY
Supported by US-Japan Collaboration since FY2003
M. Tobiyama

## Slide 46: Collaboration with LAL-Orsay
Framework
  Collaborative work in the framework of TYL-FJPPL (Toshiko Yuasa Laboratory, France Japan Particle Physics Laboratory)
    LAL: P. Bambade, C. Rimbault, D. E. Khechen, D.Jehanno
    KEK: S. Uehara, Y. Funakoshi, M. Iwasaki
  Budget (300kYen(KEK), ~7000€(LAL) in FY 2014)
Status
  Fast luminosity monitor system based on diamond sensor has been being developed at LAL.
  To determine the location of the monitor, beam loss simulations have been done using SAD and GEANT4.

## Slide 47: SuperKEKB-LNF collaboration
Proposal by the LNF scientists (December 2013)
  1) Feedbacks implementation (collaboration started already, Contact Person: Dr. Alessandro Drago),
  2) Optics studies, in particular the problem of the “crab waist” sextupoles (Contact Person: Dr. Maria Enrica Biagini),
  3) Lifetimes and backgrounds studies (Contact Person: Dr. Manuela Boscolo),
  4) Rings injection studies (Contact Person: Dr. Susanna Guiducci).
Status
  Things seem to have been delayed in Director General/Trustee-level communication between both labs.
  We have received official endorsement from a Trustee (Okada-san) and have begun discussing and writing a rough draft of collaboration agreement.

## Slide 48: Collaboration with Frascati
Proposal from LNF (Dec. 2013)
  Four possible collaboration topics have been propsed:
    1) Feedbacks implementation (collaboration started already, Contact Person: Dr. Alessandro Drago)
    2) Optics studies, in particular the problem of the “crab waist” sextupoles (Contact Person: Dr. Maria Enrica Biagini)
    3) Lifetimes and backgrounds studies (Contact Person: Dr. Manuela Boscolo)
    4) Rings injection studies (Contact Person: Dr. Susanna Guiducci)
Status
  Since the proposal was offered to KEK, things have been delayed in Director General/Trustee-level communication between both labs.
  Recently, we have received an official endorsement from the trustee, Okada-san, and have begun discussing and writing a rough draft of collaboration agreement.
D. Zhou in this MAC

## Slide 49: Remarks
The collaborative works with other laboratories have been very helpful for the construction of SuperKEKB.
The beam commissioning will start next year and the collaborations will be increasingly important, since SuperKEKB is very difficult machine for achieving the design performance.
Recommendations from the committee members are very important as the past recommendations.

## Slide 50
Congratulations on the 20th anniversary of
the KEKB Accelerator Review Committee!!!
The KEKB accelerator members really appreciate your pertinent recommendations that we have got a lot of benefit from and the continuous encouragements and supports.
We wish to celebrate a great success of SuperKEKB
in the 30th anniversary of the review committee!

## Slide 51: backup slides

## Slide 52
 | KEKB (e+/e-) | SuperKEKB (e+/e-)
Charge [nC] | 1/1 | 4/5
Normalized emittance[mm] | 2100/300 | 100/50 (H)
 |  | 20/20 (V)
SuperKEKB requirements (tentative)
09:50 Injector commissioning and issues 30'
Speaker: Masanori Satoh (KEK)