## Slide 1: Alignment of injector linac
KEKB Accelerator Review
24 February, 2015
Toshi Higo (Injector linac group)

## Slide 2: Contents
Initial alignment along laser line
Hard ware alignment on each girder.
Floor movement
Near future development
Conclusion

## Slide 3: Linac layout and alignment requirement
A
B
1
C
2
3
4
5
J-ARC
Rings
500m
120m
Requirement
Local s < 0.1mm
Global s < 0.3mm
  s < 0.1 mm: bge 20 mm·mrad is almost satisfied.
  s > 0.1 mm: emittance preservation is required by some methods.

## Slide 4: Alignment method
Hard ware
Reflectors for laser tracker use
Mechanical reference
Laser PD
Girder
Reference point of girder
1
2
4
3
Girder set to laser reference by PD
Support set w.r.t. mecha. reference
Hard ware aligned with mecha. reference
Hard ware alignment checked by tracker

## Slide 5: Hard wares around standard 9.6m girder
Standard unit
He-Ne Laser line
e+- beam
4-segmented silicon PD (dia.=10mm)
Acc Structure
Arm from PD
to reflector
Laser pipe
Accelerator Girder

## Slide 6: Major steps since last review
Established 500m laser straight reference line over C—5
Established reference points for DR
Installed target/FC followed by LAS with Solenoid and large-aperture Q magnets
First girder alignment done in 3—5 sectors by laser PD
Hard ware alignment on each girder done with laser tracker
Done alignment on old Q magnets with laser tracker
Done stiffening of girders, especially positron line
Completed initial alignment of 3—5 sector with laser PD
Further evaluated floor movement
Installation of heavy radiation shield on positron generation system underway

## Slide 7: Stiffening of 9m-girder
End hor. slider
Center pivot
Soft: metal plate spring

Stiff: slide roller with bolt fixing
Eigen mode frequency
Several  more than 10 Hz

## Slide 8: Positron generation and acceleration
Road cell with ball
 Jack bolt
New aluminum girders
FC
Solenoid

## Slide 9: 1. Initial girder alignment

## Slide 10: Straight laser reference line
500m laser line was stabilized by feed back.
We can routinely measure C-5 sector by laser PD system
Some developments may still be needed
  Easy sensitivity calibration and absolute zero position
  Cares against radiation damage
However, at a moment
  Because the system is most practical, we utilize it for initial alignment
  Automatic in/out devices were developed to monitor floor motion continuously

## Slide 11: 500m straight reference line by laser
Gaussian beam
Tilt feedback

## Slide 12: PD sensitivity
Fitted with Rayleigh function along 500m linac was used in the present analysis
Recent estimation from mechanical girder movement in 3—5 sector
Sensitivity varies by a factor 2 , but the center identified as zero output voltage should be OK

## Slide 13: Finished initial alignment of girders
Girders in sectors 3—5 were quickly aligned in 2011 after the earthquake.
Positron generation area was installed by the summer 2014.
Until late July 2014, C—5 sectors were aligned with leaving V-shape residual.
In late Jan. 2015, all in the 3—5 sectors were aligned straight, except for the C-band unit at 44.

## Slide 14: 3—5 alignment in Summer 2014
After alignment in summer 2014.
Big spike-like misaligned points are those to be corrected between standard girders.
C-2 sectors were aligned by laser PD, but 3-5 sectors were kept with preliminary alignment correction since earthquake.
C 1 2 3 4 5

## Slide 15: Present 500m alignment over C-5 after completion of initial alignment in late Jan. 2014

## Slide 16: Summary of girder alignment
Girder alignment can be done with the present laser PD system probably within 0.2mm in sigma.
Residual misalignment of the first initial alignment was 0.3mm in sigma, mainly comes from those aligned earlier but moved later in a year scale.
Floor moves in a big scale, especially at expansion joint, so that the swift measurement is needed, or the movement should be taken into account.

## Slide 17: 2. Hard ware alignment on girder

## Slide 18: Hard ware alignment on each girder
Accelerator structures in units at sectors 3-4-5 were corrected during summer shutdown in 2014, followed by those in sectors A-B-C-1.
Reflector base was put on the top of old Q magnets. Their alignment was measured and mostly corrected.
New Q magnets with big bore were set w.r.t. the mechanical reference on girder. Confirmation is yet to be done.

## Slide 19: Reflector setting for hard ware positioning
Mounted on coupler OD
Arm from PD to reflector
Reflectors for old Q-magnet

## Slide 20: ACC str. In unit 34 Horizontal
Before adjust
After adjust
W
E
ACC Structure
10m size

## Slide 21: ACC str. In unit 34 Vertical
Before adjust
After adjust
10m size
UP
DN
ACC Structure
Mecha. reference

## Slide 22: Hard ware alignment on a girders in sector 3—5
Horizontal
s=34mm
Vertical
s=47mm
Horizontal
Vertical

## Slide 23: Alignment error estimation w.r.t. reference straight line
Laser straightness
    Pointing stability being fedback  s~0.05mm
Girder alignment error
    Setting errors  s~0.3mm
    PD sensor setting error on holder  s~0.015mm
    Radiation damage of PD sensors  ?
PD center to girder for setting laser tracker reference
    Arm setting error  sv~0.05mm
Girder reference to hard ware setting
  Tracker confirmation of reference position  0.05mm/5m
All the above in random manner
    ~0.3mm which will be improved by more alignment times to probably 0.2mm level, unless any systematic error is left

## Slide 24: 3. Floor movement

## Slide 25: Floor moves significantly
It has been long pointed out.
Laser PD monitor over half a year showed
  Significant movement being localized at junction
  Mostly vertical (upward from summer to winter) by a few to several mm.
Following pages show the movements.

## Slide 26: Variation in half a year from July to January

## Slide 27: Floor horizontal movement in half a year from summer to winter
C3
11
18
28
38
48

## Slide 28: Floor vertical movement in half a year from summer to winter
C3
11
18
28
38
48

## Slide 29: Long-term floor movement near junction
Upward drift at junction
~0.3mm/month
Not evident but
~0.05mm/month

## Slide 30: Junction and after-pouring concrete
15cm step not well stick on the base plate
Expansion joint between two solid plates

## Slide 31: Tunnel basic structure
15cm-high after pouring concrete
40-50m deep piles
Solid base
Klystron gallery
Tunnel
Concrete shield
Base structure

## Slide 32: PD for continuous measurement
PD_28_G6DA
PD_28_REFUA
Located at
28 Expansion joint
Nov. 2014
Automatic IN/OUT

## Slide 33: Daily motion between junction
Downstream
Downstream
Upstream
Upstream
Upstream from junction
Downstream from junction
Well correlated in vertical plane
Little hor. correlation
Ver. daily Oscillation
~ 0.1mm/day
Some correlated motion

## Slide 34: Longer-term motion
Horizontal
Vertical
40 days
Horizontal
Vertical
15 days
0.1mm/1000hr/250m
A~10-5mm2/s/m
in ATL law
Exists some drift
0.1~0.15mm/mo
May not be only diffusive
Should see how it varies in a year range

## Slide 35: Estimation of floor movement some typical observed values
 | Horizontal | Vertical
Daily | 0.1 | 0.1
Week | 0.1 | 0.1
Half a year | 0.5 | 2
Speed | 0.01mm/hour | 0.01mm/hour
Unit mm
We should study/develop the linac system
with these values in mind.

## Slide 36: Trial to understand the expansion joint
Beam
West wall
East wall
Down
Notrth
Up
South
Junction

## Slide 37: Junction relative movement at 28 19 Sep. 2014 – 31 Jan. 2015
Up
North (beam)
East
↑ Up, East, North(beam line)
↓ Down, West, South
14 Sep.
23 Nov.
1 Feb.
Air cond. restart
Water flood due to typhoon
0.4
0.3
0.2
0.1
0.0
-0.1
-0.2
Linac stop
Found daily movement, month-long drift, climate effect, etc. These are related to those observed in laser PD long-term result.

## Slide 38: 4. Near future developments

## Slide 39: We should study and develop cures against floor movement
Near future for Phase-I
  Make quantitative analysis at more places and more in systematic manner
  Try to monitor movement with beam
  May study other monitor methods, such as HLS
Development for phase-II and -III
  Beam steering by targeting golden orbit
  Movers, at least locally
  Sophisticated compensation such as offset injection

## Slide 40: Possible time frame in mind

## Slide 41: Concluding remarks on alignment
Girder stiffening done.
Most of the hard wares set in the beam line, except for pulse-Q.
Initial girder alignment done with the residual ~0.3mm in sigma over 500m line.
Hard wares alignment on each girder improved to be 0.05mm in sigma.
Local smoothness will be improved by laser tracker.
Floor moves a few mm in half a year, mostly at expansion joint, while the daily motion ~0.1mm.
Floor movements should be evaluated at more points and with beam study to develop a practical cure method.