## Slide 1: Injector Commissioning
Masanori Satoh
(Accelerator Laboratory, KEK)
for the Injector Linac Commissioning Group
The 20th KEKB Accelerator Review Committee, Feb. 23-25, 2015

## Slide 2: Contents
Injector upgrade overview
Energy spread/low emittance preservation
Simultaneous top-up for 4-rings
Progress of injector commissioning
Issues
Summary and plan

## Slide 3: Injector upgrade overview
Low emittance photo-cathode rf gun
  e-: 1 nC, 100 mmmrad (KEKB) => 5 nC, 20(H)/50(V) mmmrad (SuperKEKB)
  e+: 1 nC, 2100 mmmrad (KEKB)=> 4 nC, 20(H)/100(V) mmmrad (SuperKEKB)
  Component alignment and fine beam control for low emittance preservation
New positron capture system (Flux concentrator, Large aperture S-band structure), and damping ring
New timing system (bucket selection for DR/MR)
Fast RF monitor, high precision BPM readout and other new subsystems
Simultaneous top-up injection
Main ring commissioning Phase-I: Jan. of 2016
  e-/e+ 1nC w/o low emittance

## Slide 4: Energy profiles and beam properties
low emittance
RF gun
A
B
C
1
2
3
4
5
1.5 GeV e-
e+ target
e-:Chicane
10 nC x 2 bunches x 50 Hz (SuperKEKB e+)
5 (1) nC x 2 bunches x 50 Hz (SuperKEKB e-)
5 nC (0.3) x 1 bunch x 5 (25) Hz (PF-AR)
0.3 nC x 1 bunch x 25 Hz (PF)
1.1 GeV
DR
Decelerate
e+ target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.219 GeV
1.5 GeV
same energy
e-/e+ beams are delivered to 4-rings with different bunch charge and energy.
Beam acceleration modes must be switched by 50 Hz pulse-by-pulse for top-up injection.
HER: 7 GeV e-
PF-AR: 6.5 GeV e-
PF: 2.5 GeV e-
LER: 2.5 GeV e+
5 nC x2
5 nC x1
0.3 nC x1
4 nC x2
Pulsed Quad (Doublet) for pulse-by-pulse switching
Compatible settings for e-/e+ beams (DC Quads)

## Slide 5: Energy spread requirement
Energy spread should be less than 0.1%.
Uniform beam distribution is necessary for mitigation longitudinal wakefield and reduce energy spread.
Temporal manipulation of laser system
0.1%
Gaussian
Uniform

## Slide 6: Emittance growth due to component misalignment
Sector Cto5: -10 deg rf phase R56 =-0.20
Simulation results from 100 different seeds.
Misalignment of Quadrupole magnets and Accelerating structure:
  s < 0.1 mm: bge 20 mm·mrad is almost satisfied.
  s > 0.1 mm: emittance preservation is required by some methods.
20 mm·mrad
<Emittance growth>
・quadratic curve as a function of misalignment
・final emittance depends on error seed
Norm. projected rms emittance (mmmrad)
Misalignment s (mm)
Simulation
SAD code, Elegant
Initial bunch charge: 5 nC
Initial emittance: 6 mmmrad
Initial bunch length: 10 ps (FWHM)
Initial energy spread : 0.4%
Initial beam energy: 20 MeV
Uniform longitudinal beam distribution

## Slide 7: Offset injection for emittance preservation
Low emittance e- beam transport w/o damping ring
Emittance preservation is key issue for e- beam.
Offset injection: intentional change of misalignment seed.
Control the steering magnet at the beginning of Sector C
Bunch compression
Offset injection

## Slide 8: Offset injection (simulation)
Sector Cto5: -10 deg rf phase R56 =-0.20
Kick angle is relatively small.
Need a high-precision and stable orbit control.

## Slide 9: Emittance w/ bunch charge fluctuation
Emittance simulation w/ 10 misalignment seeds (accelerating structure).
SectorC to Sector5 (Linac end)
Assuming 5 nC, initial emittance of 10 mmmrad (SectorC)
When bunch charge increases by 10%, emittance increases by 6.5%.
Try simulations w/ measured component misalignment, dynamic beam line movement, energy jitter.
5 nC => 5.5 nC
12.4 => 13.2 mmmrad

## Slide 10
BPM readout system
Current system:
  Windows-based digital oscilloscope
    10 GSa/s, 8 bit, 1 GHz bandwidth, 4 channels
    Twenty four systems process: 90 BPMs
    Position measurement precision: 25～50 mm (3-BPM)
New system:
  VME module w/ band-pass sampling scheme
    250 MSa/s, 16 bit ADC,
    BPF (fc: 180 MHz, BW: 60 MHz, 22 MHz)
    Signal can be well damped within 80 ns
  Meas. precision: 3 mm
  ~ 100 modules under pre-delivery inspection
80 ns

## Slide 11: e-/e+ beam fast switching (SuperKEKB)
Positron production target with a hole (e- beam pass through inside a hole)
A hole is at the center of beam line for low emittance e- beam.
Same scheme was successful in KEKB operation.

## Slide 12: Simultaneous top-up injection for three rings
Stored beam current stability in 2000. - KEKB: 300 mA (~ 50%)
- PF: 240 mA (~ 53%)
Stored beam current stability in Apr. 2010. - KEKB: 1 mA (~ 0.05%) : e-: 12.5 Hz, e+: 25 Hz
- PF: 0.05 mA (~ 0.01%) : 0.5 Hz
KEKB e-
KEKB e+
Luminosity
PF
PF-AR injection (twice daily) interrupt KEKB injection.
Big issue for SuperKEKB operation.
Beam lifetime ~ 6 min.

## Slide 13: Simultaneous top-up including PF-AR injection
PF-AR and KEKB share the long part of beam transport line.
Existing tunnel space is very tight.
New tunnel has been constructed in Mar. of 2014.
Pulsed bend will be installed at #3 switch yard of Linac.
New BT will be available in Jan. of 2017.
H. Takaki (KEKB review 2013)

## Slide 14: Injector commissioning
Injector commissioning has been started in Oct. of 2013.
  Oct. and Dec. of 2013 (e+ beam line construction in Nov.)
  Apr. ~ Jun. of 2014
  Oct. ~ Dec. of 2014
  Commissioning (Jan.-Mar. of 2015) was canceled. (operation budget)
  Day shift: beam line construction, laser tuning
  Evening shift: beam study
  Early morning shift: beam study, rf conditioning

## Slide 15: Charge history
0.75 nC
5.6 nC

## Slide 16: Bunch charge from rf gun in last Dec.
1 week

## Slide 17: Beam orbit example
x (mm)
y (mm)
I (nC)
During commissioning, 3T gun continuously provides e- beam for PF ring (top-up).
Full Linac study can be conducted in Wednesday.
PF dedicated magnet settings are used in Sector3 - Sector5
RF F can switched in pulse-by-pulse (LLRF F control)
3T gun
A1 rf gun

## Slide 18: Typical beam charge stability
1 hour
sI: 10% ~ 20%
~ 2.5% (KEKB operation)

## Slide 19: Bunch charge and laser power
Laser power (Arb. Units)
Bunch charge (nC)
Bunch charge (1st BPM) as a function of laser power.
Clear correlation between them

## Slide 20: Bunch charge fluctuation
Bunch charge fluctuation as a function of bunch charge (2D histogram)
Oct. of 2013 – Dec. of 2014
Requirement for Phase-I

## Slide 21: Beam diagnostics
Beam position measurement
  BPMs x 90 (strip-line type electrodes)
Beam profile/Emittance measurement
  Fluorescent screen monitors x100
  Single wire scanner x1
  Multiple wire scanner x5
Bunch length measurement
  Streak camera x3

## Slide 22: Emittance measurement
Emittance as function of bunch charge (drop the results w/ large error )
Small bunch charge (< 1 nC) shows good emittance at injector section.
  < 10 mmmrad (Vertical), < 15 mmmrad (Horizontal)
Results at SectorB show larger emittance than our goal.
20

## Slide 23: Offset Injection (experiment)
Feasibility of offset injection was studied w/ bunch charge of 0.3 nC.
Changing the excitation current of steering magnet at Unit-A4.
Emittance was measured multiple wire scanner at SectorB end.
We will conduct this measurement w/ various bunch charges.

## Slide 24: Bunch compression at Unit-A1
A1 RF F 0°: 30 ps
w/o bunch compression
30 ps
Chicane
Laser length
30 ps
A1 RF F -30°: 10 ps
w/ bunch compression
10 ps

## Slide 25: Bunch compression @ J-ARC
Isochronous (w/o bunch compression), R56 = -0.3 m (w/ bunch compression) w/ different RF F in SectorA/B
Clear bunch compression has not yet been measured.
Emittance measurement by multiple wire scanner at Sector2 w/ and w/o J-ARC bunch compression.
Streak camera at SectorC

## Slide 26: e+ beam measurement
First e+ beam was measured by current system at Jun. 9th 2014.
Primary e- beam charge: 0.5 nC
e+ charge: 0.02 nC @ SP_28_4
e- beam
e+ beam
x (mm)
y (mm)
I (nC)
target

## Slide 27: R16, R36 elements at J-ARC
Design value
w/ fudge factors
R16, R36 values were measured at J-ARC and SectorC.
w/ and w/o fudge factors (B’ = Afudge x B’model )
Find suitable fudge factors
  Typical fudge factors used for KEKB operation are 1% ~ 5%.

## Slide 28: Beam loss at first acc. structure
Beam transmission rate is reduced at 2nd BPM (downstream 1st accelerating structure) when bunch charge from gun increases.
To improve it, 1st accelerating structure will be removed soon.
x (mm)
y (mm)
I (nC)
1 (nC)
4 (nC)

## Slide 29: Timing system
J-ARC
e+ Target
e– BT (PF: 2.5GeV, 0.2nC)
EVRs
Cont-1
KL_51/52
SB_5
SB_4
SB_3
Cont-5
Cont-4
Cont-3
Cont-2
SB_2
KL_B5/B6
SB_A
SB_B
Cont-ABC
SB_1
SB_C
SH_A1
Injection
e– BT (PF-AR: 6.5GeV, 5nC)
e− Gun
EVG
e+ BT (SuperKEKB: 4GeV, 4nC)
e– BT (SuperKEKB: 7GeV, 5nC)
Main timing station
Event generator (EVG)/Event receiver (EVR) based on VME64x. (Micro-Research Finland)
EVG (EVG-230) x1, EVR (EVR-230RF) x24
Arbitrary injection pattern can be set via HLA.

## Slide 30: New timing system configuration
J-ARC
e+ Target
e– BT (PF: 2.5GeV, 0.2nC)
EVRs
Cont-1
KL_51/52
SB_5
SB_4
SB_3
Cont-5
Cont-4
Cont-3
Cont-2
SB_2
KL_B5/B6
SB_A
SB_B
Cont-ABC
SB_1
SB_C
SH_A1
Injection
e– BT (PF-AR: 6.5GeV, 5nC)
e− Gun
EVG#2
EVG#3
e+ BT (SuperKEKB: 4GeV, 4nC)
e– BT (SuperKEKB: 7GeV, 5nC)
EVR
TTL
TTL
Event signal (optical fiber)
Main Rings
Damping Ring
EVG#1
Main timing station
PF
PF-AR
EVG
EVR
Bucket selection: MR, DR
# of EVG: 1 => 3
CPU: MVME5500 => MVME6100
RTOS: VxWorks5.5 => 6.8
Firmware updated

## Slide 31: Beam injection study (new timing system configuration)
Beam orbit for PF injection (new system)
Beam orbit for PF injection (current system)
PF/PF-AR injection study were conducted w/ new EVG configuration and software.
Beam orbit and injection rate is quite similar between current and new system configuration.
Wire scanner/BPM works well.
Long-term stability will be tested after this Apr.

## Slide 32: Unit A1 (reconfiguration)
Thermionic e- gun will be temporarily back in end of this Apr. (for radiation control license and e+ primary e- generation of 10 nC)
  Keep the beam line for rf gun in current position.
  Beam line level of beam line will be changed from 1200 mm to 1950 mm.
  Spare magnets will be used for new beam line.
Thermionic e- gun commissioning will be started in early May.
RF e- gun beam line
Thermionic e- gun
1950 mm
1200 mm
Merger line

## Slide 33: Optics design
Quadrupole triplets will be installed in merger line.
Beam size is not so large in comparison with bore radius of vacuum chamber .
(mm)
Ver. beam size (mm)
Hor. beam size (mm)
Beam energy (MeV)
Merger line

## Slide 34: Issues
Injector commissioning
  Oct. and Dec. of 2013/ Apr. ~ Jun. of 2014/ Oct. ~ Dec. of 2014
  Not enough time for commissioning
  e+ commissioning:
    Installation of flux concentrator delayed from Dec. of 2013 to May of 2014.
    Twice accidents in Dec. of 2013 and Dec. 2014 (cable burned)
    First e+ beam was measured in Jun. of 2014.
    Progress of LAS rf conditioning is slow.
    Not enough primary e- bunch charge at target ( 1 nC)
  e- commissioning:
    Discharge of rf gun cavity. Not enough power for rf gun cavity (12 MW/20 MW)
    Shot-by-shot beam stability of charge and position/angle from gun is not yet enough. Difficulty to keep the high bunch charge in long term period.
    Beam loss at Unit-A1 (chicane) and J-ARC

## Slide 35: Summary and Plan
Beam commissioning w/ A1 rf gun started in Oct. of 2013.
  Not enough time for commissioning
  5.6 nC (from rf gun), 0.75 nC (Linac end)
  Stability is still issue. (Shot-by-shot and long term)
Unit-A1 reconfiguration will be completed before end of Apr. Thermionic e- gun commissioning in May.
Beam commissioning w/ thermionic e- gun (May, June)
  Measure Quadrupole center to BPM center offset
  Reduce beam loss at Unit-A1/J-ARC
  Development of commissioning tools and tests (beam based alignment/emittance preservation)
  Pulsed Quads (x2) and steering (x2) will be tested in Sector2.
Prepare stable e-/e+ beams (1 nC w/o low emittance) before MR commissioning Phase-I.

## Slide 36: backup

## Slide 37: e- beam parameters
 | SuperKEKB | KEKB
Energy (GeV) | 7.0 | 8.0
HER stored current (A) | 2.6 | 1.1
HER beam lifetime (min.) | 6 | 200
Maximum beam repetition (Hz) | 50 | 50
Max. # of bunch in an rf pulse | 2 | 2
Emittance (mmmrad) | 50/20 (Hor./Ver.) | 100
Charge (nC) | 5 | 1
Energy spread (%) | 0.1 | 0.05
Bunch length sz (mm) | 1.3 | 1.3
Damping ring | - | -
Simultaneous top-up injection | 4 rings (SuperKEKB e-/e+, PF, PF-AR) | 3 rings (KEKB e-/e+, PF)

## Slide 38: e+ beam parameters
 | SuperKEKB | KEKB
Energy (GeV) | 4 | 3.5
LER stored current (A) | 3.6 | 1.6
LER beam lifetime (min.) | 6 | 133
Maximum beam repetition (Hz) | 50 | 50
Max. # of bunch in an rf pulse | 2 | 2
Emittance (mmmrad) | 100/20 (Hor./Ver.) | 2100
Charge (nC) | 4 | 1
Energy spread (%) | 0.07 | 0.125
Bunch length sz (mm) | 0.7 | 2.6
Damping ring | 〇 | -
Simultaneous top-up injection | 4 rings (SuperKEKB e-/e+, PF, PF-AR) | 3 rings (KEKB e-/e+, PF)

## Slide 39: Design drawing of A1 beam line

## Slide 40: Shot-by-shot beam profile stability

## Slide 41: Beam position stability @ SP_A1_C5
Measured beam position at first BPM (SP_A1_C5)
  sx ~ 0.57 mm
  sy ~ 0.11 mm
Fluctuation of horizontal beam position is larger than vertical one.
30 min.

## Slide 42: Emittance measurement example (Unit-A1)
Quadrupole scan
Screen monitor at chicane
Horizontal
bgenx: 15.43 mm·mrad
Vertical
bgeny: 9.42 mm·mrad
Chicane

## Slide 43: Emittance measurement example (Sector B)
Multiple wire scanner at the end of Sector B
Typical result (1 nC):
  en,x: 66.006 ± 10.755 mmmrad
  en,y: 77.309 ± 14.522 mmmrad
Charge stability is not so small. Software is under development for subtracting shot-by-shot beam fluctuation.

## Slide 44: Emittance measurement
Emittance of rf gun and SectorB were measured by Quad scan and multiple wire scanner, respectively.
Results measured in Nov. and Dec. of 2014.
Vertical emittance is smaller than horizontal one.

## Slide 45: Two bunch operation example
1st bunch charge
2nd bunch charge

## Slide 46: Profile monitor
Screen material is made of 99.5% Al2O3 and 0.5% CrO3 (AF995R, Demarquest Co.). (t: 1 mm)
Linux/PLC (x31) control profile monitor (insert/remove, video signal select, limit switch, LED illumination, pneumatic air pressure).
EPICS IOC is running on Linux/PLC. HLA is implemented by Python.
Controller and HLA
Beam profile
Monitor and CCD camera

## Slide 47: Profile monitor (cont’d)
7/97 were replaced by 30-mm-thick one for precise beam size/emittance measurement (Quadrupole scan).
CCD cameras have been replaced by new one.
  Allied Vision: GC650 w/ GbE
  Ext. trigger input
  EPICS IOC, CSS for HLA

## Slide 48: Energy spread measurement @ J-ARC
Measure beam energy spread by screen monitor (middle of J-ARC) w/ and w/o bunch compression at A1 chicane.
Bunch compression at A1 unit is effective for energy spread compensation.
A1 chicane On
(w/o bunch compression)
A1 chicane Off
(w/ bunch compression)

## Slide 49: Summary of e- commissioning
Item | Requirement | Current status
Beam charge (nC) | 5 (10 for e+ primary) | 5.6 (first BPM) 0.58 (Linac end)
Beam energy (GeV) | 7 | 7
Normalized emittance (mmmrad) | 50/20 (Hor./Ver.) (at the end of Linac) | 20/7 (Hor./Ver.) (from RF gun)
Bunch charge stability | 2.5% (KEKB), 1% (PF/PF-AR) | 10% ~ 20%
Bunch compression (Unit-A1) | 30 ps => 10 ps | 30 ps => 10 ps
Bunch compression (J-ARC) | 10 ps => 5 ps | n/a
Temporal manipulation of laser | Uniform shape | n/a
Emittance preservation | 20 mmmrad (Linac end) | n/a
Max. beam repetition | 50 | 25
# of bunches | 2 | 2
Operation | Simultaneous top-up | n/a