## Slide 1
Tetsuo ABE
For SuperKEKB-RF / ARES-Cavity Group
(T. Abe, T. Kageyama, H. Sakai, Y. Takeuchi, and K. Yoshino)
The 21th KEKB Accelerator Review Committee Meeting
2016-06-13
MR: Main Ring
DR: Damping Ring
Normal-Conducting RF Cavities for SuperKEKB / MR & DR

## Slide 2: Contents
RF cavities for the Main Rings (MRs) (“ARES”)
  Introduction
  Operational status in Phase 1
  Two serious troubles
RF Cavities for the Damping Ring (DR) (“DR Cavity”)
  Introduction
  Results of the performance tests

## Slide 3: ARES for the MRs

## Slide 4: NC RF Cavity System for SuperKEKB (ARES) (Accelerator Resonantly coupled with Energy Storage) -- Three cavity system stabilized with the accelerating p/2 mode --
High-Purity Copper Resonators
Gap length: 256 mm
Three-cavity system (unique)
Rsh/Q0=15 Ohms
Q0=~1.1x105
Vc=0.5 MV/cav
Pc=150kW (60kW in AC, 90kW in SC)
Loss factor: 0.48 V/pC (bunch length: 5 mm)
Esp/Eacc = 3.8
(Cavity trip rate) < 1 /cav/3months
Us/Ua=9 (explained in the next page)
High energy (Us) stored as a low-loss mode (TE013)

## Slide 5: Three Main Characteristics of the ARES Cavity System
Large Storage Cavity (SC)
  Optimum detuning suppressed by Us/Ua(=9)
    SC acts as an electromagnetic flywheel.
    Dfp/2 = Dfa / (1 + Us/Ua) = Dfa /10 < frev
      Dfa = -200kHz (KEKB design), -280kHz (SuperKEKB design)
      frev = 99kHz
    Therefore, coupled bunch instabilities (CBIs) driven by the accelerating mode are suppressed (Appendix A).
p/2-mode operation
  Stable against the detuning and deformation
  The stored-energy ratio: Us/Ua changeable
    Us/Ua = ka2/ ks2
  Parasitic 0 and p modes
    Damped selectively out of CC by an antenna-type damper (“Coupling-Cavity Damper”)
    Have a almost symmetric impedance w.r.t. fRF
Hybrid HOM-Damped Structure
  Explained in the next page
SC : Storage Cavity
CC : Coupling Cavity
AC : Accelerating Cavity

## Slide 6: The ARES has -- Two-types of HOM-Damped Structures. --
Type_1: HOM WG (HWG)
Type_2: Grooved Beam Pipe (GBP)
beam
Bullet-shaped SiC ceramics
Directly water-cooled
HOM absorber
For damping
Monopole HOMs
Vertically-polarized dipole modes
SiC ceramics tiles
Indirectly water-cooled
HOM absorber
T. Kageyama, “Grooved Beam Pipe for Damping Dipole Modes in RF Cavities," KEK-PREPRINT- 91-133, 1991.
For damping
Horizontally-polarized dipole modes
Note:
No HWG in the horizontal direction due to the (H)CC
To suppress CBIs driven by HOMs (Appendix A)

## Slide 7: Type_2: Grooved Beam Pipe (GBP)
Electric-field Vectors
TM110
TE mode in the
Grooved Beam Pipe

## Slide 8: Upgrade of the ARES for SuperKEKB
(Selection)

## Slide 9
(Shown by T. Kageyama at KEKB Review 2011)
SuperKEKB Phase 1
KEKB
NKlys:NCav=1:2
NKlys:NCav=1:1
Relocation: HER  LER

## Slide 10
3D Transparent View of ARES Cavity System
Input Coupler
High-Power Input Coupler / Performance Upgrade
Fine grooving inside the outer conductor of the coaxial line to suppress multipactoring discharge.
2. The coupling loop is extended to increase the input coupling factor (up to b = 6).
The optimum input coupling factor βopt is given by βopt = 1 + Pbeam/Pc .
Power Handling Capability (Spec.)
Pinput Pc Pbeam
SuperKEKB : 750 kW = 150 kW + 600 kW
KEKB : 350 kW = 150 kW + 200 kW
Pc = 150 kW generating Vc = 0.5 MV per ARES cavity.
T. Kageyama
(T. Kageyama, et al., Proc. of PASJ, TUPS126, 2011)
(Appendix B)

## Slide 11: Upgraded Input Coupler Increasing the Input Coupling Factor
Input couplers with increased input coupling (bmax = 56) needed for the stations with the Nklys:Ncav=1:1 configuration to accelerate beams with the design current.
Used at the KEKB/MRs
With increased input coupling for the SuperKEKB
The high-power performance was demonstrated both at the test stand and in the KEKB operation.
Pinput = 740 kW (= Pc: 130kW + Pbeam: 610 kW)

## Slide 12
High Power Test Stand
ARES Cavity System / Upgraded Input Coupler / Production & Processing
ARES
Storage Cavity
Input Coupler
Under Test
Input Coupler
used as
Output Coupler
RF Power from
1MW CW Klystron
(TOSHIBA E3786)
To 1MW Water Load
Snapshot of Status Monitor for RF Processing
For the first two production couplers, stable power feeding was demonstrated
  Up to Pinput = 800 kW (= 750 kW + 50 kW) at the test stand.
So far, 13 couplers have been processed up to 750-800 kW.
  The same shown in the last report
As of June, 2016, 5 couplers are waiting for high power test.
  Pinput = 850 kW (= 750 kW + 100 kW) to be demonstrated (after Phase 1)
(Photo and diagram by T. Kageyama)
  (Max. RF power stably supplied by the high power source)

## Slide 13
Almost no vacuum break before T=0
All the Input couplers for NKlys:NCav=1:1 stations in OHO D4&D5 have been replaced by upgraded couplers.
One coupler has been replaced by an upgraded one for one of the FUJI D8 stations.
For other NKlys:NCav=1:1 stations, to be replaced before starting Phase 2.

## Slide 14: Two ARES Cavities Newly Installed in OHO D4-E,F
Pressure-sensitive paper 
to check the RF contact
between CC and SC

## Slide 15: Crack found on the welding lip of the D4-F Cavity
Sealed with a O-ring (non-metal)
The vacuum pressure in this cavity is one order of magnitude higher than others.
 Vacuum sealing impossible with lip welding
To be fixed after Phase 1

## Slide 16: Monitoring ALL the Cavities with TV Cameras
TV camera attached in the opposite side of the input coupler
During the KEKB operation, only some cavities were monitored.
For SuperKEKB, all the cavities are to be monitored and recorded.
(Top View)
TV Camera (NTSC)
Input Coupler
beam

## Slide 18: Example of the Recorded Videos
Useful for isolating problems caused by input couplers
(Note: Input couplers are removable.)
(Top View)
D5-B cavity
Vacuum interlock activated with RF input power of 60 kW during the RF conditioning.
Input Coupler
TV Camera
beam

## Slide 19: Operational Status of the ARES in Phase1

## Slide 20: Operation Summary in Phase 1
Two serious troubles
Successful operation except for

## Slide 21: Vacuum Trouble of the D8-D Cavity
Vacuum-pressure behavior for the ARES D8-D cavity,
plotted together with the RF input power.
RF Input Power [kW]
Vacuum CCG [V]
(T. Kageyama)

## Slide 22: Vacuum Trouble of the D8-D Cavity
The ARES cavity D8-D at the FUJI RF section for LER could not be operated due to abnormal vacuum pressure rise, sometimes observed other than during the RF operation.
The gas source may be some subsurface defects, possibly between the copper plating layer and the carbon steel structure of the storage cavity.
Now detuned  out of operation
Plans toward Phase 2:
  Plan A: hopefully locate and remove the defects in situ, followed by high power testing for confirmation.
  Plan B: replace this ARES cavity by a spare one.
(Original version by T. Kageyama)
<Notes>
Successful operation at KEKB
No vacuum break since KEKB

## Slide 23: Other Serious Trouble: Chillers for RF Windows
Object to be cooled: RF Ceramic Windows
Coolant: water + antirust(5%), pH: 6 to 7 %
Coolant pressure: 0.2 to 0.3 MPa ( < 0.4 MPa)
Put in the sub-tunnel (not seen from the beam)
No trouble related to the chillers used at KEKB
RF
RF Ceramic
Window
Cooling
Channel
Coupling-Cavity Damper
(Solid Model by K. Yoshino)
RF Ceramic
Window
Input Coupler
Cooling
Channel
We have replaced all the 15 chillers used at KEKB for a long time.
(Further details on the chillers are
described in Appendix C.)

## Slide 24: During Phase 1 Operation
We observed precipitates growing in the coolant.
  Especially in the FUJI D8 stations
  Triggered LER beam aborts at D8-B (3 times)
    The flow rate of the coolant decreased with precipitates.
  Principal component : para tertiary butyl benzoic acid
    Widely used as antirust
Temporary treatment
  Cleaning the filers
  Replacement of the coolant by new one
Measures toward Phase 2
  Understanding of the chemical process of the precipitate creation (on-going)
    Including basic test (beaker test)
  Sealing the reservoir tanks against the (activated) air in the tunnel
    From the basic test (beaker test) with H2O+antirust(5%)+Cu+Mo
      Precipitates created in the beaker open to the air
      No precipitates created in the beaker sealed against the air
  Monitoring of pH of the coolant during operation
Example of the filters with huge amount of precipitates
Example of the filters with small amount of precipitates

## Slide 25: pH and Water Solubility
Chart: pH of the coolant in each chiller (measured on June 2, 2016)
| D4-A | D4-C | D4-E,F | D4-G,H | D5-A,B | D5-C,D | D5-E,F | D7-A | D7-B | D7-C,D | D7-E | D8-A | D8-B | D8-C,D | D8-E
PH | 6 | 6.3 | 6.1 | 6.1 | 6 | 6 | 6.1 | 6.6 | 6.6 | 6.7 | 7.2 | 6.4 | 5.9 | 6.1 | 6.2
Water solubility of the antirust
- 12600 mg/L at 20degC (pH7)
- 47.1 mg/L at 20degC (pH4.3)
(K. Yoshino)

## Slide 26: RF Cavities for the DR (“DR Cavities”)

## Slide 27: NC RF Accelerating Structure for the DR
RF operating frequency: 508.9 MHz
  Same as that of the MRs
Based on the HOM-damped structure of the successful ARES cavity system
Three cavities at max. to be installed in a limited space originally designed for one cavity (3.8 m in the beam direction, excluding the taper sections)
  Total Vc = 2.4 MV at max. with 0.8 MV/cavity
Apart from the CC and SC of the ARES, this DR cavity has the following space saving features that are not included in the ARES:
  The HOM absorbers are all compact tile-shaped SiC ceramics;
  The neighboring cavities share a GBP in-between; and
  The cavity is connected directly to GBPs with lip welding for vacuum sealing at the outer periphery (“weld ring gasket”).
“Multi Single Cell” structure
  Coupling of the Accel. mode and HOMs among the cavities significantly suppressed by the HOM absorbers on the GBPs
  One big mechanical structure with solid connections of the components
Loss factor of this structure: 2.3 V/pC (bunch length: 6.0mm)
Vacuum pumps directly attached to each cavity
In the DR tunnel, we will assemble the cavities separating them with GBPs similar to LEGO blocks.
The blue, gray, green, and magenta regions indicate a vacuum, HOM absorbers, coaxial lines of input couplers, and plungers of movable tuners, respectively.
The colored arrows indicate the direction of the positron beam.
NC : Normal-Conducting
HOM: Higher Order Mode
MR: Main Ring
DR : Damping Ring
CC: Coupling Cavity
SC: Storage Cavity
GBP: Grooved Beam Pipe
1225
1225

## Slide 28: Main Characteristics of the DR Cavity
3 cavities (max) in a limited space (3.8 m) originally designed for one cavity
  Required Total Vc = 0.26 MV (until 2010)  1.4 MV (from 2011)
  Three cavities with 0.7 MV/cav ( tot. 2.1 MV) in operation
  Up-down separation of the HOM waveguides
  The neighboring cavities share a Grooved Beam Pipe in-between.
  The cavity is connected directly to Grooved Beam Pipes with lip welding for vacuum sealing at the outer periphery (weld ring gasket)
  Compact HOM absorbers (SiC tiles)
Complete HOM-damped structure
  Based on the ARES cavity system
  CBIs suppressed (Appendix D)

## Slide 29: Components of the RF Structure except for the cavity
One Set of six SiC ceramic tiles
GBP
Solid connection between the cavity and GBP
HOM WG Load

## Slide 30: RF Cavity for the DR (DR Cavity)
Design Parameters
HOM Waveguide Load with SiC Tiles Inside
Grooved Beam Pipes
with SiC Tiles Inside
Turbo-Molecular Pump
Sputter Ion Pump

## Slide 31: History of the DR Cavity Development
No.2
No.1
No difference between No.1 and No.2 in the:
Electric design
Mechanical structure, and
Fabrication method
0. Cavity No.0 (prototype) developed in JFY2011
  Surface protection of the endplates: acid cleaning followed by chromating
1. Cavity No.1 fabricated in JFY2012
  Surface protection of the endplates: Electropolishing (EP)
2. Cavity No.2 fabricated in JFY2013
  Surface protection of the endplates: Electropolishing (EP)
(3. Cavity No.3 to be fabricated in JFY2017?)

## Slide 32: Vc = 0.95 MV/cav demonstrated at the Test Stand
Pin (Prefl) : input power to (reflected power from) the cavity
Wall-loss power: Pwall = Pin – Prefl = ~0.99 x Pin
Cavity No.2 reached 0.95MV/cav successfully.
(> 0.7 MV/cav required for DR operation)
Vc [MV/cav] | Wall-Loss Power [kW] | Total Holding Time [hours] | Number of Cavity Trips
0.80 | 144 | 30.5 | 1
0.85 | 164 | 18 | 0
0.90 | 186 | 14.5 | 3
0.95 | 210 | 8 | 1
During the stability test after the RF conditioning
Cavity No.1
Cavity No.2
During the RF conditioning

## Slide 33: Configuration in the DR Tunnel
At the beginning of the DR commissioning
Total Vc = 1.4 MV
Ultimate
If we need this,
depending on results of the DR commissioning and the budget.p
Total Vc = 2.1 MV
Dummy duct
Cavity No.3

## Slide 34: What We Learnt from the R&D of the DR Cavities
Electro-polishing (EP) for the end plates gives significant improvement in:
  Q0
  Field emission during RF conditioning
Same performance between DR Cavity No.1 and No.2 in:
  Q0
  Field emission
  RF conditioning speed
  Vacuum performance
  High-gradient performance:
Significant Findings directly related to cavity breakdown
(Note: No EP applied to the barrel part.)
Breakdown Rate at Vc=0.90 MV/cav (after RF conditioning)
Cavity No.1: 5.0+4.8-2.7 /24hrs
Cavity No.2: 3.3+1.3-1.0 /24hrs

## Slide 35: 1. Improvements with the EP
 | Q0(meas) / Q0(sim)
Prototype | 92.9%IACS
Cavity No.1 | 97.1%IACS
Cavity No.2 | 97.3%IACS
= Indirect observation of the dark current:
Field emission
Acceleration
Impact on the inner surface
Emission of X-ray

## Slide 36: 3. Significant Findings directly related to cavity breakdown
by the direct in-situ observation of the inside of DR Cavity No.2
using 3 TV cameras for Multi-directional and wide-field observation during the high-gradient test
All of the cavity-breakdown events recorded in storage media automatically
(5 seconds before, until 1 second after the moment of the breakdown)

## Slide 37: Significant Finding (1)
60% of the cavity breakdown events are accompanied with a spot-type explosion
without any other significant phenomena.
Example of the spot-type explosion 
at the moment of the breakdown
(Vc = 0.56 MV/cav)
Frame Number
Intensity in the
green-square region

## Slide 38: Significant Finding (2)
20% of the cavity breakdown events are accompanied with an explosion and disappearance of a stable bright spot
without any other significant phenomena.
Mini-Supernova
Frame Number
Intensity in the
green-square region
Example of the bright-spot explosion 
at the moment of the breakdown
(Vc = 0.95 MV/cav)
 This bright spot disappeared

## Slide 39: Pyrotechnical phenomena are minority!
A few % of the cavity breakdown events
Flash
Lightning
For more details T. Abe et al., “Breakdown study based on the direct in-situ observation of inner surfaces of an RF accelerating cavity during a high-gradient test”, submitted to PRAB.
(Preprint: KEK-Preprint_2015-25 )

## Slide 40: Summary
ARES cavities for the MRs
  Successful operation except for the two serious troubles:
    Vacuum trouble on the D8-D cavity
    Precipitate growth of the antirust in the chillers
DR Cavities
  Good performance demonstrated
  Significant findings directly related to cavity breakdown on the NC CW UHF cavities obtained through the high-gradient test
MR: Main Ring
DR: Damping Ring
NC: Normal-Conducting
CW: Continuous Wave
UHF: Ultra High Frequency

## Slide 41
Thank You!
Photo on June 10, 2016, in the DR/RF section
(Assembly testing)

## Slide 42: Appendices

## Slide 43: Longitudinal CBI driven by the accelerating p/2 mode
To be cured by the RF feedback systems
(shown in the next page)
Appendix A (1/5)

## Slide 44
(S. Yoshimoto)
S. Yoshimoto, et al., presented in the 14th Symposium on Accelerator Science and Technology, Tsukuba, Japan, 2003 (PaperID: 1P072)
Appendix A (2/5)

## Slide 45: Longitudinal CBI driven by the parasitic 0 and p modes
To be cured by the longitudinal
bunch-by-bunch feedback system
Appendix A (3/5)

## Slide 46: Longitudinal HOM Impedance (Simulation Results) and CBI Threshold at SuperKEKB/LER
τ=13ms for SuperKEKB/LER / 22 ARES cavities
with 3.6 A beam current
 With the full structure (including SC)
 Only AC + half CC (without SC)
< 21.6 ms (Longitudinal rad. damping time of LER)
Fastest longitudinal CBI source
To be cured by the longitudinal bunch-by-bunch feedback system
Both impedances from
wakepotentials in time-domain
Appendix A (4/5)

## Slide 47: Horizontal HOM Impedance (Simulation Result) and CBI Threshold at SuperKEKB/LER
τ=300ms for SuperKEKB/LER / 22 ARES cavities
with 3.6 A beam current
>> Transverse radiation damping time
of LER: 43.2 ms
From wakepotentials in time-domain
From eigenmode analysis
Frequency
1GHz
0
0.6GHz
(by T. Kageyama)
Appendix A (5/5)

## Slide 48: Multipactoring suppression by fine grooving of conductor surfaces of coaxial-line input couplers
T. Abe, et al., Phys. Rev. ST Accel. Beams 13, 102001, 2010
Appendix B
Ø77mm
Outer conductor of the coaxial line

## Slide 49: We have replaced all the 15 chillers used at KEKB for a long time.
First, we used the same type of chiller with the almost the same specifications (ORION RKE-1500A-VW) at the test stand (D1-A) on the ground.
  Performance and stability demonstrated
  No trouble so far for 8-year operation
We purchased succession machines (ORION RKE-1500B1-V) for MR and DR operation, and replaced the old 15 chillers (ORION RKS-1500-V-C) by these (ORION RKE-1500B1-V).
  Small amount of precipitates observed in the reservoir tanks in two of the chillers in FUJI D8 on 2015-10-07
Appendix C (1/2)

## Slide 50: Comparison between the Chillers
 | Capacity of the reservoir tank | Top cover on the reservoir tank | Feed-water inlet | Overflow-water outlet
ORION RKS-1500-V-C (used in the KEKB tunnel) | 45 L | Yes (in addition to the top cover on the chassis) | Closed in operation | Closed in operation
ORION RKE-1500A-VW (used at the test stand (D1-A) on the ground) | 30 L | None (only the top cover on the chassis) | Closed in operation | Open always
ORION RKE-1500B1-V (used in the SuperKEKB tunnel) | 15 L | None (only the top cover on the chassis) | Closed in operation | Open always
Appendix C (2/2)

## Slide 51: CBIs driven by the HOM Impedances
From wakepotentials calculated, using GdfidL, for the whole RF section
CBI thresholds for the DR design
Growth Time ＞ 30ms
＞ 10ms (rad. damping time)
Growth Time ＞ 20ms
＞ 5ms (rad. damping time)
Longitudinal
Transverse
Appendix D

## Slide 52
EOF