## Slide 1: Injector alignment
KEKB Accelerator Review Committee
14 June, 2016
Toshi Higo (Injector linac group)

## Slide 2: Contents
Alignment scheme
  Laser PD and tracker
Initial alignment
  Accelerator girders and magnets
Floor movement
  Refinement of PD measurement
Effort against emittance growth
  Present development
  Near future perspective
Conclusion

## Slide 3: Who are contributing
Accelerator group
  Enomoto, Higo, Kakihara, Tanaka, …..
Control group
  Mikawa, Satoh, Seimiya, Suwada, ……
Injector group
  Yoshida,
Mitsubishi Electric.
  Mizukawa, Kimura, Kudo, Kusano, Suzuki, Toyotomi, Ushimoto, ….
Outside company
  Nishitani, Chiyokura, …
Magnet group of KEKB ring
  Masuzawa, Sugawara, ….. but still loose coupling

## Slide 4: Requirement and strategy
Requirement
Strategy
Laser PD measurement
Initial alignment of girder
Hard ware alignment on girder

## Slide 5: Linac layout and alignment requirement
A
B
1
C
2
3
4
5
J-ARC
Rings
Laser
End PD
500m
120m
Requirement
Local s < 0.1mm
Global s < 0.3mm
  s < 0.1 mm bge 20 mm·mrad
  almost kept.
  s > 0.1 mm emittance preservation
  required.

## Slide 6: Alignment scheme
2
Hard ware
Reflectors for laser tracker use
Mechanical reference
Laser PD
Girder
Reference point of girder
1
4
3
Girder set to laser reference by PD
Support set w.r.t. mecha. reference
Hard ware aligned with mecha. reference
Hard ware alignment checked by tracker

## Slide 7: 500m straight reference line by laser
500m laser line stabilized by laser passage tilt.
Improved data reliability with robust measurement.
Sensitivity calibration done with laser tilting
Some sensors automatically and continuously measuring now
Started PD radiation damage evaluation

## Slide 8: Initial alignment of girders
Girders in sectors 3—5 were quickly aligned in 2011 after the earthquake.
Positron generation section was installed by summer 2014.
By late Jan. 2015, all units in 3—5 sectors were aligned straight.
These alignment reading is better than 0.1mm at the timing of installation.
Alignment has been measured from time to time without further re-alignment.

## Slide 9: Measurement 141128 -- 160330
Vertical
Horizontal

## Slide 10: Mounting tracker reflector on each hard ware
Mounted on coupler OD
Arm from PD to reflector
Reflectors for old Q-magnet

## Slide 11: Hard ware alignment on each girder measured in Jan. 2016
B4
C5
26
36
46
54
55
Chart: Horizontal
| -0.15 | -0.1 | -0.05 | 0 | 0.05 | 0.1 | 0.15
 | 2 | 10 | 25 | 38 | 28 | 9 | 0
Chart: Vertical
| -0.15 | -0.1 | -0.05 | 0 | 0.05 | 0.1 | 0.15 | 0.2
 | 0 | 2 | 13 | 35 | 40 | 20 | 1 | 1
s=0.056mm
s=0.051mm

## Slide 12: Accelerator position on girder unit 54 from August 2014 to May 2016
ACC’s can be aligned on each girder within below +/-0.1mm.
It is speculated to be stable within +/-0.05mm.
This should be confirmed or realized.
E
W
D
U
[mm]
[mm]
[mm]
[mm]
Unit 54 in nearly 2 years
from Aug. 2014 to May 2016
Movement in 1.5 year between July 2014 and January 2016

## Slide 13: Floor movement
Laser PD measurement showed movement of larger than a millimeter
Severe at expansion joints
Started continuous measurement over 500m
Will start detailed 40m evaluation across a joint

## Slide 14: Floor moves by fraction of 1 mm example in more than a year (2015/4/3~2016/6/2)
Vertical
Horizontal

## Slide 15: Floor movement close-up w.r.t. 2016/3/30
Expansion joint
Expansion joint
~20m from expansion joint is mostly moved.

## Slide 16: Expansion joint and evaluation
Expansion joint
Beam
West wall
East wall
Down
Notrth
Up
South
Dial gauges

## Slide 17: Relative movement across expansion joint at 28 unit
Daily regular motion exists
Gradual drift over a month after operation starts
Sensitive on tunnel temperature
Big perturbation due to typhoon
Show a year cycling.
Typhoon
Up
North
East
Operation
OFF
19 Sep. 2014
31 Oct. 2014
Notes: 台風による浸水
ドリフトしている

## Slide 18: PD measurement automatic and continuous
Measurement in every 4 hours

## Slide 19: Automatic measurement in every 4 hours at 10 locations for half a year
Horizontal
Vertical
Absolute
Rotation
from January to June in 2016

## Slide 20: Daily motion Movement in 4 hours or those in a week
Daily motion full ~ 0.1mm
Motion in 4 hours ~ 1 week +/- 0.1mm
Red arrow = +/- 0.1mm band
4 hour motion
Hor.
Ver.
1 week motion
Hor.
Ver.
During 2 weeks
Hor.
Ver.

## Slide 21: A concern PD deterioration due to radiation
Channel sum (V)
Time
Ch1-4
Sum
Deterioration observed during phase-1 operation for those at collimator.
How to use the PD information needs to be studied.

## Slide 22: Simulation and cures
SAD simulation started
Possible cure methods are under consideration.
How to stabilize position to keep alignment?
  Studies should be made how to compensate the floor movement
  Do we need other tool to evaluate the floor motion? i.e. HLS or WPS
  How to implement beam information into feedback
Compensation algorithm
  One-to-one steering  Minimize residual error^2
  DF or WF steering
  How fast can we and how frequent should we apply offset injection?

## Slide 23: SAD simulation on emittance growth along 500m straight section
Assumption
Sector C~5 over 500m
einj = 10 mm
sz = 10ps / 2.35
de = 0.4%
sQ = 0.2mm (3s cut)
XACC, YACC = Girder(measured)
2aACC = 20mm (diam.) for wake calc.
Wt = Yokoya formula
Procedure
Orbit correction at BPM without wake field
Offset injection (x, x’, y, y’) at the front of sector C with wake field ON
Add variation in misalignment of ACC and Q
Add jitter in ST and Q
Check response to beam injection jitter

## Slide 24: 60 seeds of misalignments
Phase-2
2nC
Phase-3
5nC

## Slide 25: 60 seeds of misalignments + perturbation unable to be compensated
ST: K jitter = Peak K value X 0.08% (P-P)
Q: K jitter = Peak K value X 0.32% (P-P)
Injected beam: No jitter
Mainly due to ST-K jitter
K-value jitter
ST, Q: K jitter = Operation K value X 0.2% (P-P)
Injected beam position jitter ~ beam size:
Sigma 0.1mm Gaussian in 100 seeds
Mainly due to injection jitter
Jitter should be less than beam size
Injection jitter

## Slide 26: Emittance growth under measured misalignment + random movement not to be compensated
2016/01/21
2015/04/03
Black: σACC=0.1mm, σQ=0.2mm
Red = X2
Red = X4
Red = X8
Uncompensated random movement of 0.4mm in sigma is marginal?

## Slide 27: Floor movement to be compensated
 | Horizontal | Vertical
Daily | 0.1 | 0.1
Week | 0.1 | 0.1
Year | 0.5 | 1
Speed | 0.01mm/hr | 0.01mm/hr
Unit mm

## Slide 28: Movers under study
Mover tests for accelerator girder
Support structure being developed for pulse magnets

## Slide 29: Requirements and strategy against floor movement
In phase-2 timeframe
  Alignment as is with trial cures at some points
  Confirm overall and year-scale floor movement
  Evaluate distance scale from joint
  Try to detect movement with beam
  Investigate the cure algorithm with simulation
  Study feasibility of mover or passive bridge
Development for phase-3
  Alignment corrected once more and stabilized with movers or suppression mechanism near relevant expansion joints
  Beam manipulation to keep golden orbit
  Compensation such as offset injection is developed

## Slide 30: Concluding remarks

## Slide 31: Development toward Phase-3

## Slide 32: Concluding remark
Initial girder alignment in 2014
  Done with residual ~0.3mm in sigma over 500m line.
Hard wares alignment on girder improved
  Done with errors 0.05mm in sigma
  Kept for in a year scale
Floor continuous measurement
  Movement mostly near expansion joints
  Daily motion ~0.1mm to yearly ~1mm
Floor sophisticated evaluation
  Will explore near expansion joint
  Will design compensation mechanism
Compensation mechanism
  Basic study of movers is under way
  Passive structure design study to be made

## Slide 33: Concluding remark (cont.)
Tools to identify the movement
  Radiation resistive PD is being searched
  Pending now to develop other evaluation tools
  Should study how to use which beam information
Beam study
  Should study beam emittance on floor movement
  Study offset injection
Test girder
  Installation in mid 2017
  Should study effectiveness during phase-2
Full scale cures
  Installation by Phase-3
  Sophistication in parallel to phase-3 operation