## Slide 1: Beam Transport, Injection
13/Jun/2016
21th SuperKEKB Review
N.Iida for KEKB/BT Group

## Slide 2: Contents
Introduction
Upgrades for SuperKEKB
  Changes of the beam energies
  New septum magnets
Phase1 Commissioning and status
  Orbit, charge, and Injection
  Optics measurement with wire scanners
Issues
  Water interlock
  X-Y Coupling in e+ line
Summery

## Slide 3
LINAC
LER
HER
BT for AR
0th Arc
1st Arc
2nd Arc
3rd Arc
4th Arc
4th Arc
BT for PF/AR
Switching Yard 3
(SY3)
e-/e+
KEKB/BTe+
KEKB/BTe-
PF/BTe-
e- Dump
e+ Dump
New
AR/BTe-
Introduction
The half of BT lines have double-story structure of e- and e+ lines
Slope down to the MR
11 m underground.
Notes: This is a layout of the BT.
The e- and e+ beams come from LINAC, they are branched off in the Switching Yard 3, whose picture is here.
Many ring wait for the LINAC beams.
The half of BT lines are double-story structure of e- and e+ lines.
Each line has 5 arcs like these.
After the 3rd Arc, there are slope down to the KEKB Main rings eleven m under ground.

## Slide 4: Components of BT lines
Monitor, Collimator | e- | e+
BPM | 60 | 60
Screen monitor | 20 | 20
Wire scanner | 5 | 6
Collimator | 4 | 9
Beam shutter | 2 | 1
Magnet, PS | e- |  | e+ | 
 | Magnet | Power Supply | Magnet | Power Supply
Dipole | 65 | 18 | 58 | 16
Quadrupole | 53 | 23 | 53 | 53
Sextrupole (Phase2) | 2 | 2 | 2 | 2
Steering | 45 | 45 | 50 | 50
Backleg | 25 | 25 | 16 | 16
Injection Septum | 4 | 4 | 2 | 2
Injection Kicker | 3+3 | 3+3 | 3+3 | 3+3
Introduction
Notes: The components and their numbers are like these.
The sextupoles will be used in Phase 2.

## Slide 5: Upgrades for SuperKEKB
  Changes of the beam energies
  New septum magnets

## Slide 6: 1. Change of the Beam Energy
e- : 8 GeV to 7 GeV, and e+: 3.5 GeV to 4 GeV
  The layout of Switching Yard 3 (SY3) has been reconstructed.
Increase of e+ energy
  Some dipoles : The power supplies are upgraded.
  Dipoles in 2nd and 3rd Arc : The gaps have been made narrower, which increase magnetic fields without upgrading their power supplies nor the water cooling of magnets.
Upgrades for SuperKEKB
Notes: the energy of the beams are changed.
With the change, the layout of SY3 has been reconstructed, because the 1st …
For the increase of e+ energy, Some of …
And the gaps of dipoles…

## Slide 7: Energy Compression System(ECS) at SY3
Chicane of ECS
Cavitis of ECS
8
7
3.5
4
1st Dipole of ECS
(Separation dipole)
from KEKB to SuperKEKB
e+
e-
e+/e-
e+
e-
Upgrades for SuperKEKB
    The 1st dipole of Energy Compression System(ECS), whose magnetic field is static, is also used as a separator of e- and e+.
    The orbits are changed from KEKB operation.
    The dipoles other than 1st one are renewed.
Notes: This is a layout of the SY3 with positron ECS.
There is a chicane and cavities for ECS.
The 1 dipole of …

## Slide 8: SY3 Construction changed
20/Jul/12
New Energy Compression System(ECS) of positron line at the end of LINAC is under construction, which is needed to change the energy of positron from 3.5 GeV to 4 GeV.
Magnets of ECS were removed
and the new ones will be installed
in this summer.
SY3
DR
PF
LER
HER
Chicane of ECS
N. Iida, 18th MAC
Upgrades for SuperKEKB
Notes: Here is the 3rd switching yard.
I already reported in 18th MAC.

## Slide 9: 1. Change of the Beam Energy
e- : 8 GeV to 7 GeV, and e+: 3.5 GeV to 4 GeV
  The layout of Switching Yard 3 (SY3) has been reconstructed.
Increase of e+ energy
  Some dipoles : The power supplies are upgraded.
  Dipoles in 2nd and 3rd Arc : The gaps have been made narrower, which increase magnetic fields without upgrading their power supplies nor the water cooling of magnets.
Upgrades for SuperKEKB
Notes: the energy of the beams are changed.
With the change, the layout of SY3 has been reconstructed, because the 1st …
For the increase of e+ energy, Some of …
And the gaps of dipoles…

## Slide 10: 2. New Septum Magnets
T. Mori, 19th MAC
For smaller injection error, the effective septum thickness is narrowed from 5mm to 3.5mm. (only HER in Phase1, and LER in Phase2)
Upgrades for SuperKEKB
Notes: This is also reported in the 19 MAC by Mori-san.
The HER septa work well now.

## Slide 11: Phase 1 Commissioning and Status
  Orbit, charge, and Injection
  Optics measurement and matching with wire scanners

## Slide 12: 1. Orbit, Charge
Phase 1 Commissioning and Status
LINAC
BT
LINAC
BT
e+ Target
The e+ beam with huge emittance comes from the Flux Concentrator without Damping ring now.
We use the collimators to guard the cavities.
0.45 (nc)
gex=1400mm
gey=1590mm
e+ Target
e+ Simulation
F. Miyahara,
T. Miura,
N. Iida
Collimation
Collimation
Notes: These show the orbit and charge of electron and positron from LINAC to the end of BT.
This is the horizontal and vertical orbits, and here is the charge.
The huge e+ beam comes from the FC w/o DR.
We collimate the e+ to guard the cavities.
The charge amount is consistent with the simulation.

## Slide 13: 1. Injection
The injection efficiencies are good for the both rings.
The vertical jitter of the electron beam is large, which affects the injection efficiency.
Phase 1 Commissioning and Status
Horizontal position
of 2 BPMs
Vertical position
of 2 BPMs
Y. Ohnishi
Orbit FB Panel at the end of BT
Notes: This shows the injection status of one day.
The injection efficiencies are almost good for the both rings.
This is a BT end orbit FB panel.
The vertical jitter of the electron beam affects the injection efficiency.
I will talk about it later.

## Slide 14: 2. Optics Measurement with Wire scanners (WS’s)
LINAC
KEKB Ring
SectorA(1)
SectorB(4)
SectorC(4)
Sector5(4)
Sector2(4)
BT e+(4)
BT e-(4)
BT e-(1)
BT e+(1)
Sector3(4)
Detector:
Optical Fiber
F. Miyahara, Y. Yano, N. Iida
Several wire scanners are in LINAC and BT.
A set of 4 wires is installed at each location.
Phase 1 Commissioning and Status
Wire moving
Notes: The next topic is about the optics matching with wire scanners.
We have several wire scanners in LINAC and BTs.
A set of 4 wires is installed at each location.
The wire is set as this.
Three wires measure the horizontal, 45 degree, and vertical beam sizes.

## Slide 15: Beam size measurements of e- at upstream of BT
X
Y
X
Y
X
Y
X
Y
e- from the Thermal gun
e- from the RF-gun
Thermal gun
RF gun
T. Mori
X
Y
X
Y
X
Y
X
Y
The measured vertical jitters for 20min. of e- beam in the vertical phase space are almost same for the both of guns. (All scales are same)
Phase 1 Commissioning and Status
Leak of Dispersion of BT
jitter from LINAC
V. Phase space at QXD6E
The beam sizes of RF-gun is small than those of Thermal gun.
Notes: For example, the measurement of e- beam at the BT is shown.
The beam sizes are fit by asymmetric Gaussian.
These are thermal gun and this is RF gun.
This peak is broader than other ones, which is due to jitter from LINAC beam.
The horizontally, maybe there is leak of dispersion.
The vertical jitters of …

## Slide 16
T. Mori, N. Iida
Jitter X
Jitter Y
Beam size X by WS
Beam size Y by WS
e- from RF-gun
Phase spaces at the 1st Wire scanner
The vertical jitter is large and comparable with 1s of the beam distribution.
Phase 1 Commissioning and Status
The red circle shows emittance coresponding to 1s of beam size.
Notes: These are measured phase space at the wire scanner.

## Slide 17: Measured Emittances by WS
SectorC
Sector5
BT
BTend
Phase 1 Commissioning and Status
These blow-up caused by leak of the dispersion at BT
The emittance of RF gun is smaller than thermal gun.
SectorC
Sector5
BT
BTend

## Slide 18: Issues
Water interlock
  The dipoles are down due to the water interlock 2-3 times for a week.
    The water of the cooling system is polluted by CuO. The Cu is dissolved from the cooling-water pipes.
  The water interlocks of some dipoles whose gap is narrowed work by the leaked magnetic field (20~30Gauss) from the dipoles.
    The iron cans are covered over the flow meter.
    The reason is thought the interlock switches became older.
X-Y Coupling in e+ line
〜450mm

## Slide 19: Abnormal X-Y Coupling in the e+ BT
When the beam is kicked horizontally the vertical orbit distortion appears.
Vertical position/kick
Horizontal position/kick
H. Sugimoto
A large vertical dispersion exits around the same place where the vertical design dispersion is zero and horizontal dispersion exits.
Issues
Between 2nd and 3rd Arc

## Slide 20: Abnormal X-Y Coupling in the e+ BT (Cont’d)
Some hypothesis can be thought to explain the dispersion pattern.
  The quadrupole, QCD2P, is rotated -107 mrad.
  Some of the quadrupoles around the 3rd Arc are rotated ~10mrad.
  The dipoles of the 3rd Arc, BH3P, have sextupole components.
    K2=0.1 at DY=10mm.
    The magnetic measurements of the dipoles were not so large.
    The interference from the neighbor magnets are also suspended.
All of them are not realistic.
We will study more.
Measurement
Simulation
Y. Onishi, N. Iida
Issues

## Slide 21: Summery
The performance of BT is almost well.
Some issues are not serious in Phase 1, but they should be improved by the beginning of Phase 2.

## Slide 22
Thank you.

## Slide 23: Charge at the end of BT
Phase 1 Commissioning and Status
e- injection
from RF Gun

## Slide 24: e- Orbit from RF-Gun

## Slide 25: e+ Orbit

## Slide 26: Collimation
Phase 1 Commissioning and Status

## Slide 27
〜450mm

## Slide 28: Measured Emittances
SectorC
Sector5
BT
Phase 1 Commissioning and Status
These blow-up caused by leak of the dispersion at BT
The emittance of RF gun is smaller than thermal gun.
SectorC
Sector5
BT