## Slide 1: Positron Source Status
KEKB injector linac
Takuya Kamitani
KEKB Review 2016
(2016 June 14)

## Slide 2: Positron source members
KEK
  Y. Enomoto, Yokoyama, Zang, Fukuda, Kamitani
  Tanaka, Ikeda, Kakihara, Arakida, Ohsawa, A. Enomoto
  Nakajima, Akemoto, S. Matsumoto, Higo
  Miura, Miyahara, Sugimoto, Seimiya, Iida, Ohnishi
  Okada, Takatomi, Someya, Kazama
Mitsubishi Electric System Service Co.
  Ushimoto, Suzuki, Kimura
Toyama Co.
  Iino, Morota, Sakai, Satoh

## Slide 3: SuperKEKB Injector
4.0 GeV e+
4nC x 2
3.5 GeV
10nC x 2 (prim. e-)
5nC x 2 (inj. e-)
1.1 GeV
Damping Ring
circ. 136 m
ECS
Energy-spread
Compression System
Bunch
Compressor
7.0 GeV e-
5nC x 2
low emittance
photo-cathode
RF gun
+ thermionic gun
for primary e-
SuperKEKB injector
e+ target &
LAS capture section
50 Hz (e+ or e-)
pulse-by-pulse
mode switching
S-band
linac
2.5 GeV e-
0.1nC x 1
PF
HER
LER
AR
3.0 GeV e-
(-> 6.5 GeV)
3T
RF gun
positron damping ring introduced
new positron focusing lens: flux concentrator (3.5 T) + bridge coils (1.0 T)
large-aperture (2a=30mm) accelerating structure (LAS) in capture section
positron focusing beam line layout reorganized with 100 new quad. magnets
Upgrade items in positron source
Low emittance e+
e+ intensity (x4)

## Slide 4: SuperKEKB positron source
positron
production
Target
Flux
Concentrator
Bridge
Coils
primary
e- beam
3.3 GeV
e+ beam

## Slide 5: target offset & beam hole
Flux
Concentrator
e+
injection e-
primary e-
bridge coils
target
beam
hole
pulse ST
DC QM
pulse QM
side view
rear view
injection e- beam : on axis to preserve low emittance
primary e- beam : 2.5 mm off axis to minimize e+ yield degradation (target offset 3.5 mm, FC offset 2.0mm)
target
offset
3.5 mm
2.0 mm
FC offset
7.0 mm
FC aperture
spoiler
target
diameter
4.0 mm
hole
diameter
2.0 mm
solenoid
Accel.
structure

## Slide 6: Positron Capture Section
KLY
1-5
KLY
1-6
SLED
SLED
LAS 14 MV/m
deceleration & phase slip & acceleration
LAS 10 MV/m
acceleration
Solenoids
target
+FC
LAS : Large Aperture S-band structure
Large Aperture
S-band structure (LAS)
LAS with SLEDs for sufficient field gradient
breakdown issue of LAS in solenoid field
needs careful RF conditioning
operated at 10 MV/m
with SLED detuned

## Slide 7: e+ capture section in linac tunnel
Flux concentrator,
target, bridge coil
(inside)
elecron beam
DC solenoids & LAS accel. structures

## Slide 8: e+ status at previous Review (2015/02/24)
e+ source components had been installed and operated at limited performance
  FC : IFC = 6 kA (spec. 12 kA) with temporary pulse modulator
  BC : IBC = 600 A (=full spec)
  DC Solenoids : IDC = 370 A (spec. 650 A)
  Acc. field : EACC = 10, 12 MV/m (spec. 14, 10 MV/m)
  DR not yet available
(Linac stand-alone) e+ initial commissioning (first e+ for SuperKEKB)
  Q(e+) = 0.12 nC@SY2 with Q(e-) = 0.60 nC, E(e-) = 3.1 GeV spec. (5.0 nC after DR -> 4.0 nC) (10.0 nC) (3.3 GeV)
  Y(e+) = (0.12 nC / 0.60 nC) = 20% @SY2 (= at entrance to DR)
FC coaxial feeder cable accident -> renewal planned for thicker cable (insulator 2.3 -> 7.4 mm) and parallel plate feeder line (two plates -> triplate)
higher voltage tolerance
lower induced voltage

## Slide 9: FC test stand (2015 July)
test operation performed with
  spare FC-base (#4)
  12-kA pulse modulator
  new coaxial cables
  new triplate feeder line
  snubber circuit
  but w/o bridge coils
full-spec (12 kA) operation for continuous 200 hours achieved with no serious breakdowns and problems
FC-base (#4)
triplate
feeder line
snubber
circuit
coaxial
cables
cable connection
inside modulator

## Slide 10: Installation in linac tunnel (2015 August)
triplate
feed line
12 kA
pulse
modulator
FC &
target
radiation shield
Installed for beam operation
  12-kA pulse modulator
  new coaxial cables
  new triplate feeder line
  snubber circuit
Same as before
  FC assembly #1 (FC-base #3)
  Bridge Coils
  DC solenoids & accel. structures

## Slide 11: Double-deck pre-injectors
Lower deck photo-cathode RF gun
+ magnetic bunching
Upper deck (former KEKB pre-injector, reconstructed !)
thermionic gun + RF bunching section
RF gun 25 ps
Chicane 10 ps
bunch
length
bunch
length
shield
wall
Gun 200 kV (=> 5 MV/m) 1300 ps
Sub Harmonic Buncher 1 (114 MHz) 500 ps
Sub Harmonic Buncher 2 (571 MHz) 330 ps
Prebuncher (2856 MHz) 70 ps
Buncher (2856 MHz) 10 ps
e- beam for
e+ generation
e- beam for
HER injection

## Slide 12: FC processing with BC field
2015.09.24
FC stable at IFC = 11.5 kA
w/o BC field
2015.09.28
Huge gas burst occurred
at IFC = 9.8 kA @IBC = 750A
2015.09.29
Gas bursts occurred
even w/o BC field
Vacuum Pressures [Pa]
at FC and at LAS
Currents
of FC and of BC
Irreversible damage in FC
by breakdown !!
Operable current
lowered -> 6 kA

## Slide 13: FC copper block work hardening
Y. Enomoto and T. Higo visited SLAC and discussed with the positron experts (A. Kulikov and E. Bong) on the FC gas bursting issue.
They suggested that the work hardening of the OFC block of FC is essential against the damage by breakdown. (We neglected this process!)
"Work hardening (strain hardening)" is a method of strengthening of a metal by repeated plastic deformation.
When a breakdown occurs in FC, the spiral structure is deformed but it springs back to the original shape if it is work hardened.
Unless work hardened, deformation remains permanently and makes very narrow gap in the slit.

## Slide 14: Hardening test
Press FC-head till the gaps are contacted.
Insert spacers into the slit.
Remove the spacers.
Measure the gap size.
Repeat them from (1) (~ 100 times)
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0
1回目 | 0.32577 | 0.40412 | 0.30515 | 0.31134 | 0.3299 | 0.29691 | 0.23711 | 0.17938 | 0.18557 | 0.12371 | 0.084536
2回目 | 0.43404 | 0.42553 | 0.31702 | 0.33617 | 0.34468 | 0.32979 | 0.27234 | 0.21702 | 0.25319 | 0.18298 | 0.078723
3回目 | 0.42609 | 0.41957 | 0.31739 | 0.33913 | 0.32391 | 0.34565 | 0.29783 | 0.2913 | 0.31739 | 0.25217 | 0.056522
4回目 | 0.36842 | 0.36421 | 0.28211 | 0.28421 | 0.30105 | 0.28421 | 0.25053 | 0.22737 | 0.23158 | 0.15368 | 0.044211
5回目 | 0.43158 | 0.40211 | 0.31579 | 0.34105 | 0.36421 | 0.35789 | 0.25684 | 0.23368 | 0.26105 | 0.22526 | 0.11579
6回目 | 0.56 | 0.46526 | 0.36211 | 0.38947 | 0.39579 | 0.40842 | 0.34105 | 0.29684 | 0.30316 | 0.39789 | 0.27158
Hardening Procedure
natural gap size (mm)
slit position (downstream <- upstream inside FC)
# of trials
The natural gap size transfers to the spacer thickness (0.3 mm) by repeated hardening.

## Slide 15: FC assembly #2 & test stand
Operation test with BC field is essential.
FC assembly #1 is radio-activated in the beam line.
Construct assembly #2 for operation with BC field at test stand.
Test-1: operation with FC-head #4 (not work-hardened model) to see what happens in the same situation as the damaged FC. [2016 June, soon]
Test-2: operation with FC-head #5 (well work-hardened model) to check the operability at full current (12 kA) under the BC field. [2016 August ~]

## Slide 16: e+ beam performance (2015 Nov.)
target
Sector-2 end
Primary Electron
intensity at target
Q(e-) = 6.3 nC
beam
intensity [nC]
Q(e+) = 1.9 nC
at entrance
of DR LTR line
Beam tuning to optimize e+ yield performed in 2015 Oct ~ Dec.
IFC = 6 kA (design 12 kA) enhancement by FC ~ 1.8
Q(e-) = 6.3 nC @ target Q(e+) = 1.9 nC at SY2 Y(e+) = 1.9/6.3 => 30 % (design 50 %)
Deceleration
Capture
Acceleration
Capture
Yield enhancement by FC (6 kA) ~ 1.8
Y(e+) upon FC pulse timing
FC on
timing
FC off
timing
Y(e+) upon capture RF phase
operation
phase

## Slide 17: Is achieved e+ charge consistent with simulations ? (committee member’s question)
We do not have a simulation result which reflect all the operation condition. (GEANT simulation [e+ generation at target] +GPT simulation [e+ capture simulation] +SAD tracking simulation [e+ transport in linac & BT line)
  precise beam spot size on the target is unknown -> planning to install thin screen monitor and triggered camera in this summer shutdown
  DC solenoid field distribution modified to optimize e+ intensity
  FC 6 kA situation
  Lower LAS acceleration field situation
Possible comparison simulation expectation now is Y(e+) ~ 45 % at capture section exit and the observed Y(e+) ~ 30 % at after the 1-6 chicane.
It is my homework for next KEKB Review.

## Slide 18: SuperKEKB e+ injection beam
Gun
J-arc
target
Linac end
Q(e+) = 0.3 nC
at BT-line end
Primary Electron
intensity at target
Q(e-) = 7.0 nC
orbit-X
[mm]
orbit-Y
[mm]
beam
intensity [nC]
Q(e+) = 0.75 nC
at linac-end
Q(e+) = 1.3 nC at SY2
[2.0 nC if no collim.]
BT end
Beam collimators inserted to localize
beam loss in low energy region.
Due to limited beam acceptance, inevitable beam loss
occurs in linac & BT-line in direct injection w/o DR.
Typical e+ injection beam at linac and BT-line

## Slide 19: SuperKEKB e+ beam performance
IFC = 5.2 kA
FC OFF
IFC = 2.2 kA
with temporary
pulse modulator
e+ beam intensity history (2016 Jan ~ June)

## Slide 20: Diamond beam loss monitor
Radiation-hard diamond beam loss monitor was developed by S. Kazama in collaboration with V. Kubytskyi and P. Bambade (LAL Orsay)
single crystal CVD diamond 2.0 mm x 2.0 mm x 0.5 mm with electrode (Ti, Pt, Au) operated at 400 V.
Detect beam hit/no-hit (1) on beam spoiler and (2) on target
20nsec
typical
signal
linearity to
beam charge
2mm

## Slide 21: Summary
Though test operation of spare FC (#4) with new modulator, new cables, new triplate feeder but w/o BC was successful up to 12 kA, a serious damage occurred in FC (#3) with BC field (2015 Sep.) and operable current has been 5 ~ 6 kA.
Importance of work-hardening process of FC-head was recognized. Test stand with FC assembly #2 has been constructed to perform tests of not-hardened and well-hardened models with BC field. (2015 June ~)
Positron yield Y(e+) = 30% (Q(e+)=1.9nC/Q(e-)=6.3nC) achieved with 6 kA FC current at entrance of DR-LTR line. Stable e+ injection to LER has been achieved (Q(e+)@BT-end ~ 0.3nC x 2-bunch) since 2016 Feb. Beam loss in linac and BT line is due to operation w/o DR.
After finishing operation at test stand, FC assembly #2 will be installed in the beam line in 2016 Dec. ~ 2017 Jan. DR commissioning and LER injection in Phase-2 will be started in 2017 Nov.