## Slide 1: Instabilities simulation and observation
K. Ohmi, J. Flanagan, H. Fukuma, Y. Funakoshi, H. Ikeda, Y. Suetsugu, S. Terui, M. Tobiyama, D. Zhou
21-th KEKB Accelerator Review Committee
KEK, 13-15 June, 2016

## Slide 2: Contents
Beam size blow-up due to Electron cloud
Coupled bunch instability due to electron cloud
Coupled bunch instability in HER
Tune shift measurement and transverse impedance
Bunch length measurement

## Slide 3: Beam size blow-up in LER
June 1, 2016
4 train x150 bunches, Nbunch=600
H. Fukuma et al.,
Beam-size blowup observed in KEKB has been seen in early stage of SuperKEKB commissioning
Threshold I~300mA in Apr 19 (Y. Funakoshi)
Electron cloud has been monitored at AL chamber w and w/o TiN coating (Y. Suetsugu).
Beast study threshold I~600mA, Nbunch=1576 in May 17 (Nakayama et al)
Systematic study in 1 June ( H. Fukuma et al.)
Permanent magnets are set at aluminum bellows.(Y. Suetsugu et al.)
Systematic studies in 8 July ( H. Fukuma et al.)
Threshold beam current
160, 200, 260,500 mA for 2, 3, 4, 6 bucket spacing

## Slide 4: Instability simulation at SuperKEKB design stage
Using code PEHTS
Simulation, reth=3.8x1011 m-3.
re=4.2x1011 at 4000-th turn
Design target for vacuum system: re<1011 m-3 in average of whole ring

## Slide 5: Simulation studies using beam study condition
Np=1.6x1010 Ith=160mA, 4ns spacing
Np=2.1x1010
Ith=200mA, 6ns spacing
Np=2.7x1010
Ith=260mA, 8ns spacing
Np=5.2x1010
Ith=500mA, 8ns spacing
Np=2.1x1010, ey=100pm
Np=2.4x1010, ey=100pm
Threshold of the electron density
ex=2nm, ey=15pm, sz =6mm, ns=0.019

## Slide 6: Simulated threshold electron density (condition before solenoid installation)
Nb=600, ex=2nm, ey=15pm, sz =6mm, ns=0.019
spacing | Ip,th (mA) | Np,th (1010) | we/2p (GHz) | wesz/c | reth (Q=10) (1011m-3) | reth (Q=6) (1011m-3) | reth (Simu) (1011m-3)
2 (4ns) | 160 | 1.6 | 61 | 7.7 | 1.91 | 2.45 | 3.4
3 (6ns) | 200 | 2.1 | 71 | 8.9 | 1.65 | 2.45 | 3.4
4 (8ns) | 260 | 2.7 | 80 | 10.1 | 1.47 | 2.45 | 3.8
6 (12ns) | 500 | 5.2 | 111 | 14.0 | 1.47 | 2.45 | 5.0
3.06 | 500 | 2.0 | 37 | 5.5 | 2.89 | 2.90 | 4.4
3.06 | 600 | 2.4 | 41 | 6.0 | 2.63 | 2.65 | 4.4
Nb=1576, ey=100pm
6

## Slide 7: Electron cloud measurement
Retarding bias, V=500V or 0V, select electrons with E>500eV or all, respectively.
Electron E=500eV, v=1.3x107m/s. R/v=3.8ns, R=5cm, density can be estimated considering volume with energy gain 500eV from a bunch. 500eV may be critical for 2 (4ns) spacing.
For V=0V, electron rate production including secondary is detected.

## Slide 8
Measured electron current
Al部分
Al w TiN coating
Al wo coating
Al wo coating
Al w TiN coating
Vr = -500 V
Vr = -500 V
Vr = 0 V
Vr = 0 V
For V=0V, 1mA, electron production rate is 0.3x109 m-1/bunch
Y. Suetsugu

## Slide 9: Electron density at the blow-up threshold
Simulated electron density at the threshold current
Measured threshold current and density
Simple formula Q=6
Only Al part

## Slide 10: After installation of permanent solenoid at Al bellows
Simple formula Q=6
2016/6/8
4/150/3
4/150/2
4/150/4
Ith=200 mA
Ith=330 mA
Ith>600 mA
Simulated electron density at the threshold current

## Slide 11: Threshold of electron cloud density after solenoid attach
spacing | Ip,th (mA) | Np,th (1010) | we/2p (GHz) | wesz/c | reth (Q=10) (1011m-3) | reth (Q=6) (1011m-3) | reth (Simu) (1011m-3)
2 (4ns) | 200 | 2.1 | 71 | 8.9 | 1.65 | 2.45 | 3.4
3 (6ns) | 330 | 3.5 | 91 | 11.5 |  | 2.45 | 4.8
4 (8ns) | >600 | >6.3 |  |  |  |  | 
6 (12ns) |  |  |  |  |  |  | 
3.06 | 500 | 2.0 | 37 | 5.5 | 2.89 | 2.90 | 4.4
3.06 | 600 | 2.4 | 41 | 6.0 | 2.63 | 2.65 | 4.4

## Slide 12: Simulated electron cloud build up in Drift
Np=2.5x1010, I=240 mA for Nb=150x4=600
Np=4x1010, I=380 mA for Nb=600
Np=9.4x1010, I=900 mA for Nb=600
2016/6/8
4/150/3
4/150/2
4/150/4
Ith=200 mA
Ith=330 mA
Ith>600 mA
Beam current: Slightly higher than measured threshold
re(r=0)~lex1000
Y1=Photon numberx0.1x0.01

## Slide 13
t(sec)
electron density near beam(m-3)
dmax=1.0
dmax=1.2
dmax=1.4
dmax=1.5
計算を打ち切った。
E cloud buildup
dmax=1.3
CLOUDLAND, Fukuma
Np=3.13x1010,
Density R<4mm
Y1=Photon numberx0.1x0.01
quantum eff. antechamber

## Slide 14: Coupled bunch instability caused by electron cloud
Electron cloud motion reflects coupled bunch instability mode.
Electrons in drift, short range wake ~10ns
Electrons in solenoid, slow rotation around chamber surface.
KEKB
400 f0
1000 f0

## Slide 15: Unstable mode (before solenoid installation)
Typical signal of coupled bunch instability caused by drift electrons
Fast, strong
400 f0
400 f0
1000 f0
M. Tobiyama

## Slide 16: Mode spectrum
By 2 ver 300mA 400mA
By 4 ver 350mA 600mA
Drift origin
Solenoid origin
Solenoid origin
Solenoid origin

## Slide 17: Unstable mode (after solenoid installation)
Typical mode caused by electrons in solenoid is seen.
Mode seems to change to those of drift origin at high current.
Fast, strong
540 f0
700 f0
400 f0
Solenoid modes

## Slide 18: Coupled bunch instability in electron ring (HER)
Ion?
Fast, strong
CO
Resistive wall
5120-1=5119
M. Tobiyama

## Slide 19: Impedance estimation- transverse
Tune shift as function of bunch current
KEKB-LER: -0.0034mA-1, 81kW/m
coll. open 33-46 kW/m T. Ieiri, EPAC00
LER
HER
Collimator dependence
HER y
LER x

## Slide 20: Longitudinal impedance issue-Bunch length measurement
L
Measured by a Streak camera
The behaviors are similar as KEKB for both of LER and HER.
Bunch lengthening is stronger than that of simulation.

## Slide 21: Summary
Beam size blow-up has been observed since early stage of SuperKEKB commissioning.
Electron density at Al bellows part (5% of circumf.) is high (re>1012m-3). Simulations show the electrons can cause fast head-tail instability.
Coupled bunch instability caused by electron cloud has also been observed as is predicted.
Installation of Permanent solenoid reduced the blow up. It is possible to operate with 1A, 4 bucket spacing at present condition.
Tune shift as function of bunch current was measured to estimate transverse impedance. It was 30-50kW/m, similar as KEKB.
Bunch length was measured by a streak camera. Bunch lengthening, which was similar as KEKB, was observed, 7-8 mm at the design current, while no bunch lengthening in prediction.

## Slide 22: Thank you for your attention

## Slide 23: Rough estimation of Electron density
Electron current, Ie=1mA.
Acceptance of the electron detector, Smon=1 cm2.
Number of electron absorbed (=produced) at chamber wall, d=10cm.
Electron stay time in the chamber, te=100ns. Electron density

## Slide 24: Emittance dependence
Vertical emittance knob
by=67m

## Slide 25: Design current & spacing
Np=9.4x1010, I=3600 mA

## Slide 26
金澤氏の式を使った電子密度の算出*
＊PAC2005, p.1054
e = 1.602E-19 [C]
frev = 1E5 [s-1]
re = 2.818E-15 [m]
me = 9.109E-31 [kg]
c = 3.0E8 [ms-1]
nb = バンチ数
pA = 通過確率 = 0.0003x1/4 = 7.5E-5
Vb = グリッド電圧 [V]
Nb = バンチ内のe+の数
Nb =
I
nbfreve
I = ビーム電流 [A]
例えば、2/150/3 Vr = -30 V, I = 200 mA, Iobs = 1E-7 A の場合 (平均で)
nb = 600, Vb = 30
まとめると、
D = 2.630E13 x
I2
IobsnbVb
D = 1.18E12 [e- m-3]

## Slide 27: Simulated electron cloud build up in Bend
Np=2.5x1010, I=240 mA for Nb=600
Np=4x1010, I=380 mA
Np=9.4x1010, I=900 mA
4/150/3
4/150/2
4/150/4
Ith=200 mA
Ith=330 mA
Ith>600 mA
Multipactoring arises Y2max>=1.5 at the threshold beam currents.
bucket
bucket
bucket

## Slide 28
Solenoid-Off
0
0.1
0.2
0.3
0.4
0
200
400
600
800
1000
1200
1400
Mode
Horizontal
0
200
400
600
800
1000
1200
1400
0
0.4
0.8
1.2
Mode
Vertical
Simulation
0
200
400
600
800
1000
1200
1400
0
1
2
3
4
5
x 10
4
Horizontal
Mode
0
200
400
600
800
1000
1200
1400
0
1
2
3
Vertical
Mode
x 10
3
Experiment
Su Su Win et al,(EC2002)
KEKB