## Slide 1: High-energy laser source of RF gun
Xiangyu Zhou

## Slide 2: Contents
Laser system, underground
  Yb-doped fiber & Thin-disk Yb:YAG @ 1030 nm
New laser system, on the ground
  Yb-doped fiber & Rod Nd:YAG @ 1064 nm
  Yb-doped fiber & Thin-disk Yb:YAG @ 1030 nm

## Slide 3: Requirement of laser system for RF-Gun
Gaussian
Square
5nC
10nC
15nC
20nC
20nC
15nC
10nC
5nC
5nC electron
15nC
Primary beam for positron production
t
t
Nd-doped △
Yb-doped ◎
○ 4-state laser is easy to operate.
○ High power pump LD is available.
○ Large crystal is available
× Pulse width is determined by SESAM. (Gaussian)
○ Wide bandwidth => pulse shaping
○ Long fluorescent time => High power
○ Fiber laser oscillator => Stable
○ Small state difference
× ASE
× Absorption
Laser energy
  500 mJ for Ir5Ce cathode
  50 mJ for Ce2Te cathode
50 Hz, 2-bunch (96ns spacing)
Temporal pulse shaping to reduce energy spread => Broadband laser crystal (Yb or Ti:Sapphire)
Continuous operation => High power pump LD (Yb or Nd)
Ti-doped ×
○ Very wide bandwidth
○ High breakdown threshold
× Low cross section
× Q-switched laser is required for pumping
  No laser system company in Japan.
  Support cost for commercial product is very high.

## Slide 4: Yb-doped Solid-state laser
disk
fiber
Fiber amplifier
Thin-disk amplifier
○ Long gain media
○ Compact
○ No need cooling
○ Good beam quality
× Pulse energy
× Thin gain media (low gain)
× Cooling system
× Thermal lens effect
○ High pulse energy

## Slide 5: Underground laser system
Yb-doped fiber oscillator with Transmission grating
Yb-doped fiber pre amplifier
Yb-doped fiber main amplifier
Pulse picker
Yb:YAG thin-disk multi-pass cavity amplifier
Yb:YAG thin-disk multipass amplifier ×3
SHG
Synchronization system
SHG
RF GUN
51.9 MHz
2, 5, 25 Hz
Single or Double bunch
0.2 nJ @ 1030 nm
Yb-doped fiber main amplifier
Transmission grating pair stretcher
2856 MHz trigger
From Accelerator
Yb-doped fiber pre amplifier
>μJ @ 1030 nm
Pulse picker
10 MHz

## Slide 6
Fiber Oscillator & Amplification
WDM
coupler
4μm
LD
Pump
750 mW
Collimator
Low power amplifier
Yb-doped Fiber
Low loss
Compact
Isolator
Yb-doped Double cladding Fiber
PM
LD
Pump
Collimator
Dichroic mirror
HR@976 nm
HT@1050 nm
Ɵ=20°
75 W
High power amplifier
High amplify efficiency
LD
Pump
WDM
coupler
Isolator
Yb-doped fiber
SMF
SMF
Collimator
Collimator
Polarizing
l/4
l/4
Output
l/2
250mW
976 nm
1000-grooves/mm
Grating pair
PIEZO
P.D.
l/4
Yb fiber Oscillator
51.9 MHz
Stable

## Slide 7
Yb:YAG thin-disk amplifier
LD
Laser Diode
INPUT
OUTPUT
1pass
10-15pass
←
1pass
LD
Laser Diode
2pass
3pass
4pass
5pass
Balanced offset lens to avoid damage.
940nm LD (2.4 kW / module)
Yb:YAG disk
10 % doped
0.5mm thickness
To obtain higher gain,
=> Higher pumping density
Focused type amplifier to avoid thermal lens.
Cavity multi-pass amplifier (15 pass x 2 loop) to simplify the laser

## Slide 8: Temperature of the Yb:YAG thin-disk amplifier
10% dope, α=12/cm, 5kW/cm2, 25Hz
0.5t
1t
Repetition rate limitation of 25 Hz is reached!

## Slide 9: Spectral Range Adjustment
t
Chirp
t
Spatially dispersed
d
For chirped pulse, the pulse shaping in the time domain can be controlled by adjusted the spectral shaping of the pulse.
Spatial Mask
~200fs
~30ps
Distance of the grating pair
l
Pulse shaping
Width of the slit

## Slide 10: Optimized pulse shape by streak camera (After adjustment 2015.12.17)
ω：~10 mJ, 2ω： ~2 mJ, 4ω： 230 μJ
Due to the Non-linear effect was occurred, Output power limitation is reached!

## Slide 11
Entrance
Entrance
Elevator
PCF fiber
amplifier
Fiber
pre-amplifier
Grating pair
stretcher
Thin-disk
multi-pass
amplifier
Thin-disk
multi-pass
amplifier
Thin-disk
multi-pass
amplifier
Streak camera
Sheld
To GR_A1
Control
rack
PCF fiber
amplifier
SHG
1033nm
↓
532nm
Yb-doped
Fiber
Oscillator
1
Yb-doped
Fiber
Oscillator
2
Thin-disk Multi-pass
cavity amplifier
EO Pulse
picker
Layout of A1 laser room
0.2 nJ
20 μJ
10 mJ
SOA Pulse
picker
3 mJ
Fiber
pre
amplifier

## Slide 12
Tunnel
RF-Gun
Laser Hut
Laser line to RF-Gun
Laser line underground
2nd SHG stage
Energy loss of the UV in the air: >50%

## Slide 13: SHG for the 4ω
Motorized Translation Stages

## Slide 14
Stability of lasers (3 days)
Elevator maintenance
Laser off

## Slide 15
Stability of lasers (4/26—6/9)
Trig stoped
Last laser Maintenance
No signal, LD work on

## Slide 16: Summary of the underground laser
Yb-doped fiber & Thin-disk Yb:YAG hybrid system @ 1030 nm
Development of Underground Laser is finished.
The stability of laser is improved.
The laser is employed for the Phase-I study.
The limitation of the output power (10 mJ) and repetition rate (25 Hz) is reached.

## Slide 17
Laser Hut
KLY Gallery
Tunnel
Laser line to RF-Gun
RF-Gun
Laser line on the ground

## Slide 18
Yb fiber laser system on the ground
Menlo
1030nm oscillator
(commercial)
Grating stretcher
(Transmission)
SOA
pulse picker
Yb single mode
fiber amp
Yb-doped double clad
fiber amp
Repetition frequency
114.24MHz
Wavelength selection
1030nm & 1064nm
Repetition frequency
10MHz
Nd:YAG
regenerative amplifier
EO module
pulse picker
10Hz
Yb:YAG Thin disk
regenerative amplifier
1030-64 nm ANDi type oscillator
Output(1030nm)
Output(1064nm)
ASE rejection
grating pair
1030nm
1064nm
1064nm
Fiber part
Yb-doped PCF
fiber amp

## Slide 19: New System
Grating pair
Spatially dispersed
Yb fiber Oscillator
Fiber+Yb:YAG Thin-disk
Amplifier @1030 nm
Fiber+Nd:YAG Rod Amplifier @1064 nm

## Slide 20: Issue of the underground laser
Complex structure (Stability, Maintenance)
50 Hz double bunch repetition rate
  10 MHz oscillator
  High energy fiber amplifier
  Yb:YAG & Nd:YAG Regenerate amplifier
Amplifier efficiency & Non-linear effect
  Chirped Pulse Amplification (CPA) system

## Slide 21: Oscillator of 10 MHz repetition rate
Repetition rate | Cavity length | Fiber length
114.24 MHz | 2.6 m | ~1 m
10.38 MHz | 28.9 m | ~20 m

## Slide 22: Chirp Pulse Amplification (CPA)
Yb fiber Oscillator
Yb PCF
amplifier
Thin-disk amplifier
Harmonic generation
Stretcher
2 ns
Compressor
30 ps
Yb fiber Oscillator
Yb PCF
amplifier
Harmonic generation
Thin-disk amplifier
Stretcher
30 ps
Under ground Yb laser system
On the ground Yb laser system

## Slide 23: Grating pair compressor
63.65°
180 mm
ΔƟ
l
 | Δλ | ΔƟ | l
Fiber amp | 20 nm | 4.5° | 1020 mm
Yb:YAG Gain Spectrum | 2 nm | 0.45° | 10173 mm
2ns pulse can be dechirped
Vacuum Chamber
Canon transmission grating
Size: 180mm×50mm
Groove density: 1740 lines/mm
Diffraction efficiency: 95%

## Slide 24
Yb:YAG thin disk regenerative amplifier
For picosecond and nanosecond laser pulse, the regenerative amplifier is very powerful
Strong amplification factor can help relieve stress of multi-pass amplifier stages and reduce thermal effect
New dichroic mirror with high optical quality and high damage threshold

## Slide 25
Low temperature Yb:YAG thin disk laser
Low temperature laser operation feasibility analysis
  Available high gain is possible
  Low amplified spontaneous emission (ASE)
  Simpler and more stable (compare with cryogenic laser)
Current low temperature laser operation
  Peltier cooling plates: 23 oC  -36 oC
  Small vacuum chamber
  Home made laser soldering laser head
  50 Hz repetition rate test

## Slide 26: Yb fiber and Nd:YAG multi-stage laser @ 3-2
・Laser energy
4.0mJ@1064nm
550uJ@532nm
120uJ@226nm
・Under beam comissioning

## Slide 27: Nd:YAG Diode-pumped solid-state (DPSS) Regenerative amplifier
○ 4-state laser is easy to operate.
○ High power pump LD is available.
  808nm : Commercial product
○ High gain efficiency.
○ Large crystal is available
× Small gain bandwidth. (Gaussian)
1.1% Dia. 4×93mm AR/AR@1064nm

## Slide 28: Plan A
Stretcher to 2 ns
Nd:YAG
regenerative amplifier
EO module
pulse picker
10Hz
Yb:YAG Thin disk
regenerative amplifier
10 MHz ANDi type oscillator
Output
1064nm
Yb-doped PCF
fiber amp
High-energy Yb-doped ROD PCF fiber amp
1030nm
Grating pair Compressor to 30 ps
< mJ
SHG × 2
Grating stretcher
To 30 ps
SOA
pulse picker
Yb single mode
fiber amp
114 MHz fiber oscillator
Yb fiber + CPA + Yb:YAG
Developed
Developing

## Slide 29: Plan B
Stretcher to 2 ns
Nd:YAG
regenerative amplifier
EO module
pulse picker
10Hz
Yb:YAG Thin disk
regenerative amplifier
10 MHz ANDi type oscillator
Output
1064nm
Yb-doped PCF
fiber amp
High-energy Yb-doped ROD PCF fiber amp
1030nm
Grating pair Compressor to 30 ps
< mJ
SHG × 2
Grating stretcher
To 30 ps
SOA
pulse picker
Yb single mode
fiber amp
114 MHz fiber oscillator
Yb fiber + Nd:YAG

## Slide 30: Summary
Laser system, underground
  Yb-doped fiber & Thin-disk Yb:YAG @ 1030 nm
    Development of Underground Laser is finished.
    The stability of laser is improved.
    The limitation of the output power and repetition rate is reached.
    The laser is employed for the Phase-I study.
New laser system, on the ground
  Yb-doped fiber & Rod Nd:YAG @ 1064 nm
    Fiber parts are finished.
    Nd regenerative amplifier for the Phase-II stable injection.
  Yb-doped fiber & Thin-disk Yb:YAG @ 1030 nm
    10 MHz oscillator to simplify the laser system
    High-energy fiber ROD amplifier μJmJ
    CPA system to avoid non-linear effect
    Yb regenerative amplifier for the Phase-III