## Slide 1: SuperKEKB 概要と補足説明
Sep. 8, 2017 国内レビュー
Haruyo Koiso,
for the SuperKEKB Accelerator Group

## Slide 2: 資料
https://kds.kek.jp/indico/event/15914/
Design Report ドラフト
マシンパラメター表
Strategy of Phase 2 by 大西さん

## Slide 3
40 times higher luminosity
2.1x1034 --> 8x1035 cm-2s-1
SuperKEKB
Colliding bunches
Nano-Beam scheme
extremely small by*
low emittance
Beam current double
New e+ Damping Ring
HER
e- 2.6 A
7 GeV
LER
e+ 3.6 A
4 GeV
Injector Linac upgrade
Injector Linac upgrade
RF electron gun
improve e+ source
Wiggler sections upgrade
Redesign the lattice to squeeze the emittance (replace short dipoles with longer ones, increase wiggler cycles)
Replace beam pipes with TiN-coated antechamber-type ones
New superconducting final focusing magnets near the IP
Reinforce RF systems for
higher beam currents
Improve monitors and control system
IP

## Slide 4: SuperKEKB
Beam current (LER/HER):
1.64/1.19 A (KEKB)
→ 3.6/2.6 A (SuperKEKB)
Beam-beam parameter:
0.129/0.090 (KEKB)
→ 0.088/0.081 (SuperKEKB)
Vertical  at the IP:
5.9/5.9 mm (KEKB)
→ 0.27/0.3 mm (SuperKEKB)
Lorentz factor
Classical electron radius
Beam size ratio
Geometrical reduction factors due to crossing angle and hour-glass effect
Luminosity:
2.11 ×1034 cm-2s-1 (KEKB)
→ 80 ×1034 cm-2s-1 (SuperKEKB)
Challenging
Beam energy (LER/HER) : 3.5/8.0 GeV (KEKB) → 4.0/7.0 GeV (SuperKEKB)
２倍
1倍
20倍
40倍
Luminosity gain

## Slide 5: Beam Commissioning
Phase 1
w/o QCS and Belle II
Basic machine tuning
Vacuum scrubbing
Low emittance tuning
Phase 2
w/QCS and Belle II
w/o Vertex detector
Luminosity tuning
Target luminosity: 1 x 1034 cm-2 s-1
background study
Phase 3
Physics Run
Luminosity tuning
Target luminosity: 8 x 1035 cm-2 s-1
~5 months
Feb. - June 2016
successfully finished
~5 months
Beam commissioning is being performed in three phases.
QCS: final-focus superconducting magnet system
Y. Funakoshi et al.
Here we are.

## Slide 6: Parameter
 | KEKB LER /HER | Phase 1 | Phase 2 4x8 | Phase 3
bx* (mm) | 1200 / 1200 | / | 128 / 100 | 32 / 25
by* (mm) | 5.9 / 5.9 | / | 2.16 / 2.4 | 0.27 / 0.30
ex (nm) | 18 / 24 | 2.0 / 4.6 | 2.1 / 4.6 | 3.2 / 4.6
ey (pm) , coupling | 1498 / 1598 | ~ 10 / - | 29.4 / 64.4, 1.4% (105 / 230, 5.0%) | 8.64 / 12.9 (0.27% / 0.28%)
xy | 0.129 / 0.090 | - | 0.0484 / 0.0500 (0.0257 / 0.0265) | 0.088/0.081
sy* (mm) | 0.94 / 0.94 | - | 0.25 / 0.39 ( 0.48 / 0.74) | 0.048/0.062
Ibeam (A) | 1.64/1.19 | 1.01/0.87 | 1.0/0.8 | 3.6/2.6
Nbunches | 1584 | 1576 | 1576 | 2500
Luminosity (1034 cm-2 s-1) | 2.1 | - | 2 (1) | 80

## Slide 7: Nano-beam Scheme
5 mm
100 mm
1 mm
KEKB
SuperKEKB
垂直ビームサイズ
水平方向バンチ衝突の様子
Phase 2 “4x8”
bx* = 128 mm, by* = 2.16 mm
ey = 29.4 pm (coupling 1.4%)
Phase 3
bx* = 32 mm, by* = 0.27 mm
ey = 8.64 pm (coupling 0.27%)
SuperKEKB
バンチはLERのパラメタで記述
KEKBは比較のため
水平方向は有限交差角衝突の場合を記述
垂直方向は21.08/nb/s 達成時の推定値(sy*~0.94 mm)を記述

## Slide 8: Phase-1 Commissioning
K. Akai
Achieved beam current
870 mA (HER)
1010 mA (LER)
Tasks during phase 1 operation
Basic machine tuning
Vacuum scrubbing
Low emittance tuning
Machine studies on electron cloud effect, beam background, etc.
Phase 1 milestones: Feb. to June, 2016
Feb. 1: BT tuning started
Feb. 8: LER injection tuning started
Feb. 10: beam storage in LER
Feb. 22: HER injection tuning started
Feb. 26: beam storage in HER
2/1/2016
3/1
4/1
5/1
6/1
7/1
red: beam current
purple: vacuum pressure

## Slide 9: Vacuum Scrubbing
[HER]
[LER]
Base pressure: ~3x10-8 Pa
Max. beam current: 870 mA
Int. beam current: 660 Ah
Avg. Pressure: ~ 2x10-7 Pa
(arc sections) ~ 6x10-8 Pa
Lifetime ~ 400 min.
Y. Suetsugu et al.
Base pressure: ~5x10-8 Pa
Max. beam current: 1010 mA
Int. beam current: 780 Ah
Avg. Pressure: ~ 1x10-6 Pa
Lifetime: ~ 70 min.
(with Emittance control Knob ON)
The vacuum system worked well with newly introduced components.
Integrated beam currents satisfied requirement for Belle II roll-in.

## Slide 10: Low Emittance Tuning
Y. Ohnishi, H. Sugimoto et al.
permanent skew-Q to correct error field of Lambertson
skew-Q corrector coil on sextupole
Optics corrections have been worked successfully in both rings.
Tentative target of vertical emittance has been achieved in LER.
Measurements with X-ray monitor (XRM) give larger ey in HER.
  More calibration of XRM and larger by at RXM in Phase-2.
Phase1

## Slide 11: Renovation works for phase 2
SuperKEKB phase 2
colliding bunches
New e+ Damping Ring
e-
e+
Injector Linac upgrade
RF electron gun
improve e+ source
pulse magnets for top-up injection
QCS and related works at IR
DR arc section
RF cavities for DR
Add collimators
LER
HER
Renovation for phase 2 ongoing.
Change injection part for injection from DR
Collision feedback
More mitigation for e-cloud

## Slide 12: QCS system
N. Ohuchi, Y. Ohnishi et al.
SC correctors: a1, b1, a2, a3, b3, b4
SC leak field cancel magnets: b3, b4, b5, b6
設計で使用する2極補正コイルの磁場をできる限り小さくするためにQC1,QC2にオフセットを与えている。
大穂側
日光側
Belle ソレノイド磁場
大穂側
日光側
Bz
QC2LP QC1LP
QC1RP QC2RP
QC1RE QC2RE
QC2LE QC1LE
Bz 正方向

## Slide 13: Positron Damping Ring
M. Kikuchi et al.
Reverse bend FODO
for short damping times
11.5/11.7/5.8 ms

## Slide 14: Positron Damping Ring
DR and the extraction line
Arc cells of DR
RF system tuning with cavities started in Feb. 1.
DR
Ext. line
Installation phase-4
Beam pipes (ring) and vacuum pumps
Magnets alignment (coarse)
Cooling channels for magnets
Beam pipes at BT and Linac side
Installation of ECS and BCS cavities and waveguides
Installation of septums and kickers
Magnets alignment (fine)
Adjustment of power supplies
High power RF cavity conditioning
High power conditioning of ECS and BCS accelerating units
Evacuation of beam pipes
M. Kikuchi, K. Akai et al.
DR建設・立ち上げ調整は12月4日のビーム調整運転開始に向けて順調に進んでいる。

## Slide 15: MR各種作業（衝突点以外）_1
LER入射部、アボート部の改造
  DRからの陽電子ビーム入射に変わるため、セプタムおよび近傍の機器を改造。
  ビームサイズが小さく、かつビーム電流が高くなるため、アボートを改造。
コリメータ増強
  新型コリメータのPhase 1試験結果を受け、量産5台を現在製作中、10月頃納品予定。Phase 2に必要な8台がそろう。
  コリメータ周辺の放射線遮蔽評価を受け、シールド製作を開始した。
電子雲対策の強化
  Phase 2以降の電流増強に備えて、アークドリフト部（約1000m）への永久磁石の装着を昨年と今年で実施している。
Permanent magnets at drift space (with iron yoke)
New
HER D01
H5, H4, V1
New
LER D02
H4,H3,V1
e+
e-
Collimator system in Phase-II
Vertical collimator for Phase-II

## Slide 16: MR各種作業（衝突点以外）_2
より高い信頼性、性能向上のための、加速器ハードウェアの適切な保守・改良：特に、
  電磁石電源
  電磁石アラインメント
  大電力RFシステム、加速空洞
  冷却システム
  制御システム、など。
Phase 2 commissioning運転のツール開発
  運転用ソフトウェア
  タイミングシステム、など。
安全システムの改造
  ダンピングリングやAR直接入射路の新規稼働に必要なKEKB安全システムの改造

## Slide 17: Schedule
K. Akai
・・・
2016
JFY2016
2017
2018
2019
JFY2017
JFY2018
JFY2019
Japan FY
Calendar year
Summer shutdown
(power saving)
Summer shutdown
(power saving)
phase 1
phase 2 (MR)
phase 3
MR renovation for phase 2, including
installation of QCS and Belle II
w/o QCS
w/o Belle II
w/ QCS
w/ Belle II (no VXD)
w/ full Belle II
DR commissioning
DR installation & startup
MR startup
VXD installation
HER start
LER start
(mid Feb. – mid Jul. 2018)
Summer shutdown
(power saving)
Power saving
after mid July 2018
phase 3 operation
9 months / year
We are here.

## Slide 18: Summary
IR
  予定通り8月末にQCSの磁場測定を完了。QCS後退。
  今後のIR概略予定
    2017年9月〜12月上旬
    Belle II グループの作業（ARICHやBEAST IIのインストール等）
    QCS用ビームパイプの組み込み等
    2017年12月中旬〜2018年2月中旬
    QCS前進、衝突点加速器機器の再組み込み、立上げ調整等
    phase 2用の放射線シールド構築
    2018年2月中旬: MR phase 2 commissioning start
  より詳細かつ正確な工程の検討を、加速器とBelle IIグループで協力して進めている。
IR以外も、MRの各部署において、Phase 2に向けた各種改良や、今後の長期運転に向けた機器の維持・改善を順調に進めている。
12月4日DRビーム調整運転開始、2018年2月中旬MR Phase 2運転開始に向けて、現行計画に概ね沿って進行している。
K. Akai et al.

## Slide 19
backup

## Slide 20
要検討事項
キッカー、セプタム調整の具体化 キッカーは蹴り角を変えるとタイミングが変わる。 事前にできる対応策、用意すべきツールの検討。
アライメント結果の検討 ステアリングの定格内に収まっているか？
出射キッカーのタイミングジッターに起因するLINACでのビーム品質の劣化。
シフト体制 夜中はKCGシフトは付けない。 夜中は準夜の続き、真空焼き、LINAC調整、希望者のスタディ等に充てる。 １シフトは何人体制？ LINAC調整はどれくらい必要か？
H. Sugimoto et al.

## Slide 21
コミッショニング
期間: 2017年１２月４日 ~ 2018年2月中旬？(LTR,RTL調整も含む)
まずは1バンチ、1nC、1Hzで調整を行う。
まずはLINACの東側ビームダンプまでビームを通すことを優先する。
目標平均真空圧力 = 1x10^-5Pa 柴田氏の見積りでは2nC/bunch (2bunch, 2pulse)で４日程度かかる。
エミッタンスカップリングの目標値 = 10% シミュレーション上は軌道補正だけで達成できる。
夜中はKCGシフトは付けない。 準夜の続き、真空焼き、LINAC調整、希望者のスタディ等に充てる。
H. Sugimoto et al.
Notes: ビームは基本的には東側ビームダンプに捨てる。(<50nA)

## Slide 22
M. Kikuchi
Notes: Damping time (sec):
X : 1.153777E-02 Y : 1.173292E-02 Z : 5.878446E-03
Damping time [(turns)
X: 25527.527316355438