## Slide 1: Status of RF Accelerating Cavities for SuperKEKB Positron Damping Ring
Tetsuo ABE (KEK)
for SuperKEKB-RF / ARES Cavity Group
(T. Abe, S. Enomoto, T. Kageyama, H. Sakai, Y. Takeuchi, and K. Yoshino)
The 22nd KEKB Accelerator Review Committee Meeting
2018-03-14

## Slide 2: Contents
Overview and Fundamentals of the RF Accelerating Structure
Installation into the SuperKEKB Positron Damping Ring (DR)
Status of Cavity No.0 (prototype)
Summary

## Slide 3
1. Overview and Fundamentals of the RF Accelerating Structure

## Slide 4: Overview of the RF Accelerating Structure
Operational frequency: 508.9 MHz (CW) (same as for the MRs)
HOM-damped structure based on the successful ARES cavity system
Max. three cavities to be installed in a space originally designed for one cavity
  Max. total Vc = 2.4 MV to be supplied to the DR
“Multi Single Cell” structure
  Electromagnetic field in each cavity has high independence by the contribution the HOM absorbers between the cavities.
  Number of cavities is variable; Cavities are replaceable.
  Assembled in the DR tunnel like LEGO blocks
    One big mechanical structure with solid connections of the components
Vacuum pumps directly attached to each cavity
Design Parameters | 
Operational frequency | 508.9 MHz
Rsh/Q0 | 150 W
Q0 | ~30000
Cavity Voltage (DR spec) | 0.7 MV / cavity
Cavity Voltage (Cavity spec) | 0.8 MV / cavity
Wall-loss power @ 0.7 - 0.8 MV / cavity | ~110 - 140 kW / cavity
Blue region: vacuum during operation
Gray region: HOM absorbers (SiC ceramics)
e+
e+
e+
e+
1100
1100
Downstream
Cavity
Middle Cavity
Upstream Cavity
MR: Main Ring
HOM: Higher-Order Mode
SiC: Silicon Carbide

## Slide 5: Due to predicted CSR effects, the required acceleration voltage was increased fivefold!
(N.Iida)
RF section
CSR
Injector Linac
To supply an accelerating voltage higher than 1.4 MV to the DR in the limited space of a sole RF section, which was originally designed for one cavity, this RF accelerating structure has unique space-saving features ( next page).
(CSR : Coherent Synchrotron Radiation)

## Slide 6: Space-Saving Features
The HOM absorbers are all compact tile-shaped SiC ceramics (48 x 48 x 20 mm3).
The cavity is connected directly to grooved beampipes without bellows.
The HOM absorbers in the grooved beampipes absorb not only TE modes but also higher-order TM modes.
No additional HOM absorbers (such as SiC ducts) needed
E.g. SiC duct used at the MR / RF section
(280 mm long)
Fixed with 16 M12 bolts
Vacuum-tight lip welding at the outer periphery (“weld ring gasket”)

The neighboring cavities share a grooved beampipe in-between.
3.8 m

## Slide 7: HOM impedances of the RF section are low enough below CBI thresholds.
From wakepotentials calculated, using GdfidL, for the whole RF section
CBI thresholds were calculated for the DR design (8 nC / bunch).
Longitudinal
Transverse
(CBI: Coupled Bunch Instability)
Growth Time > 20 ms
> 5 ms (radiation damping time)
Growth Time > 30 ms
> 10 ms (radiation damping time)

## Slide 8: DR Cavities
No.2
No.1
No difference between No.1 and No.2 in the:
Electric design
Mechanical structure
Fabrication method
Low-power performance
High-power performance
0. Cavity No.0 (prototype) developed in JFY2011
  Surface protection of the endplates: acid cleaning followed by chromating
1. Cavity No.1 fabricated in JFY2012
  Surface protection of the endplates: Electropolishing (EP)
2. Cavity No.2 fabricated in JFY2013
  Surface protection of the endplates: Electropolishing (EP)

## Slide 9
2. Installation to the DR Tunnel
(November, 2016)

## Slide 10: Components of the RF Accelerating Structure for the DR
Downstream Cavity
Upstream Cavity
Upstream
End Beampipe
Downstream
End Beampipe
Upstream
Middle Beampipe
Downstream
Middle Beampipe
556
544
556
544
544
556
Dummy Pipe
544
Seven components (= two cavities + five beampipes) to be aligned 
e+
e+


## Slide 11: Into one big mechanical structure (3.8 m long)
3844 mm
10
e+
e+
Seven components (two cavities and five beampipes) to be aligned Connected

## Slide 12: Alignment Policy
Accuracy
  0.3 mm in the transverse directions
    Same as for the ARES cavities at the MRs
  (1.0 mm in the longitudinal direction)
What to be aligned: beam-port flanges (not cavities)
Beam axis defined by the quadrupole magnets next to the RF section (upstream and downstream)
Position measurement of the Beam-port flanges prior to the installation

## Slide 13: Position measurement of the beam-port flanges
Measurement range: 1.8 m (in diameter)
Five axes
Precision at a fixed point: 0.024 mm (spec)
FaroArm Edge
from KEKB monitor group 
using FaroArm Edge (portable CMM):

## Slide 14: Offsets of the component centers predicted from the measurement results using FaroArm Edge
We selected the best permutation
out of 2048 permutations of the components
to make the offsets as small as possible,
or to make the structure as straight as possible.
1 mrad unexpected bend
T. Abe, Y. Takeuchi, H. Sakai, T. Kageyama, K. Yoshino, M. Masuzawa, T. Kawamoto, “Installation of Normal-Conducting RF Accelerating Cavities into the SuperKEKB Positron Damping Ring”, in Proceedings of the 14th Annual Meeting of Particle Accelerator Society of Japan, 2017 (Paper ID: TUOL06).
For details on the algorithm to select the best permutation,
please see:
beam axis
beam axis
(Cavity No. 2)
(Cavity No. 1)

## Slide 15: We also measured distances between the 150-duct center and the reference planes of the beam-port flanges.
To be used in the position measurement after the installation
~245 mm
~150 mm
150

## Slide 16: We defined and marked the beam axis (horizontal).
Boundary
Boundary
Upstream Q-mag
Downstream Q-mag
The 22nd KEKB Review (2018-03-14)

## Slide 17: We defined and marked the beam axis (level).
Upstream Q-mag
Downstream Q-mag

## Slide 18: Connecting the grooved beampipes to the cavities
+
=
Viton O-Ring


## Slide 19: Alignment of the Beam-Port Flanges of the Cavities

## Slide 20: Then, we connected the dummy pipe.
Fixed with double nuts to avoid too much stress
Dummy pipe

## Slide 21: Position Measurement of the Beam-Port Flanges after the Installation
Using FARO Laser Tracker ION
From KEKB Magnet Group
to check the installation accuracy

## Slide 22: Redefined the beam axis based on the reference base plates of the Q-magnets
5660 mm
(Upstream)
(Downstream)

## Slide 23: Position Measurement using the laser tracker
Target Holder
1.5-inchi Reflector Target

M6 tap

## Slide 24: Two-step measurement
Upstream Cavity
Downstream Cavity
Q-mag
(upstream)
Q-mag
(downstream)
Meas. 1
Meas. 2

## Slide 25: Measurement using the laser tracker by Masuzawa-san and Kawamoto-san
(From KEKB Magnet Group)

## Slide 26: Combined with the measurement results using FaroArm Edge on the distances between 150-duct center and the reference planes of the beam-port flanges,
150
~245 mm
~150 mm
Using FaroArm Edge

## Slide 27: We obtain deviations of the beampipe center from the beam axis.
■ Meas. 1 (using the laser tracker)
▲ Meas. 2 (using the laser tracker)
★ Measurements during installation (using a laser marker)
- - - Theoretical prediction based on the beam-port flange meas.
(Inner)
(Outer)
(Top)
(Bottom)
We achieved an alignment accuracy of 0.3 mm as a whole!
beam axis
beam axis

## Slide 28: After all the installation works
Taken by Nobukazu Toge (KEK)

## Slide 29: High-Power RF Conditioning after the Installation
For two weeks from May 19, 2017
Only daytime, weekdays
Note: High-power RF conditioning of each cavity was completed at a test stand beforehand.
Break due to other works in the DR tunnel
Klystron Output Power (red) [kW]
Total Vc (blue) [MV]
Smoothly reached Total Vc = 1.6 MV (350 kW klystron output)
over the DR spec: total Vc = 1.4 MV

## Slide 30: However,
After maintaining total Vc = 1.6 MV (350 kW klystron output) during the conditioning,
small vacuum leaks (10-9 to 10-8 Pa m3/sec)
occurred at the 7 rectangular flanges of the HOM waveguides .
Possible cause is a thermal cycle
accompanied by high temperature
at the rectangular flanges
(~50 degC at max. for total Vc = 1.6 MV)
The vacuum leaks stopped by increasing the clamping torque except for one waveguide flange*.
(*The gasket was replaced, and then no leak)
HOM waveguide load

## Slide 31: Measures against thermal cycles
1. We added more cooling pipes on the E-bends of the HOM waveguides to suppress the thermal cycle at the rectangular flanges.
Cooling pipe brazed on the E-bend during the fabrication of the cavity
High thermal-conductivity glue (Devcon)
2. We inserted rubber bushes at the end of the support bars to make small degree of flexibility.
No vacuum leak since we took these measures
(last leak test performed on Feb.22, 2018)
(taken in Oct., 2017)
E-bend
Cavity
(EPDM)

## Slide 32
3. Status of Cavity No.0 (prototype)

## Slide 33: Cavity No.0 was used for Lip Welding Test in 2012.
We have demonstrated:
(1) It is possible to perform vacuum-tight lip welding in the DR tunnel after the installation of the cavities, and
(2) Lip welding  Leak test: OK  Disassembly -> Re-welding  Leak test: OK  Disassembly
Cavity No.0
Grooved beampipe (prototype)

## Slide 34: Cavity No.0 was re-tested on its high-power performance.
March, 2017
(1) Reached Vc = 0.90 MV (radiation limit) smoothly.
(2) Maintained Vc = 0.90 MV for six hours.
 Comparable performance with Cavity No.1 and No.2.
Conditioning Histories up to Vc = 0.90 MV/cavity
The light blue lines indicate the reference vacuum pressure specified by the computer controlled automatic aging.
If the vacuum pressure is higher than the reference, the input RF power (Pinp) is slightly stepped down until the vacuum pressure becomes lower than the reference, and then Pinp is slightly stepped up as long as the vacuum pressure is lower than the reference. Prefl and Vc indicate the reflected RF power and cavity voltage, respectively.

## Slide 35: We decided to promote Cavity No.0 to be a spare cavity for DR operation.
Enough high-power performance
Four HOM waveguide loads to be made soon
Bellows for vacuum-tight lip welding to be replaced

## Slide 36: Status of the Bellows of Cavity No.0
Blank flange
Upstream side
Downstream side
Grooved beampipe (prototype)
Cavity No.0
Grooved beampipe (prototype)
Used in the lip welding test performed in 2012
To be replaced by new one!

## Slide 37: Replacement Test of Bellows
(performed in 2017)
Using the grooved beampipe prototype
End mill
Bellows for vacuum-tight welding is welded
on a SUS frame.
Flange
The end mill revolved around the beam axis (14 rounds),
scraping the SUS frame (0.5 mm / round).
(0.5 mm / round)

## Slide 38: By End Milling
Before
After the 4th round
After the 14th round (last)
The bellows was removed after the 1st round.

…


…

Bellows for vacuum-tight welding
Flange
The SUS frame was completely removed.

## Slide 39
 No leak detected
New bellows (0.2mm-thick bellows welded on a SUS frame)
Lip welding test

## Slide 40: Summary
Cavity No.1 and No.2
  Were successfully installed to the DR tunnel / RF section
    ~0.3 mm accuracy in the transverse directions achieved
  Position measurement of the beam-port flanges prior to the installation was successful and useful.
  High-power performance re-checked: OK
  Now accelerating positrons without any serious problems
Cavity No.0
  To be promoted to be a spare cavity for DR operation
  High-power performance re-checked: OK
  Its bellows for vacuum-tight lip welding to be replaced by new ones this coming spring
  Will be a spare cavity during Phase II

## Slide 41
Thank you for your attention!

## Slide 42: Backup Slides

## Slide 43: 2  3 Cavity Configuration
Ultimate!
Starting with 2 cavities
(if necessary)
Total Vc = 2.4 MV at max. @ Phase III?
(0.8 MV/cavity)
Total Vc = 1.4 MV for nominal DR operation @ Phase II
(0.7 MV/cavity)

## Slide 44: The Endplates of DR Cavity No.1 and No.2 were Electropolished (EP).
Fixed End Plate (FEP)
w/o tuning bump
Tuning End Plate (TEP)
w/ tuning bump
  Before EP
f500mm
  Ra=0.2mm, Ry=1mm ( < d = 3mm)
  Ra=1.5mm, Ry=8mm
  After EP
Material: OFC (class1), 40mm etching, Skin depth(d)@500MHz: 3mm
(Upstream)
(Downstream)

## Slide 45: Low-Power Measurements of Unloaded Q-factor (Q0)
 | Q0(meas) / Q0(sim)
Prototype | 92.9%IACS
Cavity No.1 | 97.1%IACS
Cavity No.2 | 97.3%IACS
4% improvement with EP
(Note: No EP applied to the barrel)
of the coaxial-type input coupler

## Slide 46: Setup of High-Gradient (HG) Test
Toshiba
CW Klystron
E3732
(1MW, 508.9 MHz)
(No beam injected into the cavity during the HG test)

## Slide 47: Detection of Cavity Breakdown by the Decay Time in Pickup Signal
QL = ~13000 
The interlock system was activated with a reflection level over the threshold.
Check the decay time of the pickup signal of the accelerating mode
  ~8 ms  Not cavity breakdown
  << 8 ms  Cavity breakdown
T. Abe, T. Kageyama, H. Sakai, Y. Takeuchi, and K. Yoshino, “Breakdown Study based on Direct In Situ Observation of Inner Surfaces of an RF Accelerating Cavity during a High-Gradient Test”, Phys. Rev. Accel. Beams 19, 102001 (2016).

## Slide 48: Histories of the RF Conditioning
95 hours to reach Vc=0.90MV
107 hours to reach Vc=0.95MV
83 hours to reach Vc=0.90 MV
The light blue lines indicate the reference vacuum pressure specified by the computer controlled automatic aging.
If the vacuum pressure is higher than the reference, Pin is slightly stepped down until the vacuum pressure becomes lower than the reference, and then Pin is slightly stepped up as long as the vacuum pressure is lower than the reference.
Pin (Prefl) : input power to (reflected power from) the cavity
Wall-loss power: Pwall = Pin – Prefl = ~0.99 x Pin
Cavity No.2 reached 0.95MV/cavity successfully.
Comparable conditioning speeds btwn Cavity No. 1 and 2

## Slide 49: After the RF Conditioning (up to Vc=0.95MV) completed, Stability Test with Holding Vc = 0.90 MV
Cavity No.1: 3 breakdowns for 14.5 hours in total = 5.0+4.8-2.7 /24hrs
Cavity No.2: 11 breakdowns for 80 hours in total = 3.3+1.3-1.0 /24hrs
Example of the daily histories 
Same high-power performance between DR Cavities No. 1 and No. 2 within the statistics
> Vc = 0.70 MV
(required for DR operation)

## Slide 50: Radiation Dose Rate
= Indirect observation of the dark current:
Field emission
Acceleration
Impact on the inner surface
Emission of X-ray
No significant difference
between DR Cavity No. 1 and No.2
Constant during the stability test
(20 cavity breakdowns in this period)
for the DR Cavity No.2

## Slide 51: Permittivity of the SiC ceramic tiles
Relative permittivity of the SiC ceramics (CERASIC-B), as a function of frequency, used in designing this accelerating structure.
These permittivity values are typical measurements on the SiC ceramic tiles used for the GBPs of the ARES.
Typical Measurements of SiC ceramics
We aggressively controlled the permittivity by changing the amount of aluminum contained in the SiC powder so that the permittivity should be close to that used in designing the accelerating structure.
Permittivity of SiC ceramics largely depends on
Source SiC powders
Sintering conditions of SiC ceramics
Y. Takeuchi, et al., “Control of RF Dielectric Properties of SiC Ceramics for HOM Absorbers", in Proceedings of the 8th Annual Meeting of Particle Accelerator Society of Japan, Aug. 2011 (Paper ID: TUPS137)

## Slide 52
End of This File