## Slide 1: DR Vacuum
The 22nd KEKB Accelerator Review Committee
March 14, 2018
Kyo Shibata
(on behalf of KEKB Vacuum Group)
Inter-University Research Institute Corporation High Energy Accelerator Research Organization (KEK)
大学共同利用機関法人 高エネルギー加速器研究機構 (KEK)

## Slide 2
Contents
Overview
Construction
& NEG activation
Dynamic pressure
& Vacuum Scrubbing
Concerns
Summary
  “Updates of MR Vacuum system” will be presented by Suetsugu-san (3/14)
  “IR assembly” will be presented by Kanazawa-san (3/15)

## Slide 3
To SuperKEKB LER via Linac & BT
Large-emittance beam from Linac
Low-emittance beam
Overview
Vacuum system is divided into 7 sections by GVs.
  East arc sect. : SR monitor, FB monitor & kicker, DCCT, RGA
  West arc sect. : Inj. kicker, Ext. kicker
  South straight sect. : Ext. septum, Beam stopper for safety system
  North straight sect. : Inj. septum
  RF sect. : RF cavities
  LTR
  RTL
Target pressure : < 110-5 Pa
  Required beam lifetime due to residual gas scattering : > 1000 sec.
  Vacuum pumps : NEG & ion pumps
Beam energy | 1.1 | GeV
Bunch number | 4 | 
Circumference | 135.5 | m
Maximum stored beam current | 70.8 | mA
Maximum bunch charge | 8 | nC
Bunch length | 6.53 | mm
Bending radius | 2632/2967 | mm
Critical energy | 0.93/0.82 | keV
Total SR power | 7.2 | kW

## Slide 4
SR
SR
SR
Overview (Arc sect.)
Beam pipes for arc sections (Al alloy)
  Two types of beam pipes corresponding to B1&B2 magnets
    Each beam pipe covers one dipole, one quadrupole and one sextupole magnet.
  Designed to fit narrow spaces between the closely-located magnets
  Having BPM blocks, pumping ports, RF-shielded bellows, CF flange with RF contact
  Having antechambers on both sides of a beam channel to deal with SR which irradiates both side of the beam pipes and reduce beam impedance.
  TiN coating & grooved surfacing are adopted as countermeasures against ECE.
  Having water cooling channels on both sides of beam pipes
    Total SR power with design beam current (70.8 mA) : 7.2 kW
Layout of the beam ducts in one cell of the reverse-bend FODO lattice.

## Slide 5
Overview (Arc sect.)
Type II
1.2 m
1.5 m
Type I
Aluminum beam pipes for arc sections :
RF shielded bellows
RF contact on Conflat flange
BPM block
TiN coating
Space-saving connection flange
Cross-section
Pumping port
NEG
IP
TMP
Groove structure

## Slide 6
Overview (Arc sect.)
Pump location :
NEG
NEG
NEG
NEG
NEG
Ion pump, rough pump
Ion pump, rough pump
Type-I (1.5 m)
Type-I (1.5 m)
Type-II (1.2 m)
Type-II (1.2 m)
Two NEG pumps are installed in Type-I.
One NEG pump or ion pump is installed in Type-II alternately.
Distance between pumping ports : 0.7 m
Seff_NEG : 0.01 m3/s (10 L/s) for CO
Seff_IP : 0.008 m3/s (8 L/s) for CO
Type-II (1.2 m)
Pumping port (NEG & IP)

## Slide 7
Overview (straight sect.)
Beam pipes for straight section. (Al alloy)
  Much simpler than beam pipes in the arc sections.
    No antechamber
    No groove surfacing
    No water cooling channel
    Isolated bellows chambers instead of bellows part welded to the beam pipe
  Having different cross-sections to fit special components installed in the straight sections.
    Cross-sections of beam pipes change as smoothly as possible.
RF section | Circular | 150 mm
Feedback kicker | Octagonal | 62.8 mm (face-to-face)
Feedback monitor | Octagonal | 46 mm (face-to-face)
Inj. and Ext. kicker | Rectangular | 42 mm  37 mm
Inj. and Ext. septum | Circular | 41.2 mm
Adjacent area of the east arc section, etc. | Octagonal | 46 mm (face-to-face)
Example of beam pipe for the straight section
Isolated bellows chamber
Cross-sections of vacuum components in the straight sections.

## Slide 8
Overview (Control system)
Pressures are monitored by ion pumps.
  Number of IPs :
    East sect.; 11, West sect.; 11, North sect.; 4 + 4(septum), South sect.; 3
    Installation interval of IP :  6 m
  When the pressures exceed 110-4 Pa at several points at the same time in one section, the section is isolated by gate valves and beam injection is inhibited.
  One CCG is also installed in each section. (4 CCGs in DR, 1 CCG in LTR, 1 CCG in RTL)
  One RGA is installed in East arc section.
Temperatures of beam pipes are monitored.
  Number of monitoring points :
    East sect.; 13, West sect.; 12, North sect.; 4, South sect.; 1
  When the temperature exceeds 80C, an alarm is raised.
    Temperature rise due to beam operation has not been observed so far.
Flow rates of cooling water are continuously monitored.
  Water flows rate of every blanch is monitored by water flow switch. (10 blanches)
  When the flow rate falls below the threshold value, an alarm is raised.
    Since two flow switches occasionally malfunctioned due to the magnetic field from the magnet, they were wrapped in high permeability magnetic shield (Permalloy).
Thermometer
Flow switch wrapped in Permalloy

## Slide 9
Construction 1
Pre-installation works :
  Almost all beam pipes (105) were coated with TiN film (t200 nm) and baked (150C, 24 h) at the coating & baking facility in KEK.
    Not including ceramics pipes for Inj. & Ext. kickers, Ext. septum, special beam pipes for RF sections, FB monitor & kicker, DCCT, Inj. & Ext. septums.
    NEG pumps were activated during the baking.
    Not baked in-situ after installation.
Magnetron discharge sputtering
TiN coated beam pipe for arc sections
Coating & baking facility in KEK

## Slide 10
IP
Scroll pump
TMP
Construction 2
Installation works :
  The installation of the beam pipes commenced in May 2016 and finished in January 2018.
Evacuation from atmospheric pressure :
  Each section was evacuated by rough pumps (TMP + scroll pump) & ion pumps before and during NEG activation.
    When the pressure decreased to 10-4 Pa, ion pumps were operated.
    When the pressure decreased to 10-5 Pa, NEG activation was started.
    It takes about several days before NEG activation.
  After NEG activation, rough pumps were isolated by angle valves and removed.
Inserting beam pipe into B magnet
Connecting beam pipes
L type valve

## Slide 11
Heating power for NEG activation was controlled so that the pressure did not exceed 110-4 Pa.
  The pressure was monitored by ion pumps and vacuum gauges at manifold between TMP and IP port.
  Since the conductance of beam pipe and the conductance between pumping port and beam duct are small, the pressure in NEG port during activation is higher than measured value.
  It takes about 3 weeks from the start of evacuation to the end of NEG activation.
NEG activation
IP
IP on
Start of rough pumping
NEG activation (13 days)
Angle valves closed
Pressure (vacuum gauge)
Pressure (IP)
Current for NEG activation
Pressure during NEG activation (East arc section)
TMP
Vacuum gauge
Angle valve

## Slide 12
Pressure estimation
Pressure in the beam pipes was estimated by Molflow+ (Monte-Carlo Simulator developed at CERN)
  Model : 1 Type-I beam pipe + 1 Type-II beam pipe
  Pumps : 2 NEG pumps (0.05 m3/s) in Type-I, 1 ion pump (0.04 m3/s) in Type-II.
  Mass : 28, Temp. : 20 C, Thermal gas desorption rate : 110-9 Pam3/s/m2 = 110-11 mbarL/s/cm2
  PSD rate : =0 molec./photon (No stored beam)
CCG port
IP port
Average in beam channel
CCG port
IP port
Result is similar to the measured pressure before beam operation.

## Slide 13
Dynamic pressure 1
Beam operation started on Feb. 8th.
  Storage of beam started on Feb. 9th.
  The pressure exceeded 110-5 Pa, when the beam was accumulated for the first time.
1 bunch, 1 Hz, 1.5 mA
First storage day!!
Current [mA]

## Slide 14
Dynamic pressure 2
Beam current gradually increased and pressure gradually decreased.
  Maximum storage current reached 10 mA (4 bunch, 25 Hz) on Feb. 23rd.
Current [mA]

## Slide 15
Vacuum scrubbing has been progressing smoothly so far.
Vacuum scrubbing
East arc
West arc
Beam current
  Beam dose : 1 Ah =
  Photon dose 5.21022 photon/m

## Slide 16
Beam lifetime
Beam lifetime was larger than 1000 s when beam current was 10 mA.
  Operation mode : 4 bunch, storage mode
  Beam dose : 0.7 Ah (Photon dose : 3.61022 photon/m)
Lifetime
Lifetime
current
Pressure
Time [hh:mm]
Time [hh:mm]

## Slide 17
  110-5 molec./photon is required to obtain enough lifetime (1000 s) with design beam current (70.8 mA).
PSD rate estimation
Pressure in the beam pipes was estimated by Molflow+ (Monte-Carlo Simulator developed at CERN) to estimate PSD rate.
  Pumps : 2 NEG pumps (0.05 m3/s) in Type-I, 1 ion pump (0.04 m3/s) in Type-II.
  Mass : 28, Temp. : 20 C, Thermal gas desorption rate : 110-9 Pam3/s/m2 = 110-11 mbarL/s/cm2
  PSD : =110-4 molec./photon, stored beam current = 8.85 mA
    SR irradiates both sides of antechambers evenly.
NEG port
CCG port
IP port
Average in beam channel
The calculated pressure is close to the measured pressure.
(Pmeasured_CCG : 1210-8 mbar)
  110-4 molec./photon (beam dose : 0.7 Ah, photon dose : 3.61022 photon/m)
Almost as expected!!

## Slide 18
RGA data of the dynamic pressure was taken at the east arc section.
Main gas components at beam dose = 0.7 Ah
  H2 (beam current = 0 mA, PIP = 4.310-7)
  H2, CO, CH4, CO2 (beam current = 9.8 mA , PIP = 1.410-6)
    They are typical residual gas components in beam pipes irradiated by SR and evacuated by NEG.
Residual gas components
RGA
H2
CH4
CO
CO2
H2O
IP

## Slide 19
Concerns 1
Pressure rise during beam operation at a repetition rate of 25 Hz.
  Pressure at a repetition rate of 25 Hz is larger than that of 1 Hz.
    Vacuum scrubbing was performed by storage mode or at a repetition rate of 1 Hz, and time of beam operation at a repetition rate of 25 Hz is very short.
    It may be caused by the increase in the time stored with large-size beam.
    It seems there are places where only large-size beam can scrub.
  It is expected that the vacuum scrubbing of such places will progress during Phase-II operation.
25 Hz
1 Hz
1 Hz

## Slide 20
Concerns 2
Saturation of NEG pump
  Re-activation (conditioning) of NEG pumps is required when pumping speed of NEG pump becomes small.
  It takes several days to re-activate NEG pumps.
    DR can not be operated during re-activation of NEG pumps.
  There is no indication that the pumping speed of NEG decreases up to now.
  Re-activation will be performed during long shutdown. (this summer?)
Electron cloud issue
  Antechamber, TiN coating and Grooved surfacing are adopted as countermeasures against ECE.
  It is expected that electron cloud density integrated over the ring is 0.131014 m-2 by using TiN coating and antechamber (not including grooved surface) when stored beam current is 70.8 mA.
    Assumption : max of TiN coating = 1, photons irradiating beam channel/whole photon = 0.1
    Threshold of electron cloud instability : 1.41014 m-2
  Electron cloud instability will not occur in DR.
    It is necessary to continuously observe whether the ECE occurs or not as the stored beam current increases.

## Slide 21
Summary
Beam operation of DR started on Feb. 8th, and DR vacuum system have no problems so far.
Vacuum scrubbing has been progressing smoothly so far.
  The pressure in the beam channel is estimated to be less than 110-5 Pa with a stored beam current of 10 mA at present. (beam dose = 0.7 Ah)
  Currently, beam lifetime is larger than 1000 s when the stored beam current is 10 mA.
  It seems that vacuum scrubbing by beam operation at a repetition rate of 25 Hz is insufficient.
  10 times the beam dose is required to achieve enough lifetime (>1000 s) with design beam current (70.8 mA).
There is no indication of decrease in the NEG pumping speed.
  Re-activation will not be required until this summer shutdown.
As countermeasures against ECE, antechamber, TiN coating and Grooved surface are adopted.
  It is necessary to continuously observe whether the ECE occurs or not as the stored beam current increases.

## Slide 22
Fin.
Thank you for your attention.

## Slide 23
Back-up

## Slide 24
Average pressure estimation
Rough estimation of average pressure in arc sections
  Required averaged pressure is lower than 110-5 Pa to obtain enough beam lifetime.
  Beam pipes have three pumping ports in one cell with a length of about 2 m. (d  0.7 m)
  Two of them are for the NEG pumps and one is for ion pump.
    Average effective pumping speed will be 0.01 m3s-1 (just after activation) .
  Photon stimulated desorption by SR is major dynamic gas load during beam operation.
    After the sufficient scrubbing,  will drop to below less than 110-5 molec./photon.
  110-5 Pa with a stored beam current of 70 mA is achievable goal with sufficient scrubbing.
Stored beam current : 70 mA

## Slide 25
Average pressure estimation
Rough estimation of average pressure in arc sections
  Required averaged pressure is lower than 110-5 Pa to obtain enough beam lifetime.
  Beam pipes have three pumping ports in one cell with a length of about 2 m. (d  0.7 m)
  Two of them are for the NEG pumps and one is for ion pump.
    Average effective pumping speed will be 0.01 m3s-1 (just after activation) .
  Photon stimulated desorption by SR is major dynamic gas load during beam operation.
    After the sufficient scrubbing,  will drop to below less than 110-5 molec./photon.
  110-5 Pa with a stored beam current of 70 mA is achievable goal with sufficient scrubbing.