## Slide 1
RF GUN, LASER & ELECTRON BEAM COMMISSIONING
The 23rd KEKB Accelerator Review Committee
Rui Zhang 2019.07.09
Accelerator Laboratory Division V, Injector G

## Slide 2
SuperKEKB REQUIREMENTS
 | Electron HER 7 GeV | Positron LER 4 GeV
Normalized Emittance | 40 / 20 [μm] | 100 / 15 [μm]
Energy Spread | 0.07% | 0.16%
Bunch Charge at Injection Point | 4.0 nC | 4.0 nC
Stable electron beam with high charge and low emittance is required for SuperKEKB

## Slide 3
Requirements
4 nC electron charge generation
10 μm emittance preservation
Long term operation
Operating at 4 nC
Less space charge effect
  Longer pulse: 20-30 ps
Necessary strong focusing field
  Preserves the emittance
Stable long time operation
  Lower electric field: < 100 MV/m
Side coupler or Disk and washer is preferred
SuperKEKB RF Gun

## Slide 4
RF gun cavity: strong focusing electric field
Disk and washer (DAW): tested in 3-2
Quasi travelling wave side coupler (QTWSC): A1 primary RF gun
Cut disk structure (CDS): A1 secondary RF gun
04-17
S-band RF Gun System for SuperKEKB
Photocathode: long life time
Medium QE with long life time: 10-4~10-3 @266nm > 1 year
Metal composite: Ir5Ce
Laser: simple, stable with temporal and spatial manipulation
Laser active material pumped by laser diode
  Yb doped fiber & Neodymium (Nd) doped laser crystal: A1 ground laser hut
  Yb doped fiber & Ytterbium (Yb) doped laser crystal: A1 underground laser hut
Temporal and spatial reshaping for minimum energy spread and emittance

## Slide 5
05-17
Injector Section for SuperKEKB
Primary RF gun
QTWSC cavity
Adopted in this stage
1st milestone: full regular operation for the injection of HER (R4.3)
Thermionic gun
In the 2nd layer
Used for positron target, PF and PF-AR
Secondary RF gun
CDS cavity
Never used in this stage

## Slide 6
06-17
Photocathode in Primary RF Gun
Ir7Ce2 photocathode & QE map
y (mm)
QE(x,y)/QEMax
x (mm)
Novel type cathode plug in this stage
QE > 10-4 in off-line measurement (10-6 Pa)
QE = 10-5 in operation condition because of vacuum level (10-5 Pa)
Electron beam heating: the main cathode is bombarded by an accelerated electron beam
Successful heating over 1000 ℃
QE increased 3 times after cleaning
e-

## Slide 7: Current Nd/Yb Hybrid Laser System (R4.1)
Yb Single mode Fiber
Amplifier 1
Semiconductor optics Amplifier (SOA)
114 MHz  10 MHz
Yb Single mode Fiber
Amplifier 2
Menlo Orange 1 (1064 nm by SPM)
Menlo Orange 2 (1064 nm)
Home made ANDi type 1064 nm
EO Pulse Picker
10 MHz  1-50 Hz
Double bunch
Beam splitter 50:50
1st Nd:YAG Laser Line with 5 Stages Rod Amplifiers
YCOB in 1st Laser Line 1064 nm  532 nm
BBO in 2nd Laser Line 1064 nm  532 nm
Beam Polarizer
Combination for Two Laser Lines
Beam Polarizer
Division for Two Laser lines
BBO in 1st Laser Line 532 nm  266 nm
BBO in 2nd Laser Line 532 nm  266 nm
Fiber
Oscillators (114 MHz)
Fiber
Amplifiers
Nd:YAG Rod Laser
Amplifiers
Wavelength
Conversion
Yb Single mode Fiber
Amplifier 3
MEMS Switch
3 In 1 Out






Ground Laser Hut
 Tunnel RF gun box
Transporting Line for
Two Lasers (11 m long)




RF Gun
From Two Injection Windows

2nd Nd:YAG Laser Line with 5 Stages Rod Amplifiers
4 months 0 fault operation!
4 months 0 fault operation!

## Slide 8: Current Nd/Yb Hybrid Laser System (R4.1)
Yb Single mode Fiber
Amplifier 1
Semiconductor optics Amplifier (SOA)
114 MHz  10 MHz
Yb Single mode Fiber
Amplifier 2
Menlo Orange 1 (1064 nm by SPM)
Menlo Orange 2 (1064 nm)
Home made ANDi type 1064 nm
EO Pulse Picker
10 MHz  1-50 Hz
Double bunch
Beam splitter 50:50
1st Nd:YAG Laser Line with 5 Stages Rod Amplifiers
YCOB in 1st Laser Line 1064 nm  532 nm
BBO in 2nd Laser Line 1064 nm  532 nm
Beam Polarizer
Combination for Two Laser Lines
Beam Polarizer
Division for Two Laser lines
BBO in 1st Laser Line 532 nm  266 nm
BBO in 2nd Laser Line 532 nm  266 nm
Fiber
Oscillators (114 MHz)
Fiber
Amplifiers
Nd:YAG Rod Laser
Amplifiers
Wavelength
Conversion
Yb Single mode Fiber
Amplifier 3
MEMS Switch
3 In 1 Out






Ground Laser Hut
 Tunnel RF gun box
Transporting Line for
Two Lasers (11 m long)




RF Gun
From Two Injection Windows

2nd Nd:YAG Laser Line with 5 Stages Rod Amplifiers

## Slide 9: Stable & Efficient Nd:YAG Amplifier (R4.2)
09-17
High amplification efficiency with sample configuration
Lower pump currents by use of high dopant Nd:YAG crystals (2018 summer)
Trouble shooting in short time for stable and smooth commissioning
No problem occurred during stage (more than 4 months)
Input @1064 nm (<1 μJ)
Output
(10 mJ)
1st stage
2nd stage
3rd stage
4th stage
5th stage
Pockels cell
4 m x 0.8 m
Optical path: 22 m
Layout of Nd:YAG rod amplifier

## Slide 10: Two Lasers Injection Mode (R4.1)
2nd line
HWP
HWP
Polarizer
Delay line
11 m long
transporting line
A1 ground laser hut
Tunnel RF gun box
BBO
0o RF gun
90o RF gun
BBO
BBO
Flip mirror
HWP
Polarizer
Laser with vertical polarization, laser with horizontal polarization, HWP: half wave plate
1st line
10-17
e-
Possible to generate high e- charge
Better emittance
Backup for the smooth commissioning
Irradiated by two lasers

## Slide 11: Controllable and Monitorable Laser (R4.2)
1.3 nC
11-17
Temporary setup for laser beam shaping
Remote control
UV laser aperture
UV laser beam profile
CCD setup at the virtual cathode position
Net energy meter
Remote control actuators for fine adjustment (20 pieces)
UV laser beam profile
Optics layout in RF gun box
1st laser
2nd laser

## Slide 12: Laser Status Monitoring System
12-17
http://www-linac.kek.jp/ope/opelog2/opelog.html

## Slide 13: Electron Beam Commissioning (R4.2 & R4.4)
High Charge Test under Full Laser Energy
For
Commi-ssioning
Laser pointing stability at the virtual cathode position
SP_A1_G Charge
2856 MHz phase
>4 nC
2.8 nC
B-sector Wire Scanner 2019.06.27 1.2 nC @ SP_A1_G
4-wire ABCD: γεx=12.655 μm,
γεy=11.225 μm

## Slide 14: Stable & Continuous Operation in the Commissioning
14-17
More than 4 months stable and continuous regular injection (R4.3)
Comparable low injection background
Availability rate is 98.8% (MTBF: 394.1 h, MTTR: 4.6 h) (R4.3)
Different correspondence for different study by altering e- charge only a few seconds (R4.2)

## Slide 15: Updates (R4.1 & R4.2)
Install new Menlo fiber oscillator (1030 & 1064 nm) (2019 summer)
Photocathode development for higher QE (2019 summer)
  Ir7Ce2  Ir2Ce
Rebuild transporting line by use of relay imaging system (2019 summer)
Improve temperature stability in the laser hut (2019 summer)
Realize real time UV laser beam profile monitor (2019 summer)
  Available during continuous injection
New RF gun for better vacuum level and higher RF power (from 2020)
15-17

## Slide 16: Laser for Middle & Later Stages of Phase III
16-17
Laser temporal reshaping for low emittance, low energy spread, and injection noise suppression
t
I
t2
t1
t1
x
x’
t2
Phase space
Laser temporal distribution
Nd laser system: 17 ps
Yb laser system: 2.5 ps
t
I
t
I
Coherent pulse stacking technology by use of the birefringent effect of crystal
Demonstrated in Nd laser system (Supported by Dr. Honda in 2018, R4.2)
Due to the narrower spectrum width of the current Nd laser system (wider temporal width), the real rectangular shape is impossible (Fourier transform limit)
Yb laser system is the best and only candidate for low energy spread and low emittance electron beam generation in Phase III
 | 2019 Q1 | 2019 Q2 | 2019 Q3 | 2019 Q4 | 2020 Q1 | 2020 Q2 | 2020 Q3 | 2020 Q4 | 2021 Q1 | 2021 Q2 | 2021 Q3 | 2021 Q4
Nd Laser System | Primary laser for RF gun and HER injection |  |  |  |  |  |  |  | Backup laser system for SuperKEKB |  |  | 
Yb Laser System | Laser & monitoring system preparation with stacking |  |  |  |  |  | e- beam test |  | For RF gun and HER injection |  |  | 
t
E
Energy spread

## Slide 17: Summery
17-17
Continuous and stable full RF gun operation in this stage
Simple and precise laser and electron beam adjustment thanks to the available monitors and remote control components
Increase the stability of laser and electron beam
Will focus on improving the quality of electron beam by the Yb laser system
THANKS

## Slide 18: Backup

## Slide 19: Recommendations of the 22nd Review

## Slide 20: Plan
15-20
2019 summer: Improve stability of laser system and performance of photocathode
2020 summer (2019 winter): Improve the quality of electron beam
  Laser pulse temporal reshape: rectangular pulse shape
  Laser pulse spatial reshape: flat-top beam pattern

## Slide 21: Updates in 2019 Summer
Install new Menlo fiber oscillator
Rebuild transporting line by use of relay imaging system
Improve temperature stability in the laser hut
  Water cooling for optics table
  Exchange powerful air-conditioner
  Add insulation layer for the west wall of laser hut
Realize real time UV laser beam profile monitor
  Available during continuous injection
16-20

## Slide 22: Updates in 2020
Temporal reshape: Pulse stacking for low energy spread
Pulse stacking setup made by a crystal array
(birefringent effect of crystal)
Two stages stacking system made by YVO4 crystals
Input laser pulse with temporal Gaussian shape (FWHM~10 ps)
Output laser pulse with temporal rectangular shape (FWHM~40 ps)
Input Nd:YLF mode lock laser pulse with 9.4 ps FWHM width
Achieved laser pulse by stacking
* Supported by Dr. Yosuke Honda
17-20

## Slide 23: Updates in 2020
18-20
Spatial reshape: Diffractive optics element (DOE) for low energy spread and emittance
DOE with micro configuration as homogenizer
The homogenization is obtain with the sum of the
N*N sub-elements contributions
Simulation results: elliptical beam pattern
6 mm
3 mm

## Slide 24: Updates in 2020
19-20
Transverse reshape (spatial domain): Diffractive optics element (DOE)
  Two pieces of DOE are purchased (delivery date is September )
  One will be used for testing in 2020

## Slide 25: Wire Scanner Result @ 5 Sector

## Slide 26: Streak Camera Test Data by 2 Lasers
2 lasers mode
1st laser
2nd laser

## Slide 27: Statistics
MTBF (Mean Time Between Failure、平均故障間隔) MTTR (Mean Time To Repair、平均修理時間)
稼働率＝MTBF ÷ (MTBF+MTTR)

## Slide 28: Ir2Ce: Simple Test Result

## Slide 29
Yb:fiber/Nd:YAG laser in Phase II
Oscillator 1
Oscillator 2
Oscillator 3
Yb:fiber Amplifier
Nd:YAG 1st line
Nd:YAG 2nd line
Delay line
Transporting line
RF gun
High charge
Stable long time operation
~0.1 nJ
10 mJ (Amp factor: ~ 108 )
12-26
Stable long time operation

## Slide 30
Temperature stability for laser environment
Flexible silicon tube for cooling
19-26
Improvement of e- Stability in Phase III
Stable e-  Improved the laser stability by water cooling for optics table
Better stability for long time laser operation (fluctuation<5%)
Less adjustment for continuous e- generation
Laser output
Time
1st Amp
2nd Amp
3rd Amp
4th Amp
5th Amp
Two days laser operation history

## Slide 31
For High Quality e-
24-26
Laser Spatial Reshaping
Laser Temporal Reshaping
r
I
Laser spatial distribution
Phase space
x
x’
Linearity
Emittance
Laser beam shaper for flat-top
For Nd and Yb laser
Under purchasing
Pulse stacking by birefringent crystals
Demonstrated in Nd laser
Will be used in Yb:YAG laser for real flat
t
I
t2
t1
t1
x
x’
t2
Phase space
Laser spatial distribution
t
I
Yb:YAG laser
t
I
Nd:YAG laser

## Slide 32: Beam homogenizer
F: 1 m (Focal length of F lens)
Ф: 6 mm (on target surface)
Off-axis: 6 mm (distance between optical axis and center of target spot)
β≈1o

## Slide 33: Beam homogenizer
Simulation result
peak to valley modulations on the top hat: ±10%~15%
Transmitting rate> 80%

## Slide 35: RF-Gun for 5 nC
Space charge is dominant.
  Longer pulse length : 20 - 30 ps
Stable operation is required.
  Lower electric field : < 100MV/m
Focusing field must be required.
  Solenoid focus causes the emittance growth.
  Electric field focus preserve the emittance.
Total
Space charge
RF
Epaxial coupled cavity : BNL
Annular coupled cavity : Disk and washer / Side couple

## Slide 36: Required laser pulse energy
5nC
Ce2Te
ATF
Offline measurement
P-polarization
Offline measurement
S-polarization
Normal injection (old 3-2)
Inclined injection
Charge( C )
Laser power ( J )
QE=10-3
QE=10-4
QE=10-5
Current laser energy(500μJ)

## Slide 37
Field
Focusing field
Accelerating field
Focusing field
Field
Given force
Given force
Focusing field
Focusing
field
=> 集束力
Pill-box cavity
Annular coupled cavity with nose
Accelerating field
Accelerating field
Beam
Beam
Accelerating field
Accelerating field
Accelerating field

## Slide 38
Normal side couple structure
Quasi traveling wave sidecouple structure
Design of a quasi traveling wave side couple RF gun
Quasi traveling wave side couple has stronger focusing and accelerated gradient than DAW.
Long drift space is problem.

## Slide 39: Electron beam (EB) heating type cathode plug
【 RF shielding structure 】
Chart: Frequency (GHz)
EB heating is …
a main cathode is bombarded by an accelerated electron beam as a thermal source behind the cathode.
【Design of EB heating type cathode plug】
e-

## Slide 40: Heating Test
Heater Current (A) | 16
Heater Voltage (V) | 3.38
Intermediate electrode (V) | -25
High Voltage (kV) | 2.3
Beam current (mA) | 23
Beam Power (W) | 52.9
Surface Temperature (degC) | 1029
Heating a photocathode over 1000℃ by EB heating method was succeeded.
W wire (0.7φ)
【Experimental Setup & Results】
【Cathode plug】
Radiation
Thermometers

## Slide 41: YCOB CRYSTAL at LINAC
From Prof. YQ Zheng’s Slide, the 1st KEK and SICCAS nonlinear optics forum, Tsukuba, May 28, 2018

## Slide 42
Phase II Nd laser module