## Slide 1: Overview of Commissioning in 2021c - 2022b
December 13, 2022
Y. Ohnishi / KEK
The 26th KEKB Accelerator Review Committee

## Slide 2: Contents
Overview of 2021c and 2022ab beam commissioning
  Achievements in 2021c - 2022b
  Obstacles to luminosity improvement
  Procedure of increasing beam currents and number of bunches with safe way
Luminosity performance
  Specific luminosity
  Beam-Beam parameter
Stability of Machine
Beam Lifetime and Dynamic Aperture

## Slide 3: 2021c and 2022ab Run
injection kicker
accidental fires
in LER (Oct.28-Nov.5)
injection kicker
accidental fire
in LER (Mar.18)
2021c
2022ab
We reduced beam currents
after replacing the thyratrons
for their conditioning.

## Slide 4
 | Dec. 23, 2021c |  | June 8, 2022b |  | May 22, 2022b |  | Unit
Ring | LER | HER | LER | HER | LER | HER | 
Emittance | 4.0 | 4.6 | 4.0 | 4.6 | 4.0 | 4.6 | nm
Beam Current | 1015 | 797 | 1321 | 1099 | 744 | 600 | mA
Number of bunches | 1370 |  | 2249 |  | 1565 |  | 
Bunch current | 0.741 | 0.582 | 0.587 | 0.489 | 0.475 | 0.383 | mA
Horizontal size σx* | 17.6 | 16.6 | 17.9 | 16.6 | 17.9 | 16.6 | μm
Vertical cap sigma Σy* | 0.339 |  | 0.303 |  | 0.250 |  | μm *1
Vertical size σy* | 0.240 |  | 0.215 |  | 0.177 |  | μm *2
Betatron tunes νx / νy | 44.524 / 46.589 | 45.530 / 43.572 | 44.525 / 46.589 | 45.532 / 43.573 | 44.525 / 46.589 | 45.532 / 43.574 | 
βx* / βy* | 80 / 1.0 | 60 / 1.0 | 80 / 1.0 | 60 / 1.0 | 80 / 0.8 | 60 / 0.8 | mm
Piwinski angle | 10.7 | 12.7 | 10.7 | 12.7 | 10.7 | 12.7 | 
Crab waist ratio | 80 | 40 | 80 | 40 | 80 | 40 | %
Beam-Beam parameter ξy | 0.0433 | 0.0315 | 0.0407 | 0.0279 | 0.0309 | 0.0219 | 
Specific luminosity | 6.45 x 1031 |  | 7.21 x 1031 |  | 8.74 x 1031 |  | cm-2s-1/mA2
Luminosity | 3.81 x 1034 |  | 4.65 x 1034 |  | 2.49 x 1034 |  | cm-2s-1
*1) estimated by luminosity with assuming design bunch length
*2) divide *1 by √2
Machine Parameters : 2021c - 2022b

## Slide 5: Achievements until 2022 (1)
Peak luminosity : 4.65 x 1034 cm-2s-1 (4.71 x 1034 cm-2s-1 w/o Belle II data taking and HV OFF)
Integrated luminosity : 424 fb-1 (491 fb-1)
Peak currents : 1.46 A (LER) / 1.14 A (HER), 2346 bunches (2-bucket spacing)
: 1 mm (0.8 mm) << bunch length ~6 mm proof of the nano-beam scheme
Crab waist scheme has been applied (80 % in the LER, 40 % in the HER). luminosity improvement
Beam-Beam parameter : 0.035 at 0.7 mA (0.045 at 1.1 mA for small number of bunches as machine study)
Bunch-by-bunch FB tuning (gain, noise reduction) in the HER luminosity improvements
Bunch-by-bunch FB tuning (number of taps) in the LER suppress single bunch blowup, luminosity improvements
Chromatic X-Y coupling correction with rotatable sextupoles in the LER luminosity improvements

## Slide 6: Achievements until 2022 (2)
Long-term drift of QCS magnetic field (beta-beat) reduced by new QCS initialization procedure
Orbit deviation due to IP knob tuning (beta-beat) suppressed with QCS corrector (ZHQC2RP)
Increase of positron charge for the LER injection : 3 nC at the end of e+ beam transport line
2-bunch injection for the LER and HER improve injection efficiency (Bunch equalization is difficult.)
Adjustment of injection orbit in the HER (septum, kicker) improve injection efficiency (not enough)
Leakage orbit from injection kickers reduced by 60 % with additional inductance for the coils

## Slide 7: What Limits Luminosity Performance ?
Classification |  | Remarks | Items
A | A1 | Single-beam causes. Luminosity becomes lower as increasing bunch current. (single-bunch) | -1 mode instability
 | A2 | Single-beam causes. Luminosity becomes lower as increasing total current. (multi-bunch) | coupled-bunch, degradation of optics (linear parameters) due to beamline deformation
B |  | Single-beam causes, but interference of beam-beam interaction makes luminosity lower. | lattice nonlinearity (QCS fringe, chromatic X-Y couplings, etc.)
C |  | Pure beam-beam interaction limits luminosity. Beam-Beam limit, etc. | crab-waist, resonances, coherent beam-beam head-tail instability, parasitic collision

## Slide 8: Obstacles to Luminosity Improvement
Beam blowup in the LER (single beam, non-collision) : "-1 mode instability" (A1)
Sudden beam loss (both rings, more serious in the LER) "fireball hypothesis"
  Damage of collimator head and/or QCS quench if large beam loss
Optics degradation due to beam current dependence of beam orbit (A2)
  Orbit deviation at strong sextupoles is caused by beam line deformation due to intense SR heating.
Lower beam-beam parameter: 0.035 at 0.7 mA for physics run (0.045 at 1.1 mA) (B)
Short beam lifetime (dynamic aperture, physical aperture) : LER 8 min(1.25 A) / HER 25 min(1 A) nb=2346
Beam related background (optimization of collimators, QCS aperture and IR orbit)
Beam injection (small physical aperture of injection region, emittance growth in the beam transport line)
Earthquake : The beam aborts invariably. The becomes large in the HER. The optics correction is needed.
Lower online luminosity monitor during LER injection (Beam backgrounds affect the measured value.)

## Slide 9: Executive Summary from the 25th KEKB ARC Report
The most important challenges are:
  Top-up injection efficiency and injection stability, including HER beam blow up in the transfer line, mitigating the consequences of accidental kicker-pulser misfiring, problematic HER two-bunch injection, septum drifts, etc.
  Collimation and machine protection strategy, including overcoming the present bunch intensity limitations due to TMCI -1 mode instability; developing a strategy for safe beam current increase; and understanding and avoiding the as yet unexplained sudden large beam losses in the LER.
  Medium and long-term planning including possible upgrade paths; with an overall plan of increasing the beam currents, increasing the number of bunches, and lowering to maximize the luminosity.

## Slide 10: Accidental Fire of Injection Kicker in LER
2021c: We got several accidental fires in the LER at the early commissioning (Oct.28, Oct.30, Nov. 5). There is no accidental fire after the replacement of thyratrons and further conditioning.
Before starting 2022a, the thyratrons were rearranged and replaced with new one.
2022a: We observed large beam loss in the LER on March 18 due to accidental fire of injection kicker in the LER. Then, the collimator head of D06H3 was damaged (broken). The thyratron was replaced and conditioned.
2022b: No accidental fire of the injection kickers
Accidental fire of injection kicker is caused by a lack of the thyratron conditioning or early failure.
If we use a well conditioned thyratron, there will be no accidental fire.
There is no accidental fire in the HER even though the applied voltage is higher than the LER. The thyratrons in the HER are well conditioned.
Robust Low-Z (C) head is installed into D06H3 collimator during LS1. (used as the spoiler)
D06H1 on the upstream side is moved to the downstream side (D06H4) to collimate beam scattered by D06H3.

## Slide 11: No Fatal Accident due to Large Sudden Beam Loss in 2021c
1.2 A
0.7 mA/bunch
2021c
Sudden Beam Loss
in HER
Sudden Beam Loss
in LER
We had sudden beam loss for both rings.

## Slide 12: QCS Quench and Collimator Damage due to Sudden Beam Loss in 2022ab
2022ab
QCS (LER) quench
collimator damage
D06V1
D02V1
D06V1
D06V1
D06V1
D06V1
D02V1
1.2 A
0.7 mA/bunch
D09V1
D09V1
June 3
D06V1, D02V1
June 11
D09V1
We introduced Matsuoka Limit to avoid sudden large beam loss
which causes QCS quench and collimator damages as much as possible.
Sudden beam loss becomes a serious problem to increase total beam current.
D06V1
deviation from plan

## Slide 13: Luminosity Performance

## Slide 14: Specific Luminosity
"estimated" means is calculated by the horizontal orbit deviation
at SLY(strong sextupoles) in HER due to beam-line deformation.
Luminosity drop
is too steep.
20 %
12 %
The geometrical
luminosity
is good.

## Slide 15: Specific Luminosity
The definition of specific luminosity:
It was found that even if the setting is 1 mm, can be shifted due to beta-beat caused by a deviation of the horizontal beam orbit at the strong sextupoles in the local chromaticity correction.
  The orbit deviation is caused by beam line deformation due to intense SR heating.
  This effect is more significant for the HER rather than the LER.
Higher specific luminosity for = 0.8 mm is obtained at a bunch current product of 0.05 mA2, but the specific luminosity rapidly decreases around 0.1 mA2.
  Lsp for = 0.8 mm is about 20 % higher than 1 mm at 0.05 mA2 and decreases to about 12 % at 0.1 mA2 and above.
This implies that the corrections of the chromatic X-Y coupling and other parameters are not optimized yet for = 0.8 mm which affect beam-beam blowup.

## Slide 16: Chromatic X-Y Coupling Correction with Rotatable Sextupoles in LER
working point
Rotatable sextupoles:
M. Masuzawa, T. Kawamoto et al.
March 14, 2022
Dec. 20, 2021
SLYTLPs and SLYTRPs were not used here.
single beam
single beam
The rotatable sextupoles (6 families for right and left side of IP) are
used to make the first synchro-beta coupling resonance weak
together with the second resonance.
is optimal.

## Slide 17: Beam-Beam Parameter
The current
ratio : 6.5/4
HBC = High Bunch current Collision
2021c
2022ab
2022a HBC
(nb = 393)
physics run
physics run
~ 0.045 at Ib+ = 1.1 mA
~ 0.035 at Ib+ = 1.1 mA
Beam-Beam parameter has been improved compared to the 2021c run for higher bunch currents.
The chromatic X-Y couplings (r1' and r2') are corrected in the LER.

## Slide 18: Beam-Beam Interaction
Lower beam current in the HER tends to cause beam blowup.
This means that the HER beam size is more easy to blow-up when the beam current of the HER decreases.
The beam current of the HER is larger than the energy ratio (4 GeV / 7 GeV).
The optimum ratio of LER to HER beam current is 5:4 from luminosity tuning.
The beam-beam parameter of the LER are larger than that of the HER.
The current ratio is kept constant for daily operation in principle.
The beam-beam parameter is sluggish with LER beam currents of around 0.6 ~ 0.8 mA.
Vertical beam-beam parameter (from luminosity)
Vertical beam-beam parameter (incoherent)
nominal bunch length

## Slide 19: Contribution from Bunch Length
LER
design bunch length
design bunch length
bunch lengthening
Ib+ : Ib- = 5 : 4
beam blowup
HER

## Slide 20: Stability of Machine

## Slide 21: Stability of Beam Orbit
Control of beam orbit as well as stability is very important.
The beam orbit cannot be considered in isolation from the beam optics.
BPM gain calibration is performed before optics correction, Quad-BPM (BBA) is sometimes performed if necessary (after cabling work of BPMs).
Optics correction is scheduled every two weeks (maintenance day) or when we found luminosity degradation. Magnet initialization is performed every maintenance.
We set the reference orbit, so called "GOLD orbit" when the optics correction is performed. But it is difficult to adjust a measured orbit to the GOLD orbit in several days after the registration.
  Residual of measured orbit from GOLD orbit is typically 30 . This is not enough to keep optics stable.
  Beam position at the strong sextupole is important to correct X-Y couplings and vertical dispersions.
  Degradation of consistency, beam-line deformation, change of BPM cable length due to temperature at day and night, etc.
There are many sources to induce orbit fluctuation. Cooling water cycle, all environment as well as earthquake
Moreover, SR becomes intense and the heating might deform the beam-line. Difficulties arise how to treat of the orbit.
Orbit in the vicinity of the IP is not well understood as well as QCS magnetic field.

## Slide 22
A
B
B - A
A - GOLD
B - GOLD
Estimated orbit at the IP
LER
We can correct B-A, but neither A-GOLD nor B-GOLD can be corrected.
The difference between the measured orbit and the GOLD orbit becomes large in several days after optics corrections.

## Slide 23: Residual of Measured Orbit from GOLD Orbit in 2022ab
HER
LER
optics correction,
GOLD is registered.
/users/onishi/svn-work/SuperKEKB/operation/2022ab/momentum
optics correction,
GOLD is registered.

## Slide 24: Beam Lifetime and Dynamic Aperture

## Slide 25: Lifetime Evaluations in LER
Assuming constant gas pressure and beam emittances during the measurements, the fitting out lifetimes (w/ bunch current of 1 mA) are
Lifetime (sec) |  | 
 | Ib = 0.6 mA | Ib = 1 mA
original | 843 ± 14 | 716 ± 7
Yunhai | 825 ± 14 | 662 ± 8
B2 | 761 ± 13 | 596 ± 8
Optics parameters (I= 50 mA, 1370 bunches) |  |  |  |  | 
 | (Δβ/β)y [%] | Δηy [mm] | εy [pm] | ξx/y | IP knobs
original | 4.2 | 4.5 | ~20 | -1.24/3.58 | ≠0
Yunhai | 5.3 | 3.7 | ~20 | -1.24/3.66 | 0
B2 | 6.5 | 7.9 | ~20 | 0.1/1.9 | 0
2021c
Vertical emittance is uncertain at high bunch current
due to beam blowup (-1 mode instability).
is not a straight line,
it is different between lower
and higher than 0.6~0.7 mA.
We tested three different kinds of sextupole settings in the LER. (Original, proposed by Y. Cai, B2)
Single bunch current was measured by DCCT.
No information of beam size from XRM.
(1/s)
Bunch current (mA)

## Slide 26: Simulation of Dynamic Aperture in the LER
B2
Emittance:
Yunhai
without collimator aperture (QCS only)
Original
The Touschek lifetime is evaluated by an ellipse inscribed in the dynamic aperture (stable region).
initial phase = 0,
There are various methods of evaluation and lifetime depends on the method from DA.
Vertical emittance is uncertain at 1 mA bunch current (larger than 20 pm or bunch lengthening).
larger momentum acceptance than original
too short lifetime
300 sec @ 1 mA
Crab-Waist : 80 %
Lifetime (sec) |  | 
 | Ib = 0.6 mA | Ib = 1 mA
original | 843 ± 14 | 716 ± 7
Yunhai | 825 ± 14 | 662 ± 8
B2 | 761 ± 13 | 596 ± 8
8.2 min
6.3 min
8.5 min

## Slide 27
60 pm
22 pm
collision
single beam
nb:1174
nb:393
1174
25 pm
45 pm
28 pm
collision
single beam
nb:1174
nb:393
1174
40 pm
30 min
8 min
7 min
6 min
32 min
26 min
LER
HER
 | LER | HER
βx* | 80 mm | 60 mm
βy* | 1 mm | 1 mm
I | 800 mA | 650 mA
nb | 1174 | 1174
Ib | 0.681 mA | 0.545 mA
εy collision | 60 pm | 45 pm
εy single | 25 pm | 40 pm
life collision | 8 min | 30 min
life single | 6 min | 32 min
Lifetime
ver. emittance
current
εy depends on bunch current.
Beam Lifetime and Vertical Emittance
e+inj: 2.3 nC x 2 x 12.5 Hz x 80 %
Imax= 1.5 A for lifetime: 8 min
2021b

## Slide 28: Simulation of Dynamic Aperture and Lifetime
Open and close the collimator uniformly from the nominal setting to examine the change in lifetime.
Horizontal
DA ~ PA
Vertical
DA > PA
8 min
(meas. 6 min,
vac. lifetime inc.)
LER
Vertical
DA < PA
The simulation is
almost consistent with measurement.
Dynamic aperture is
smaller than what
we expected ?
Horizontal
DA > PA
Or machine error ?
Zero means the nominal setting for the collimators.
HER
52 min
(meas. 32 min,
vac. lifetime inc.)

## Slide 29: No Summary
-1 mode instability | K.Ohmi | "Impedance issues (BxB FB, etc.)" | Dec. 14
Sudden beam loss | H. Ikeda | "Sudden Beam Loss" | Dec. 14
Optics degradation and others | H. Sugimoto | "Optics issues" | Dec. 14
Beam-Beam simulations, interference of lattice nonlinear, etc. | D. Zhou | "Beam-Beam, comparison of Beam-Beam interaction between simulations and experiments" | Dec. 14
Collimators | T. Ishibashi | "Collimator issues" | Dec. 14
Issues of beam injection | N. Iida | "Injection" | Dec. 13

## Slide 30: Appendix

## Slide 31
Chart: 2019 a/b
| Physics Run | Machine Tuning | Machine Study | Troubles | Maintenance, Others
2019a/b | 1090.5 | 836.5 | 118.5 | 652 | 239
Chart: 2019 c
| Physics Run | Machine Tuning | Machine Study | Troubles | Maintenance, Others
2019c | 480.5 | 725.5 | 0 | 311.5 | 205.5
Chart: 2020 a/b
| Physics Run | Machine Tuning | Machine Study | Troubles | Maintenance, Others
2020 a/b | 1809 | 838.5 | 28 | 165.5 | 208
Chart: 2020c
| Physics Run | Machine Tuning | Machine Study | Troubles | Maintenance, Others
2020 c | 645.7 | 828.2 | 0 | 212 | 78.6
Chart: 2021a/b
| Physics Run | Machine Tuning | Machine Study | Troubles | Maintenance, Others
 | 2429.63 | 537.16 | 61.367 | 201.36 | 106.466
Chart: 2021 c
| Physics Run | Machine Tuning | Machine Study | Troubles | Maintenance, Others
2021 c | 929.86 | 362.51 | 148.61 | 69.15 | 47.48
Chart: 2022a/b
| Physics Run | Machine Tuning | Machine Study | Troubles | Maintenance, Others
2022 a/b | 2091.45 | 436.14 | 150.18 | 114.41 | 109.79
Operation statistics
2019 -2022

## Slide 32: Vertical Beam Size at IP
normal coordinate
(decoupled coordinate)
physical coordinate
Vertical emittance, vertical dispersion, coupling parameters r1 and r2 at the IP are fundamental parameters for luminosity performance.
X-Y couplings

## Slide 33: Beam-Beam Parameters
Vertical beam-beam parameter
Vertical beam-beam parameter (incoherent)
Here, the nominal bunch length is used.
Beam-Beam parameter
appears to be saturated
at 0.6 mA.
Bunch lengthening is important parameter.
single beam
emittance
2022ab

## Slide 34: Beam Size in 2021c
2021c HBC
2021c HBC
ΔR1', LER νy
bunch current product
bunch current
2021c
2021c
lower in the LER
lower in the LER
4.5 nm
3.6 nm
6.0 nm

## Slide 35
Collimators and Radiation Dose (measured on June 22, 2022)
Location of Movable Collimators
measured by Radiation Safety Group
e+
IP
Injection
Point
e-
Injection
Point
LER
HER
17 m
D06H3
D02H3
D12V4
D09H1
D06H3 damaged
due to accidental fire of
injection kicker on March 18
D02H3 is 17 m downstream of D02V1
which is damaged on March 11.
The radiation dose at the injection point is very high in HER.
The bottom jaw of D06V1 was opened from the usual setting due to
damage of the collimator head. In stead of D06V1, D06V2 was used to
protect D02V1 and QCS from mid. of June.

## Slide 36: Local Chromaticity Correction: Strong Sextupoles (SLY)
HER
LER
K2: -8.76 1/m2
K2: -9.62 1/m2
K2: 8.36 1/m2
K2: 7.66 1/m2
K2: 1.23 1/m2
K2: 3.48 1/m2
K2: 1.33 1/m2
K2: 3.53 1/m2
~0.0028 for
~0.01 for
Horizontal orbit in-phase for each pair
induces large beta-beat which changes .
-I'
-I'
-I'
-I'
3.6 times larger than LER
Horizontal tune shift can be ignored.
Right-side
Left-side
Right-side
Left-side

## Slide 37: Beta-Beat due to Orbit Deviation
H. Sugimoto, 2022ab Summary Meeting
The SR heating deforms the beam line.
The horizontal orbit deviation induces tune shift and beta-beat. As the result, also changes.
The orbit deviation in the local chromaticity correction (SLY) is always in the outward direction of the ring.
This implies a squeezing of .
The HER is larger effects rather than the LER.
In order to reduce optics degradation, the local bumps correct the orbit at the strong sextupoles.
  (Horizontal bump for beta-beat and vertical bump for X-Y couplings)

## Slide 38
18:50 - 23:10, October 26, 2021
nb: 393
nb: 783
nb: 978
nb: 1565
The bunch current is fixed to be 0.2 mA.
reference
reference
tune shift due to
resistive wall
impedance:
(no crab waist)
HER
corrected value
Measurement of Resistive-Wall Tune Shift

## Slide 39
CW 80 %
CW 0 %
Horizontal dynamic aperture is reduced by the crab waist scheme.
QC1
QC2
AQC1: AY =18.0 mm
AQC1: AY =13.5 mm
AQC1: AY =20.0 mm
is determined by the physical aperture of QC1 and QC2
Tested three different
vertical apertures for
QC1
If the vertical physical aperture of QC1P is increased to 17 mm, the stable region is extended in the small horizontal amplitude.
(Above 17 mm is limited by the dynamic aperture.)
Collimators : full open, QCS aperture only
Dynamic Aperture in the LER
initial amplitude at injection point

## Slide 40: Intra-Beam Scattering in LER
Ib = 0.6 mA