## Slide 1: BT
M. Tawada, K. Kikuchi, K. Kodama, T. Mimashi, T. Mori,
T. Naito, T. Takasaki, S. Terui and T. Ueda
(BT group)

## Slide 2: Contents
To improve injection efficiency
BT hardware issues and updates
Upgrade plans in BT
Summary

## Slide 3: 1. To improve injection efficiency
  Injection orbit changes and re-alignment at BT ARC4
  Field quality improvement of HER Septum 1
  Injection aperture improvement for HER

## Slide 4
Green: design
Red: misalignment of quads
Blue: misalignment of bends
0.046 mrad
Survey results for magnets of the Electron BT and HER quadrupoles in the injection region (2018)
ARC4
Slope
HER
HER line is inclined relatively to the BT design by .
Quadrupole of HER at the injection point (QI4E) has relative offset to the design by
Final quadrupole in the BT has misalignment of
Findings:
Countermeasure:
Septum angles were adjusted to absorb the relative misalignment to the current HER line.
During LS1, re-alignment will be performed for the four quadrupoles which have large misalignment greater than 1 mm.
 | mrad | mrad | SKB-design
SE1 | 38.60 | 44.59 | 39.49
SE2 | 37.82 | 28.08 | 35.35
SE3 | 36.01 | 37.5 | 37.5
SE4 | 35.24 | 37.5 | 37.5
Sum | 147.69 | 147.69 | 149.84
Example of septum angle adjustment
QI4E
Injection orbit changes and re-alignment of BT e ARC4 (Kikuchi)
e-

## Slide 5
Survey results for magnets of the Positron BT and LER quadrupoles in the injection region (2018)
ARC4
Slope
LER
Green: design
Red: misalignment of quads
Blue: misalignment of bends
Both of BT line and LER have misalignment by .
Relative positions between BT and LER are almost correct.
Findings:
Countermeasure:
Design of BT line was adjusted to match the misalignment of BT. Bend angle of ARC4 was adjusted by .
Residual misalignment to the new design will be corrected.
Septum angle are adjusted to match the current position of the injection quadrupole (QI6P).
QI6P
Injection orbit changes and re-alignment of BT p ARC4 (Kikuchi)
 | mrad | SKB-operation July 2021*)
SP1 | 53.105 | 54.057
SP2 | 44.129 | 44.090
Sum | 97.234 | 98.147
*)
Septum angle adjustment
e+

## Slide 6
HER Septum 1: Field quality improvement (1) (Mori)
It has been found that a fringe field near the septum plate has a sizable multipole component. A tracking simulation shows multipoles induces a vertical non-Gaussian tail, which could be a cause of a beam background as well as a bad injection efficiency.
Adjustment of Q-magnets at upstream of the BT line for optics matching does not work completely for non-linear components.
Improving the field quality of HER septum 1, which is nearest one to the injection point is important for injection efficiencies and backgrounds.
Field quality would be improved by (1) reducing the pulse width of 300 → 257 μs by changing power supply’s main capacitor and (2)Fine tuning of shim shape for the reduced pulse width.
HER injection amplitude could be reduced from 11 to 8 mm in total.
  2mm (by field improvement of septum magnet) + 1mm (by injection aperture improvement) could be reduced.

## Slide 7
HER Septum 1: Field quality improvement (2) (Mori)
Issue for fabrication
  We noticed the silicon steel plate ( JFE 0.35mm inorganic coating) used so far are not available any more. Another candidates (0.15 mm inorganic coating or 0.35 mm organic coating) are found but it must be evaluated for punching accuracy and outgas performance.
  Therefore, the fabrication is delayed and installation will be scheduled in summer 2024.
Simulation studies are performed and we decided shim shape as shown in the lower left figure: the flat top width h=0.24 mm, wtop=0.06mm.

## Slide 8
HER injection orbit and the chamber wall
Injected beam
Stored beam
Septum
In the current configuration the injected beam is expected to touch the quad chamber before it touches the septum wall.
Very high residual radiation-activity, which was found at the flange of the “Injection BPM” chamber, supports this hypothesis.
Kicker orbit changes cannot avoid this geometrical conflict because it interferes with the constraint from the abort orbit.
A new chamber for QI4E was designed which has enough clearance to the injected beam (see Vac-group report).
Ideal wall shape to minimize the injection amplitude
Injection Slit
QI4E
Injection BPM
The “ideal shape” of the chamber wall was partially incorporated in the new design, which minimize the injection aperture.
If the “ideal shape” is realized injection aperture will decrease from to .
Injection aperture improvement for HER (Kikcuhi)

## Slide 9: 2. Hardware issues and updates
  LER kicker issues
    Leakage of LER injection bump orbit
    self-firing troubles of thyratron tube
  DR extraction kicker stability issue
    DR kicker temperature stability improvement
    Temperature stability improvement of facility cooling water
    Fast kicker for 2nd bunch in RTL
  Monitor upgrades
    BT-BPM
    Radiation profile monitors (BT-SRM, Screen)
    CSR monitor

## Slide 10
LER Kicker: Leakage of LER injection orbit bump (Kodama and Mimashi)
K1(left) and K2(right) duct shape
Leakage of LER injection orbit bump was observed by BOR while kicker’s current waveforms are almost same between K1 and K2. The horizontal oscillation is coupled to the vertical. This may cause the luminosity degradation.
Leakage kick might comes from the differences of ceramic duct shape and Ti coating thickness.
We have tried to expand K1 current waveform with additional inductance of 550 nH in series. But the leakage couldn’t be reduced as we expected.
Need to manufacture new K2-type ceramic ducts and replace K1 ducts to new one in 2024. (The budget was not allowed in 2022.)
Ti coating: 1.5 um
Ti coating: 5.0 um
Expand wave
Additional inductance effect for K1 CT wave
Additional inductance effect for BOR

## Slide 11
LER kicker: Self-firing troubles and coutermeasure (Kodama, Naito and Mimashi)
Self-firing troubles in 2021-2022
  By using the thyratron which had been stocked for a long time but new one, self-firing had been occurred several times.
  Self-firing of new thyratrons recently purchased had also occurred.
Countermeasure for self-firing
  Prepare test stand for incoming inspection and aging of thyratrons.
  R&D of the double kicker driven by one thyratron unit.
    Double kicker has different output between K1 and K2 due to different cable length to make the time delay. K1:K2 ratio will be fixed for the double kicker. If optics accepted this condition, we will continue to design double kicker system.
Schematic image of double kicker system
Kicker1
Kicker2
7 m
Tdelay = 80 nsec
(5 nsec/m)
Transmission line
23 m
Thyratron unit
Simulated Kicker waves for double kicker system(1)

## Slide 12
DR ext. kicker stability (Tawada)
1 hour
Slow orbit drift was observed at the Linac BPM. These orbit drift changes when the repetition changed, which is more prominent in the 2nd bunch.
It takes long time to reach the equilibrium for the high repetition rate (> 2 hour for 12.5Hz).
This may be due to the temperature dependence both of capacitance and FINEMET core, which is used as a saturable inductance in the magnetics switch and thus determines the fire timing. We will replace the capacitor from a ceramic to a mica type, which is less temperature dependent. And cooling system of FINEMET will be improved by using a water-cooled forced circulating oil.
Ceramic capacitance
〜0.8%/℃
Mica capacitance
〜100ppm/℃

## Slide 13
Temperature stability improvements of facility cooling water (T. Naito)
The temperature control parameters of the facility cooling water were optimized. In order to minimize the temperature change, the on/off temperatures of the cooling towers are set to different value and the PID parameters of the three-directional valve are set to the long interval.
Before improvements
After improvements
DR magnet (M22-B cooling water)
The temperature change was reduced from 2deg to less than 0.5deg. The most of time, the temperature kept to 0.1 or 0.2 deg.
The other region of the the facility cooling water in BT, KEKB-BT magnet (AS-PWP-5 cooling water) and Septum magnet (FM-PWP-3 cooling water) can be stabilized by using same method.
2℃
Less than 0.5℃

## Slide 14
DR-RTL: Fast Kicker (Naito and Kodama)
DR-RTL fast kicker
It takes time to adjust kick angles (〜5mrad) of two bunches extracted from DR, because two successive kicker pulses are overlapped each other and they are interrelated in the fire-timing as well as in the pulse height.
Installed a fast kicker system to kick 2nd bunch only to RTL.
  Stripline kicker for ATF (L=0.33m) are reused and PS are newly built.
  Kick angle: 0.14 mrad with ±8kV, pulse width:20ns, Horz./Vert.
  Kick angle could be larger if longer kicker is used.
Before EVR change
w/o SL kicker
with SL kicker
After EVR change
Stripline kicker test with beam
DR extraction kicker
20ns
96ns

## Slide 15
Old BT-BPM Oscilloscopes
  Eight old oscilloscopes (Tektronix DPO7104, 4-ch, 1 GHz, 8-bit) have been used for BT-BPMs since 2007 and hardware troubles have occurred several times.
  Those should be updated and Rhode & Schwarz RTO2014 (4-ch, 2 GHz, 10-bit), which was only one candidate and can work at 50Hz repetition rate but it was sold out last year. We are looking for a oscilloscope or digitizer which meets the required specifications.
  Some BPM must be re-cabled not to make the 2nd bunch signals overlapped each other.
Libera SPE
  Libera SPE will be ready for BPMs at BT end of e-/e+ lines, which have direct cables , during next run.
  It can receive EVR data buffers and change parameters by event code (31=e-/41=e+) and mark it by ShotID.
  Switching of e-/e+ is performed by RF switch, which is prior to Libera SPE.
BT-BPM status: (Mori)

## Slide 16
BT-SRM (Synchrotron Radiation Monitor): (Mori)
SRM for e- was installed at the beginning of ARC3 (BH3E.1) and second one will be installed at ARC1 (BH1AE).
We have just started to measure the beam profile. The measured beam sizes are good agreement with the rough calculation. But it is still preliminary and the further check is needed.
SRM@BH3E.1

## Slide 17
BT-OTR monitors : (Mori)
Changing fluorescent screen monitors to OTR monitors in BT e±-lines.
Will measure the bunch-by-bunch beam profiles by using an imaging intensifier (Hamamatsu C14245), which can control gate width with accuracy of a few ns.
The beam profile data can be related to BPM’s position data by using ShotID or event timing.
Locations of OTR monitor at BT line
e-
Linac END
BT End

## Slide 18
Emittance growth: CSR monitor (Terui)
Plan to replace one vac. chamber of BTp 1st arc bending magnet with a branch pipe to monitor CSR. (No space for BTe.)
Gap height of vac. chamber can be changed.
Simulations for infinite parallel plates with various gap height are also on-going by Fujita-san. Smaller gap height is preferable to reduce CSR effect.
BTp: BH1P.9

## Slide 19: Upgrade plans in BT
  BT e- ECS by Linac group
  New BT e- Line for HER

## Slide 20
BT e- ECS
Because the budget of 1.7 oku-yen (1.25M$) for e- ECS fabrication had been already approved, the e- ECS components and the facility cooling water system must be fabricated in three years.
Linac group has just started the study of the effectiveness and feasibility of e- ECS, including beam loss rates.
Because BT tunnel has poor radiation shields (0.4 m of concrete + 1.1 m of soil) for public area, additional radiation shields might be needed to incorporate e- ECS but it will be problems with maintainability.
The Twenty-Fifth KEKB Accelerator Review Committee

## Slide 21
Current HER transport line
New HER transport line
Linac
New BT line for the HER has been proposed, that envisages ease of the CSR/ISR emittance growth.
New line share the tunnel in part with PF-AR transport line.
If we preserve the current BT e- line and can switch the beam pulse-by-pulse, the current line could be used for beam diagnosis.
New BT line for HER (Kikuchi)
①
①
②
②
③
③
④
④

## Slide 22
The tunnel of PF-AR BT has two independent tunnels. They are loosely connected to the utility tunnel via bellows pipes which are embedded in soil. Beam pipes pass through the bellows pipes.
The junction part has to be excavated to construct the new HER BT line.
The utility tunnel houses many cable-ladders inside, and the BT line has to avoid collision with them; the beam pipe should pass in between the cable ladders, adjusting beam height with vertical translation.
New BT line for HER (Kikuchi)
①
②
③
Upstream tunnel
Downstream tunnel
Junction with the utility tunnel
Junction part
SOIL
SOIL
Upstream tunnel
Downstream tunnel
Tunnel structure
Above the MR tunnel, floor level is elevated by 50 cm.
①
②
③

## Slide 23
Beam line
New ARC1
PF-AR BT line
ARC2
New ARC1
PF-AR BT line
New BT line for HER (Kikuchi)
①
①
②
②
ARC1 part is located side by side with the PF-AR line in the present plan .
Beam level of the new line is 0.6 m lower than the PF-AR line.
Transverse free space between the magnets of two lines are 0.5 m at minimum, which will make the maintenance work difficult.
Bend angle is smaller than current ARC1. Since longer bend is preferable for the CSR we plan to reuse the bend in the ARC2, or to fabricate new bend that has smaller width.

## Slide 24
Optics
New ARC1
ARC3
Emittance at Injection
New BT line
Current BT line
Emittance growth due to ISR
Results of tracking simulation are fitted to
, where,
(New BT line)
(Current BT line)
ISR induced emittance growth of the new BT line decreases to 1/3 of that in current BT line
New BT line for HER (Kikuchi)

## Slide 25: Summary
For better injection efficiency, a few countermeasures will be performed.
Some hardware have issues to be solved. The countermeasures are also in progress.
The budget for e- ECS has already approved and the fabrication of ECS components are on-going. The effectiveness and feasibility study of e- ECS should be performed as soon as possible.
New BT e- line for HER has just started to study. No apparent showstopper is found so far.
Need to consider a consistent upgrade plan including e- ECS and New BT e- line for HER.

## Slide 26: backup

## Slide 27
Official Design of HER line in the KEKB era
We have also found some mysterious discrepancy in the design
  In design of SKB, alignment of BT line in the KEKB era was preserved except for septum magnets.
  But we have found discrepancy in the design between SKB and KEKB:
    At the entrance ofSE4 SKB design has relative to KEKB design.
  Considering misalignment of for QI4E, net effect is a translation in for both of BT and HER by
Injection orbit changes and re-alignment of BT e ARC4 (Kikuchi)

## Slide 28
BT-BPM updates: (Mori)

## Slide 29
BT-BPM updates: (Mori)

## Slide 30
BITF_20220603_Iida
DR-RTL: Fast Kicker (Naito and Kodama)
入射効率に関しては、小玉さんより物言い有り

## Slide 31
HER/LER Abort Kicker : Trigger system
Rising time of abort kicker is less than 200 ns but It needs about 1 μs before the fire the thyratron by using Teledyne E2V triggering system.
Will replace the trigger system to new one. (1 μs → 250 ns)