## Slide 1
Injector Upgrade Plan
F. Miyahara (KEK, Acc. Lab.) for Injector Linac Group
The 28th KEKB Accelerator Review Committee

## Slide 2
Contents
The upgrades performed in 2024 and the plans for the future will be reported.
Fast Kicker to correct 2nd bunch orbit
Beam diagnostic Line with pulsed magnets
Beam tuning programs with machine learning
Big data analysis
HER BT Energy Compression System (ECS)
Summary

## Slide 3
Fast Kicker to correct 2nd bunch orbit

## Slide 4
Fast Kicker for Second Bunch
Background:
Solution:
T. Mitsuda, T. Natsui, Y. Enomoto, Y. Okayasu
1st
2nd
1st
2nd
To suppress emittance growth, 1st and 2nd bunch beams must pass through the center of accelerating structures
To achieve the same injection efficiency as the 1st bunch, the beam orbit of the 2nd bunch must be same as 1st bunch
Installation of a steering magnet capable of kicking only the 2nd bunch
Requirements:
Current response faster than the
96 ns bunch spacing
Injection efficiencies and orbit trend of the 1st and 2nd bunches (HER).
However, the orbit of the 1st and 2nd bunches differ right after the electron gun
T. Natsui

## Slide 5
Fast Vertical Kickers in the Linac
Name | Location | Beam
FY_A2_2 | A-sector | e- (HER), e- for e+ production
FY_A4_4 | A-sector | e- (HER), e- for e+ production
FY_R0_02 | J-Arc | e- (HER), e- for e+ production
FY_58_4 | 5-sector | e- (HER), e+ (LER)
FY_61_E # | SY3 | e- (HER)
# Power semiconductor device was broken due to radiation.
 We are looking for a new location with lower radiation levels that is suitable for installation and effective.
List of fast vertical kickers
installed in the
summer of 2024.
Failure due to radiation damage

## Slide 6
Beam test using a Fast Kicker
Beam test at Linac end
The beam position displacement and jitter were measured using the fast kicker
Only the 2nd bunch is kicked
t
1st
2nd
Trig. Delay
1st bunch is also kicked
Kicking only the 2nd bunch is possible
It is also possible to kick both the 1st and 2nd bunches
The beam position jitter remains constant regardless of the kick angle (The current output is stable)#
The y-position and position jitter as a function of the trigger delay of the fast kicker
In last year’s KEKB Review, it was reported that initial tests showed significant jitter, which was found to be caused by trigger timing jitter from the bucket selection. By implementing timing corrections, this jitter was eliminated.
#
1 clock = ~8.75 ns
96 ns
Fast Kicker
BPM

## Slide 7
Use case of the Fast Kicker
1) Orbit correction for the 2nd bunch
2) Beam diagnostics with separated two bunches
Trigger Delay and vertical e- beam (HER) position before the target
Orbit correction for 2nd bunch of e- beam (HER) using FY_A2_2
e- beam profile at BT
e- beam profile at BT
1st and 2nd
1st
2nd
The emittance and energy spread of the first and second bunches can be evaluated.
Fast Kicker ON
Fast Kicker OFF
2nd bunch orbit was aligned with that of 1st bunch using an auto tuning program.
1st
2nd
The beam profiles of the first and second bunches can be measured simultaneously.

## Slide 8
Upgrade plans of fast kickers
The failed Fast Kicker is planned to be relocated to 4-sector end
We aim to install at least two horizontal Fast Kickers and, if possible, a total of tree. (Two will be installed upstream of the target, and the remaining one downstream of the DR)
Only one Fast Kicker is available for positron beam correction (one unit is out of order)
There are no horizontal fast kickers in Linac#
Current Status:
Plans:
RTL
NG
# A stripline-type horizontal fast kicker is installed in the RTL.

## Slide 9
Beam diagnostic line with pulsed magnets

## Slide 10
Beam diagnostic line with pulsed magnets
Y. Okayasu, T. Kamitani, K. Yokoyama
HER
Diagnostic
Line
(Damp line)
Newly installed pulsed magnets
Newly installed DC magnet
(BM_61_H1)
Newly installed collimator
New beam position and profile monitor
New DC magnet
(BM_61_A1)
A beam diagnostic line using a pulsed magnet was developed to periodically (Hz) guide the beam to the dump line for diagnostics even during HER injection.
New pulsed diagnostic line (2024 Summer)

## Slide 11
Screen monitor with two adjustable insertion positions
Newly installed beam diagnostics devices and beam modes
An 8-electrode position monitor with a wide dynamic range.
A screen monitor with two adjustable insertion positions. In the first position, it allows continuous measurement of the diagnostic line beam without interfering with the HER beam.
The beam monitors were replaced with a new ones to cover the entire beam orbit
F. Miyahara, T. Suwada
HER Beam
Transport
60 mm
Dump
(7 GeV)
Dump
(~6.2 GeV)
Accelerating structures in 5-sector are used for giving beam energy chirp
The horizontal range of the beam passing through the new monitor
HER beam passes through left side of the screen
HER
7GeV
Low E
1st pos.
2nd pos.
The insertion position of the screen and the beam position
Home pos.
Bunch length
measurement

## Slide 12
Preparation of beam modes for beam diagnostics  OK
Passing 7 GeV e- beam to the HER BT OK
Passing 7 GeV e- beam to the Diagnostic (Damp) line  OK
Passing 6.2 GeV e- beam to the Diagnostic (Damp) line  OK
Beam test:
Utilization of the beam diagnostic line
Diagnostics of a beam same as HER injection beam
For diagnosing the bunch length, utilizing 5-sector acc. structures to apply an energy chirp  Beam energy at Linac end is ~6.2 GeV
Test experiment using a beam dump
During operations starting from September 2024, there was not enough power and time to perform sufficient beam tests using the diagnostic line.
From the 2025 operations, full-scale use of the beamline will be promoted.
Use of the beamline:

## Slide 13
Beam tuning programs with machine learning

## Slide 14
Development by T. Natsui
f = -(Q(BPM1)+Q(BPM2)+Q(BPM3))/Q(BPM0)
Example: Maximizing beam transmission
The process of the objective function decreasing during an optimization.
Example of an
optimization
General optimization program using Bayesian Optimization
A general optimization program utilizing machine learning has been developed and is being actively used for various beam tuning
Parameters
Alias used in objective
function
Objective Function
Since Kurata-san developed a similar alternative program, two optimization programs are now available for use.

## Slide 15
Utilization of the optimization program
Purpose | Execution time | Execution interval or execution count
Maximization of positron yield at positron capture section exit | A few minute (When slightly deviating from the optimal conditions) | A few times in a day (Automatically execute when the yield decrease)
Maximization of the e+ beam transmission rate from positron capture section exit to SY2 (End of 2-sector) | ~a few days (~160 params. Execute the beamline in multiple parts) | Only once
Maximization of the e+ beam transmission rate from Linac (SY2) to Damping Ring | ~20 min | Several times a day after Linac startup
Align the vertical orbit of the electron 2nd bunch with that of the 1st bunch using fast kicker | A few minute | A few (Because each beam was stable before the gun problem)
Minimization of emittance in the HER BT through beam orbit adjustments in the Linac | ~30 min | A few times a month
Increase the beam transmission rate for both the 1st and 2nd bunches in the Linac | ~20 min | Several times a day after Linac startup
Typical use cases for machine learning programs
Operators may also use it independently.

## Slide 16
Quadrupole
Dipole (steering)
Target
Linac layout from the target to switch yard to Damping Ring
~160 parameters
Manual tuning is
almost impossible
1. Maximization of e+ beam transmission rate up to SY2
The challenges that led to the development of machine learning program
Beam loss
Bunch
Charge
e+ capture section
In simulations, the transmission rate from capture section exit to 2-sector end was nearly 100%, but in the experiment, there was about a 40% loss, which could not be improved through manual adjustments.
e+ capture
section
T. Natsui
The application of machine learning was divided into multiple sections, and the transmission rate was sequentially increased from upstream.
Briefly reported in the last review

## Slide 17
Before
This tuning process (~160 parameters) takes a few days, so we have only done it once so far.
T. Natsui
After
Progression of tuning process
1. e+ beam transmission rate after the optimization

## Slide 18
2. Maximization of e+ beam transmission rate from Linac to DR
Linac End
T. Natsui
The cause of the beam loss is likely the energy spread
Tuning parameters:
Quadrupole and steering magnets at 2-sector end.
RF phases at 1-sector
to 2-sector
4.2 nC was achieved at the Linac end
Charge variation along the beamline after tuinig
(In the J-ARC, LTR and RTL, there are BPMs where charge calibration has not been performed correctly)
The highest record so for

## Slide 19: Auto-tuning for reduction of the emittance using SR monitors
SR1
Electron BT beam line
SR0
M. Kurata
3. Minimization of e- beam emittance at HER BT
(Since there is no SR monitor in the LTR BT, this tuning cannot be performed with the positron beam)
Low-emittance beam is important for injection to main ring with high injection efficiency
Empirically, adjusting the beam orbit to reduce the beam sizes observed by the SR monitors leads to a reduction in emittance

## Slide 20
σx(SR1)
σy(SR1)
Charge
Comparison of emittance at BT before and after tuning
1st bunch | εn,x [µm] | εn,y [µm]
Before ML | 64.9±8.6 | 45.6±11.0
After ML | 29.2±5.1 | 46.9±13.0
M. Kurata
3. Beam size and emittance after the optimization
Tuning parameters:
Steering magnets at J-ARC Exit (PX_R0_61, PY_R0_61, PX_R0_63, PY_R0_63)
Steering magnets before the positron target with hole (PX_13_5, PY_13_5)
By minimizing the beam size at two SR monitors, the emittance was also reduced.
Using synchrotron radiation allows for non-invasive measurement that can be performed at any time

## Slide 21
Plan: Tuning programs with machine learning
The effective tuning program will be worked continuously
A system is needed to monitor whether it is working correctly and ensure it does not interfere with other tuning or feedback programs.
To facilitate the development of tuning or feedback programs, it is essential to find parameters that are effective for beam emittance, stability, or the objective function
In addition to the physical perspective, we will also consider key parameters found through big data analysis (currently under trial) and the opinions of experienced operators.
Share information about any monitors or equipment required for tuning and proceed with their implementation

## Slide 22
Big Data Analysis

## Slide 23
Synchronized data (position, charge) from all BPMs in the Linac and BT are archived.
It has become possible to compare these with various measured values (EPICS PVs) stored in the Archiver Appliance.
Linac BPMs
Linac RF Monitors
Linac pulsed magnets
BT BPMs
Shot by shot data
Linac Data:
Laser (power, position, …),
Thermionic-gun (Heater/Vias voltage, …),
RF phase, Temperature,
…
EPICS PVs (sampling data)
SuperKEKB Data:
Injection efficiency, beam current,
Kicker / Septum, Beam loss,
SR monitor at BT, Tune, Temperature,
…
Synchronized data for these datasets can be output
Tool for finding critical parameters:
Parameters that significantly affect injection
Parameters for maintaining emittance
Factors causing beam instability
Cause of abnormal beam (cause an beam abort)
…
Big data Analysis

## Slide 24
Electron beam position at the entrance of the positron target and HER injection efficiency (100th turn)
Injection efficiency and beam orbit before the target (e- beam passes through the target hole)
Example of Big Data analysis and Future Plans
The emittance improvement achieved through upstream orbit correction using SR monitor-based tuning with machine learning is consistent with the results.
Exploring critical parameters using Explainable AI
Iwasaki-san’s group from Osaka Metropolitan Univ. is conducting analysis using SHAP (Shapley Additive Explanations)
F. Miyahara
Faster data generation
Increasing the number of people performing data analysis
Future plans
Such clear correlations cannot be seen in asynchronous data.

## Slide 25
HER BT
Energy Compression System (ECS)

## Slide 26
Background of HER BT ECS introduction
As the bunch charge increases ( current: 2 nC  4 nC) , emittance growth due to short-range transverse wakefields will become a significant issue.
Bunch compression is effective in suppressing the short-range transverse wakefields.
However, bunch compression increases the energy spread due to longitudinal wakefields.
ECS consists of four 3-meter accelerating structures will be installed in the BT section.
HER BT Energy Compression System (ECS)
ECS
SY3
Linac

## Slide 27
Construction of the ECS is under way
The installation of waveguides is approximately complete
The installation of accelerating structure is in progress

## Slide 28
BPM readout system for ECS
Position resolutions of BT BPMs evaluated using 3-BPM method.
It would be better to use the Linac readout system.
However, the stock of the readout boards for the Linac is insufficient, and since the FPGA used in the board has been discontinued.
It is not possible to produce new boards.
The Linac BPM has 1024 channels of data with a 4 ns time step, making it possible to process data from multiple BPMs on the EPICS IOC.
A beam test was performed to measure two BPMs using a single BPM readout board.
To suppress emittance growth caused by wakefields in the accelerating structures, it is necessary to accurately measure the beam position and adjust it to pass through the center.
7 mm
The BT BPM processes signals from multiple BPMs with a single oscilloscope, resulting in a low number of samples. Additionally, since the ADC is 8-bit, the resolution is not optimal.

## Slide 29
The BPM readout test and Layout for ECS BPMs measurement
The first BPM signal and the second BPM signal, with a 200 ns cable delay inserted, were combined using an RF combiner and input into the BPM board.
BPM1
BPM2
6dB Att
BPM1 with 6 dB Att
~200 ns
BPM2 with 200ns
delay
RF Cobiner
200 ns
A resolution of 15 μm was achieved without performing gain adjustment (4 electrodes: left, right, up, down)
Layout of BPM measurement
The predicted position from the other two BPMs, the measured position, and the difference between them.
Readout System
@Kly. Gallery
BPM1 + BPM2 with 200ns  Board1
BPM3 + BPM4 with 200ns  Board2
Cabling for the four BPMs in the ECS section and the readout system.
ECS
Linac SY3
Raw signals from two BPMs (after passing through the filter).
1st
2nd
Although there is attenuation due to the cables, reducing the value of the board's internal attenuator allows for signals large enough to achieve high-resolution measurements.

## Slide 30
Summary
Fast Kicker to correct 2nd bunch orbit It has been confirmed that the 2nd bunch can be stable controlled. We would like to add it where necessary.
Beam diagnostic Line with pulsed magnets The transport to both the HER BT and the diagnostic line was successful without any issues. Moving forward, we will begin utilizing it.
Beam tuning programs with machine learning (Bayesian optimization) It has been extremely beneficial for improving beam performance. The positron beam achieved the highest transmission rate to date, and the HER beam enabled emittance reduction while conducting non-destructive monitoring.
Big data analysis Synchronized data output from the injector to the ring has been enabled. Detailed analysis and the exploration of key parameters using machine learning will be advanced.
HER BT Energy Compression System (ECS) It is necessary to increase the charge of the electron beam. Construction is progressing smoothly.
Thank you

## Slide 31
Appendix

## Slide 32
Response of Fast Vertical @ 2-sector
FY_A4_4 Delay [clock]
FY_A2_2 Delay [clock]
BPM(SP_B6_4)
FY_A2_2
FY_A4_4
[mm]
[mm]
[mm]
[mm]
In the upstream section, there were a slight tendency for jitter to increase.
Energy spread might also be a contributing factor.

## Slide 33: Large-aperture pulsed quadrupole magnets (1): J-ARC
Y. Seimiya
Y. Okayasu
Background:
Solution:
Seven pulsed quadrupole magnets was installed.
Maximum current: 600 A
600 A, 400 V class pulse drivers also installed.
K. Yokoyama
T. Natsui
The transmission of e- beam for LER through J-ARC should be maximized as much as possible (less beam loss).
The optics of e- beam for HER should be matched after the J-ARC exit.
Large-aperture pulsed quadrupole magnets can separately control beam optics for each beam mode.
Lower beta and lower dispersion optics can reduce beam loss in J-ARC.

## Slide 34
e- for the HER
After installing pulsed quads,
e- beam optics at J-ARC exit can be matched to the design ones (Bmag ~ 1).
Installation of the pulsed quads
Bmag
e- for the LER
Beam transmission of the e- beam for LER in J-ARC is achieved almost 100% (almost no beam loss)
This is the result of automatic beam tuning and optics matching in each beam mode.
2023/Oct/22
T. Natsui
Large-aperture pulsed quadrupole magnets (2): J-ARC
Charge
Emittances
(Beam quality)
T. Natsui

## Slide 35
Replaced four DC quadrupole magnets with pulsed ones
Pulsed quad
DC quads
T. Kamitani
Large-aperture pulsed quadrupole magnets (3): Sec. 1 & 2
T. Natsui
Simulations revealed that replacing four DC quadrupoles (common to all beam modes) with pulsed quadrupoles enables the setup of an optics with smaller beta functions for HER beam, thereby suppressing emittance growth.
m

## Slide 36
Operation Panel Implementation
Select tuning knob. We can use any variable EPICS records and select minimum and maximum value for tuning range.
x
Select monitor EPICS records.
We use arias name for evaluation function.
And define the values to be minimized. This allows for a very flexible specification of the objective function, since any combination of measurements can be defined in the equation.
Can use any function.
= f (x)
Select optimization method.
Operator will select setting file and just push this Start button.
I use GPyOpt.
It is python library for Bayesian optimization.

## Slide 37
Injection efficiency and beam position (2024/6/30）
Correlation starts to appear around SP_A1_M, with a clear correlation observed just before the target.
In reality, it is unclear whether SP_15_T is directly correlated with injection efficiency and the upstream section is only correlated with the position of SP_15_T, or if both the upstream section and the area before the target contribute equally to injection efficiency.

## Slide 38
Correlation between SP_15_T (Target)
and SP_A2_3 (Upstream: A-sector)
Correlation between upstream and pre-target position and incident efficiency for 5 days.
The correlation varies depending on the time of day.
A linear correlation appears between SP_15_T and injection efficiency
Correlation of pre-target and upstream areas, identification of locations that work for injection efficiency

## Slide 39
SP_15_Tでの位置とビームの透過率
（左図：SP_16_5 、右図: SP_58_4)
Beam position (SP_15_T) and injection efficiency
Is the beam being reduced at the target in locations with high injection efficiency?
The position and beam transmission rate at SP_15_T.
Left: Target to capture section exit (SP165)
Right: Target to Linac End (SP584)
The positions with high injection efficiency have not reduced the beam.

## Slide 40: BTe accelerating structure installation
Bunch compression to reduce short range transverse wakefield → Longitudinal wakefield causes large energy spread
Harmful fine structure due to longitudinal wakefield
=> BTe-ECS is effective for lower energy spread and smoothing
Energy jitter reduction
Additional voltage for 6S resonance and multi-bunch(7-bunch for future) operation.
3m(longer) acceelerating structures are transferred from Harima by Ego-san’s effort
M. Yoshida

## Slide 41: BTe-ECS (FY2024) to improve injection efficiency
ECS1 was chosen due to building difficulty of ECS2

## Slide 42: BT-ECS at BT1
Low loss
circular waveguide
4 x 3m accelerating structure
Combine two klystron outputs
M. Yoshida

## Slide 43: Bunch length & Energy spread
ini
AccA1
ChicaneA1
AccAB
Eq1
AccB7
ARCJ
AccC2
Eq2
ChicaneSY2
Acc35
Eq3
ARCBT0
ECS
ARCBT1
ARCBT23
ARCBT4
Energy spread
Bunch length (FWHM)[ps]
1
C
2
3
4
5
J-ARC
20ps
5ps
TW RF-Gun
QTW RF-Gun
10ps
BTe-ECS
M. Yoshida

## Slide 44: High Power Test for Cylindrical Waveguide
M. Yoshida

## Slide 45: Copper Coating Stand
M. Yoshida

## Slide 46
Energy spread reduction by pulse shaping
Gaussian
Square
5nC
10nC
15nC
20nC
20nC
15nC
10nC
5nC
5nC electron
15nC
Primary beam for positron production
t
t
Energy spread of 0.1% is required for SuperKEKB synchrotron injection.
M. Yoshida
When bunch compression is performed to suppress vertical emittance, the energy spread exceeds 0.2%.

## Slide 47
BPM readout system in the Linac
VME based BPM readout system is used in the linac. The BPM board has two band pass filters
with bandwidth of 60 MHz (fc=180 MHz), 16bit-250Msps ADCs and a calibration pulse generators.
Position resolution of the system is smaller than requirement (s<10 mm)
Position resolution of the BPM estimated by 3-BPM method
MVME5500 (CPU): 1
VME-EVR-230RF: 1
RAS board: 1
BPM readout board: 2-8 in a create
The system covers the whole of the linac (A-sector – SY3) and a part of the LTR (SY2) BT.
The oscilloscope system is used in
LTR, RTL, HER/LER BT.
requirement
VME crate: 22, BPM board: 108

## Slide 48
BT BPM raw signals measured by Oscilloscope
Some BPMs have overlapping signals during two-bunch operation.